## Slide 1
Signaling for primary transform and transform skip (JVET-E0037)
Jan 2017
LG Electronics
Hyeongmoon Jang (hyeongmoon.jang@lge.com)

## Slide 2: Summary
  Signal emt_cu_flag only when transform skip is disabled
Experimental results
Crosscheck
  JVET-E0089 (by Orange)
All Intra main10 |  |  | 
 | Y | U | V
Overall | 0.00% | 0.00% | -0.02%
Class F (optional) | -0.21% | -0.06% | -0.18%
Random access main10 |  |  | 
 | Y | U | V
Overall | 0.04% | -0.04% | -0.10%
Class F (optional) | -0.15% | -0.03% | -0.05%

## Slide 3: JEM-4.0
Redundant syntax signaling
Transform Skip | Emt_cu_flag | Emt_tu_idx | Apply EMT
On | Signal | No Signal | No EMT
Off | Signal | Signal | Depend on flag

## Slide 4: Proposed method
Signal emt_cu_flag only when transform skip is disabled
Transform Skip | Emt_cu_flag | Emt_tu_idx | Apply EMT
On | No Signal | No Signal | No EMT
Off | Signal | Signal | Depend on flag

## Slide 5: Experimental results
 | All Intra main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.02% | 0.02% | 100% | 98%
Class A2 | 0.00% | -0.03% | -0.03% | 100% | 98%
Class B | 0.00% | 0.06% | 0.02% | 100% | 97%
Class C | -0.01% | -0.08% | -0.06% | 100% | 94%
Class D | -0.02% | 0.03% | -0.07% | 105% | 93%
Class E | 0.01% | 0.04% | 0.02% | 104% | 94%
Class F (optional) | -0.21% | -0.06% | -0.18% | 100% | 96%
Overall | 0.00% | 0.00% | -0.02% | 101% | 96%
Class F (optional) | -0.21% | -0.06% | -0.18% | 100% | 96%
 | Random access main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.05% | -0.10% | -0.18% | 102% | 101%
Class A2 | 0.13% | 0.05% | -0.18% | 100% | 99%
Class B | 0.05% | -0.05% | -0.16% | 99% | 99%
Class C | -0.04% | -0.06% | -0.17% | 100% | 99%
Class D | 0.03% | -0.01% | 0.21% | 99% | 101%
Class E |  |  |  |  | 
Class F (optional) | -0.15% | -0.03% | -0.05% | 99% | 102%
Overall | 0.04% | -0.04% | -0.10% | 100% | 100%
Class F (optional) | -0.15% | -0.03% | -0.05% | 99% | 102%

## Slide 6: Conclusion
Recommendation
  Signal primary transform on/off flag (emt_cu_flag) only when transform skip is disabled.