## Slide 1
A unified condition for affine merge and affine inter mode
(JVET-E0039)
Jan. 2017
LG Electronics
Jaeho Lee (jhlee.lee@lge.com)

## Slide 2: Introduction
Affine prediction
  Two modes: affine inter mode (AF_INTER) and affine merge mode (AF_MERGE)
  Affine enabling conditions (affine flag signalling conditions) of AF_INTER and AF_MERGE are different (see the below Table).
Proposal
  A unified condition for affine merge mode and affine inter mode is proposed.
  The potential bug (the mismatch between encoder and decoder) is reported and analyzed.
 | AF_MERGE | AF_INTER
Enabling condition (a flag signalling condition) | width * height >= 64 | width > 8 && height > 8
Notes: In Affine prediction, there are two modes, affine inter and affine merge mode.
As shown in the below table, Affine enabling conditions or affine flag signalling conditions of AF_INTER and AF_MERGE are different from each other.
For affine merge mode, CU can be coded as affine predction if the luma pixel numger is more than or equals to 64.
In other hand, for affine inter, the height and width is larger than 8.
In this proposal, we erport two contributions, as follows.
First,

## Slide 3: Proposed Method
Unified enabling condition for affine merge mode and affine inter mode
  3 variations of unified condition are tested.
  In unification method 1, mismatch occurs.
  In unification method 2 & 3, the results are reported.
 | Affine merge mode | Affine inter mode
Unification method 1 | width * height >= 64 | 
Unification method 2 | width > 8 && height > 8 | 
Unification method 3 | width >= 8 && height >= 8 | 
Notes: In this proposal, 3 variations of unified condition are tested as shown in this table.
In unification method 1, condition is based on the number of luma sample.
If the sample number is more 숨 or equals to 64, Affine can be coded.

## Slide 4: Proposed Method
Mismatch Analysis of unification method 1
  The mismatch between encoder and decoder occurs when the 4*N blocks are coded as AF_INTER.
  In affine prediction, two MVDs are signalled for CP0 and CP1.
    CP_MVD0 & CP_MVD1 is stored in the buffer and then signalled.
  In the case of 4*N block,
    In the encoding process, since two CP_MVs are located in one sub-block, CP_MVD0 is stored and then CP_MVD1 is stored at the same buffer.
    CP_MVD1 is signalled one more, instead of CP_MVD0.
    In decoding process, CP_MVD1 is decoded as CP_MVD0

## Slide 5: Experimental results (1/2)

## Slide 6: Experimental results (2/2)

## Slide 7: Conclusion
This contribution proposes a unified flag signaling condition for affine merge and affine inter mode.
The proposed unification method shows negligible BD rate changes for random access, low delay B, and low delay P configurations, respectively.
Also, we report and analyze the potential bug, the mismatch between encode and decoder when 4*N block is coded as affine inter mode.
Although the unification method of considering the CU height and width is proposed and tested, the luma sample number based condition unification is more reasonable, because affine prediction is sub-block motion prediction method.
However, we couldn’t report the results on the sample number based unification method because of mismatch. Therefore, it is recommended that we study further to solve this potential problem.