## Slide 1: JVET-E0055: “EE6: Performance evaluation of adaptive scaling of JVET-D0118 for extended color volume material”
D. Rusanovskyy, A.K. Ramasubramonian, J.Sole, M. Karczewicz

## Slide 2: Performance evaluation of JVET-D0118 for HDR/WCG
Introduction
Technologies review
Experimental setup
  Preprocessing stage
  Anchor
  Procedure for objective quality assessment
Simulation results
  D0118 vs. Anchor
  D0118 vs. D0124
Summary and discussion
Scope of the presentation

## Slide 3: Performance evaluation of JVET-D0118 for HDR/WCG
Performance evaluation of D0118 and D0124 under CTC
  Production and cross-check of test sequences
  Production and cross-check of the anchor
  Production and cross-check tested schemes
Visual quality assessment for D0118 and D0124
Assessing benefits of combined solutions
Scope of the EE6

## Slide 4: Adaptive Quantization and Scaling for HDR/WCG video coding:
JVET HDR anchor:
  Luma-adaptive delta QP derivation
  Delta QP = LUT [Mean (OrigY)]
  deltaQP is signaled to decoder
Summary of the technologies

## Slide 5: Adaptive Quantization and Scaling for HDR/WCG video coding:
JVET-D0124 proposal:
  Target to save on deptaQP signaling by replacing with decoder-side derivation
  Luma-adaptive scaling to replace luma-adaptive delta QP
  Scaling is determined as function of predicted pixels and dequantized DC
  s = LUT [Mean (Prediction)+invQuant(DC)]
  Scaling s is applied to AC only, DC is excluded
JVET-D0118 proposal:
  Target to simplify the derivation process and increase performance with scaling of all coefficients
  Scaling is determined as function of predicted pixels:
  s = LUT [Mean (Prediction)]
  Scaling s is applied to DC and AC coefficients
Summary of the technologies

## Slide 6: Adaptive scaling proposed in JVET-D0118:
Block diagram of the scaling for encoder and decoder:

## Slide 7: Experimental setup:
Pre-processing chain:
  YCbCr BT.709 converted to YCbCr PQ2100:
    Clipping to legal range, mapping to 0.01..100nits, converting to PQ2100
  Linear light EXR/TIFF converted to YCbCr PQ2100
  We are thankful Sharp for their efforts to produce CTC required SW changes and Anchor modifications
Block diagram of the test for performance evaluation of D0118
Anchor Codec
Input YUV PQ2100
Dec. YUV1
SDR YUV BT.709
HDR EXR/TIFF
Conversion BT.709 to PQ2100
Conversion to PQ2100
Tested Codec
Dec. YUV2

## Slide 8: Experimental setup:
YCbCr BT.709 conversion to YCbCr PQ2100:
  HDRTools SW change to enable clipping to 0.01..100nits
  HDRTools SW change to enable normalization with gamma
  Converting YCbCr BT.709 to linear RGB:
    System gamma 2.4
    Source normalization 100
    Output normalization 1.0
  Converting linear RGB to YCbCr PQ2100:
    Source normalization 1.0
    ClosedLoopConversion 5 (JCTVC-W1020)
  Agreed implementation is yet to be resolved
Key elements of pre-processing

## Slide 9: Experimental setup:
Linear light EXR/TIFF converted to YCbCr PQ2100 :
  Complete set of HDR PQ2100 sequences not available at: ftp://jvet@ftp.ient.rwth-aachen.de/testsequences/candidates/hdr/PQversions/
  Converting linear RGB to YCbCr PQ2100 using HDRTools:
    ClosedLoopConversion 5 (JCTVC-W1020)
  Agreed implementation is yet to be resolved
Key elements of pre-processing

## Slide 10: Experimental setup:
JEM4.0 SW branch
Luma adaptive dQP
  LumaLevelToDeltaQPMode : 1
  MaxCuDQPDepth : 0
  isSDR : 0/1
ChromaQP offset
  Subject of native colour container
  BT.709 of P3
  HDR BT.709 and SDR BT.709?
  Agreed implementation is yet to be resolved
Key elements of JVET HDR Anchor

## Slide 11: Objective quality assessment process:
Computed objective metrics:
  In YCbCr: PSNR, wPSNR
  In RGB: tPSNRY, DeltaE, PSNR-L100
  Input YUV data used to produce reference RGB data
Block diagram of the test for performance evaluation of D0118
Codec
Input YUV
Dec. YUV
YCbCr metrics
RGB metrics
YCbCr 420 to RGB
YCbCr 420 to RGB
Input in RGB
Output in RGB

## Slide 12: Simulation results:
Pre-processing stage as specified in this contribution
JVET HDR Anchor configuration files
AI, RA and LDB
Reported QPs: [22,27,32,37]
Reported metrics:
  PSNR, wPSNR
  tPSNRY, deltaE, PSNR L100
Expert viewing on:
  Sony X300
  Samsung S9xxx TVs
  SIM2
Tested configurations:

## Slide 13: Simulation results:
D0118 vs JVET HDR Anchor, All Intra:
wPSNR: gain around 1.9% of dBR reduction for Y
tPSNR: penalty around 1.4% of dBR
deltaE, L100: gain around 0.4% for deltaE and around 1.4% for L100

## Slide 14: Simulation results:
wPSNR: gain around 2.3% of dBR reduction for Y
tPSNR: penalty around 0.2% of dBR
deltaE, L100: gain around 1.4% for deltaE and around 1.9% for L100
D0118 vs JVET HDR Anchor, Random Access:

## Slide 15: Simulation results:
wPSNR: gain around 2.9% of dBR reduction for Y
tPSNR: gain around 0.4% of dBR
deltaE, L100: gain around 1.7% for deltaE and around 2.2% for L100
D0118 vs JVET HDR Anchor, LDB:

## Slide 16: Simulation results:
wPSNR: gain around 1.12% of dBR reduction for Y
tPSNR: gain around 0.5% of dBR
deltaE, L100: penalty around 0.2% for deltaE and gain 1.6% for L100
D0118 vs D0124, All Intra:

## Slide 17: Simulation results:
wPSNR: gain around 1.5% of dBR reduction for Y
tPSNR: gain around 1.15% of dBR
deltaE, L100: gain around 0.04% for deltaE and around 1.9% for L100
D0118 vs D0124, Random Access:

## Slide 18: Simulation results:
wPSNR: gain around 1.2% of dBR reduction for Y
tPSNR: gain around 0.88% of dBR
deltaE, L100: gain around 0.2% for deltaE and around 1.5% for L100
  We are thankful Sharp for their cooperation in cross-check of D0118 results
D0118 vs D0124, LDB:

## Slide 19: Summary:
Show that D0118 provides over the Anchor:
  Gains in wPSNRY: 1.9% for AI, 2.5% for RA and 3% for LDB
  Mixed results in tPSNRY: penalty 1.4% and 0.2% for AI and RA, gain 0.4% for LDB
  Gains for deltaE: 0.36%, 1.43%, 1.65% for AI, RA and LDB respectively
  Gains for L100: 1.4%, 1.9%, 2.2% for AI, RA and LDB
Show that D0118 provides over D0124:
  Gains in wPSNRY: 1.1% for AI, 1.5% for RA and 1.19% for LDB
  Gains in tPSNRY: 0.5%, 1.15% and 0.88% for AI, RA and LDB
  Mixed results for deltaE: penalty 0.23% for AI, gain 0.04% and 0.17% for RA and LDB respectively
  Gains for L100: 1.6%, 1.9%, 1.49% for AI, RA and LDB
Observed gains are higher for RA and LDB than for AI results
Results achieved with current test:

## Slide 20: Proposal and discussion:
Continue study on HDR/WCG coding:
  Define the test content in format directed used by encoder
    To be produced and cross-checked prior to Anchor production (e.g. before T2 stage)
  Define the JEM HDR anchor and reporting template:
    To be produced and cross-checked prior to EE evaluation (e.g. before T3 stage)
    Validate JEM HDR anchor vs. HM HDR anchor 3.2
  Reconfirm distortion evaluation procedure
  Study performance of D0118 algorithm vs JEM Anchor and alternative solutions
  Define viewing conditions, replicable in different labs
  Conduct HDR viewing and confirm stability of the metrics