## Slide 1: EE5: Multiple Direct Modes for chroma intra coding
JVET-E0062
Li Zhang, Wei-Jung Chien, Jianle Chen, Xin Zhao, Marta Karczewicz

## Slide 2: Summary
Multiple Direct Modes
  Was proposed in JVET-D0111
  Construct an intra prediction mode list for chroma coding
  List consists of
    cross-component linear model mode
    multiple intra prediction modes derived from co-located luma coding blocks
    chroma prediction modes from spatial neighboring blocks
  For AI, 0.2%, 1.2% BD rate savings of luma and chroma components respectively, without encoder/decoder running time increase

## Slide 3: Introduction
Chroma mode list in JEM
  one direct mode (DM) from a luma block
    Covering co-located top-left sub-block
  one cross-component linear model (CCLM) mode
  four default chroma modes
    Planar
    Vertical
    Horizontal
    DC
    * Alternative mode (mode 66, to replace the redundant DM mode )
Fig. 1 Separate QTBT structures and blocks used by DM

## Slide 4: Proposed Multiple Direct Modes
Chroma mode list
  CCLM
  DMs from multiple luma coding blocks
    five co-located sub-blocks
      CR, TL, TR, BL, BR
  Modes derived by reusing the luma MPM list construction process with minor changes
    chroma prediction modes from five neighboring blocks
    Planar and DC modes
    derived modes
    default modes
      Vertical, Horizontal, Mode 2, Mode 34, Mode 66, Mode 10, Mode 26
    missing default chroma modes are used to replace the last one or more candidates
Fig. 2 sub-blocks in proposed MDM method

## Slide 5: Experimental Results
CTC
with 6 RD checks (for the first 6 candidates), as in JEM
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.74% | -0.77% | 100% | 101% | 0.00% | -0.25% | -0.62% | 99% | 100%
Class A2 | -0.31% | -2.10% | -1.75% | 101% | 101% | -0.08% | -1.80% | -1.60% | 99% | 100%
Class B | -0.18% | -1.05% | -1.21% | 100% | 102% | -0.04% | -1.50% | -1.23% | 98% | 99%
Class C | -0.20% | -1.03% | -0.99% | 100% | 99% | -0.02% | -1.16% | -1.08% | 100% | 99%
Class D | -0.17% | -0.82% | -0.85% | 100% | 99% | 0.00% | -0.86% | -0.53% | 100% | 100%
Class E | -0.32% | -1.45% | -1.44% | 100% | 100% |  |  |  |  | 
Overall (Ref) | -0.21% | -1.18% | -1.16% | 100% | 100% | -0.03% | -1.13% | -1.02% | 99% | 100%
 | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | 0.05% | -0.05% | -0.44% | 99% | 99% | -0.02% | -0.35% | -0.72% | 96% | 98%
Class C | 0.09% | -0.39% | -0.41% | 99% | 99% | 0.01% | -0.30% | -0.31% | 101% | 99%
Class D | -0.01% | 0.00% | -0.41% | 101% | 100% | -0.01% | 0.14% | -0.50% | 100% | 98%
Class E | -0.18% | -0.25% | 0.24% | 100% | 101% | -0.13% | -0.92% | 0.64% | 101% | 101%
Overall (Ref) | 0.00% | -0.16% | -0.30% | 100% | 100% | -0.03% | -0.32% | -0.31% | 99% | 99%

## Slide 6: Cross-check report
JVET-E0099 (KDDI)