## Slide 1: EE2: Peak Sample Adaptive Offset
JVET-E0066
Marta Karczewicz, Li Zhang, Jianle Chen, Wei-Jung Chien

## Slide 2: Summary
Peak SAO
  Was proposed in JVET-D0133
  Each pixel may be modified by adding an offset
  Offset depends on both category index and pixel difference with its neighbors
  0.2% BD rate savings for RA

## Slide 3: Proposed Peak SAO
Definitions of categories
  Depends on how many neighboring pixels are larger/smaller than current pixel
  For category 2, offset is always set to 0, i.e., pixels are unchanged.
Fig. 1. Neighbouring samples.
Category | Conditions
0 | 
1 | 
2 | None of the above
Category | Conditions
0 | 
1 | 
2 | None of the above
lgr ( x ) = (x > 0) ? 1 : 0 | (1)
sml ( x ) = (x < 0) ? 1 : 0 | (2)

## Slide 4: Proposed Peak SAO
Offset selection
  Average pixel value difference between the current pixel and its selected neighboring pixels (Cm)
  Normalization factor NF
    M=3 or 4 for category 1 and 2, respectively
Signaling of side information
  Slice on/off control flag
  Offsets for each category and class index, NF, as well as maximum number of classes
 | (3)
 | (3)

## Slide 5: Experimental Results
EE2 Test 4
  Anchor: JEM4.0
  Tested: JEM4.0 + Peak SAO
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.06% | -0.02% | 100% | 114% | -0.03% | 0.01% | -0.13% | 100% | 106%
Class A2 | -0.15% | -0.04% | -0.04% | 98% | 111% | -0.21% | 0.05% | -0.06% | 100% | 104%
Class B | -0.09% | -0.01% | -0.03% | 98% | 111% | -0.31% | -0.14% | -0.11% | 99% | 104%
Class C | -0.32% | 0.01% | -0.03% | 100% | 107% | -0.30% | -0.02% | -0.05% | 100% | 101%
Class D | -0.11% | 0.02% | 0.01% | 100% | 102% | -0.20% | 0.15% | 0.14% | 100% | 101%
Class E | -0.20% | 0.02% | 0.01% | 100% | 108% |  |  |  |  | 
Overall (Ref) | -0.15% | -0.01% | -0.02% | 99% | 109% | -0.22% | 0.00% | -0.05% | 100% | 103%
 | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.01% | -0.11% | 0.01% | 99% | 106% | -0.03% | -0.29% | -0.01% | 96% | 111%
Class C | -0.13% | -0.09% | -0.31% | 99% | 103% | -0.15% | -0.06% | -0.20% | 100% | 106%
Class D | -0.12% | -0.22% | -0.03% | 100% | 102% | -0.19% | 0.45% | 0.13% | 99% | 102%
Class E | 0.60% | -0.57% | -1.43% | 100% | 102% | 0.50% | -1.14% | -0.48% | 101% | 108%
Overall (Ref) | 0.05% | -0.22% | -0.35% | 100% | 103% | 0.00% | -0.21% | -0.11% | 99% | 107%

## Slide 6: Experimental Results
EE2 Test 5
  Anchor: JEM4.0
  Tested: JEM4.0 + Peak SAO - SAO
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.10% | 1.01% | 1.85% | 98% | 107% | 0.41% | 1.17% | 0.99% | 97% | 103%
Class A2 | -0.04% | 0.53% | 0.64% | 98% | 107% | 0.03% | 2.00% | 1.66% | 97% | 101%
Class B | -0.03% | 0.25% | 0.57% | 98% | 106% | -0.15% | 0.97% | 1.20% | 97% | 102%
Class C | -0.29% | 0.87% | 1.07% | 97% | 101% | -0.24% | 1.00% | 1.38% | 98% | 100%
Class D | -0.13% | 0.39% | 0.44% | 99% | 101% | -0.26% | 0.80% | 0.71% | 98% | 99%
Class E | -0.10% | 0.03% | 0.07% | 96% | 102% |  |  |  |  | 
Overall (Ref) | -0.08% | 0.52% | 0.79% | 98% | 104% | -0.05% | 1.18% | 1.19% | 97% | 101%
 | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | 0.38% | 3.67% | 4.60% | 98% | 103% | 0.39% | 4.31% | 5.48% | 95% | 107%
Class C | 0.03% | 4.14% | 6.23% | 96% | 102% | 0.01% | 4.92% | 7.24% | 96% | 102%
Class D | -0.13% | 3.18% | 3.50% | 97% | 99% | -0.26% | 3.93% | 3.90% | 96% | 99%
Class E | 0.93% | 3.24% | 2.51% | 94% | 95% | 1.05% | 2.31% | 4.45% | 95% | 100%
Overall (Ref) | 0.27% | 3.58% | 4.34% | 96% | 100% | 0.26% | 3.99% | 5.33% | 95% | 102%