## Slide 1: JVET-E0107 AHG8: Requirements and proposed method for viewport-adaptive quality assessment
Alireza Aminlou, Alireza Zare, Miska M. Hannuksela
Nokia Technologies

## Slide 2: Viewport-dependent Encoding and Streaming
Several 2D representation of the same content
  Each representation has emphasis one specific part of the content
    Corresponding viewport at higher quality
    The remaining part at lower quality
Based on the viewing direction  send corresponding representation
  Note: Viewport-dependent streaming has uniform behavior for different viewing directions

## Slide 3: Tile-based Encoding and Streaming
Each content
  is divided to several tiles (coded independently)
  is coded in different quality levels (stored on server)
Based on the viewing direction
  Tiles covering current viewport are transmitted at higher quality
  Other tiles are transmitted at lower quality.

## Slide 4: Tile-based Encoding and Streaming
Tile based has different behavior for different viewing directions.
Questions: How the test methodology can fairly evaluate tile-based streaming, and compare to viewport-dependent?
4x2 Tiling
6x2 Tiling

## Slide 5: Factors that affect experiences quality
Projection and mapping
Number of viewport representations
Distribution of viewport representations
FOVs of viewport representations
Head motion/rotation model
Representation switching delay
Note:
  Special visual artifacts (e.g., mapping boundary effects or head motion blur) are hard to be captured with the test methodology and can be left to subjective viewing evaluation in order to check that there are no subjectively annoying artefacts.

## Slide 6: Test Methodology Requirements (1/2)
Uniform viewing direction
  In this phase that JVET wants to analyze the performance of different projections and streaming, it is better to assume that the viewer direction is uniform on the sphere
  Non-uniform assumption about viewing direction is application dependent.
Zone-wise analysis (In head motion case)
  Quality of a projection in different parts may not be mixed/accumulated.
  Report performance of main view and side views separately
  As a separate study, one may consider how to combine those performance based on the application.

## Slide 7: Test Methodology Requirements (2/2)
Uniform pixel impact
  All the pixels/area of the sphere should be considered with the same probability on the overall (average) quality.
  In our opinion, this is one fundamental requirements.
    (more details in the next slides)
Capability of handling variations in viewport scenario parameters
  Note: Variations happen a lot in tile-based encoding and streaming
  Different projection formats (basic requirement)
  Different number of viewport representations
  Viewport distribution on the sphere
  Representations with different viewport FOV
  Separation interval of the viewport representations
  Corner cases: non-viewport dependent projection (e.g. ERP)

## Slide 8: Examples of Comparison Cases
Same number of viewport, but different projection
Different number of viewports (e.g. 30 vs. 10 viewports)
Tile-based vs. viewport dependent
Viewport dependent vs. non-viewport dependent

## Slide 9: Proposed Test Method (NZ-SPSNR)
Main idea (considering head motion)
  Evaluate the quality of the projection in different regions of the projections.
Assumptions about head motion:
  Viewer is looking to a specific direction
    where an appropriate viewport representation is received.
  Viewer turns to another direction
    while the corresponding viewport representation has not been received yet.
  Direction of head motion/turn is uniformly distributed.
  Divide sphere to different zones and analyze quality (e.g., three zones)
    Front zone: viewer direction matches well with streamed representation
    Side zone: viewer direction is changed less that 90 degree.
    Back zone: viewer direction is changed more that 90 degree.

## Slide 10: Our Approach
Uniform and continuous viewing directions:
  In JVET-D0079:
    Distortion = average distortion of several predefined viewing directions (e.g. 30x9= 270).
  In JVET-E0070:
    Distortion = average distortion of limited viewing directions aligned with viewport direction (e.g. 30).
  In this contribution:
    Distortion = average distortion of views in (almost) all directions.
Rendering views on sphere
  In JVET-D0079:
    Views = front face of cube map, several (e.g. 9) for each viewport representations
  In JVET-E0070
    Views = window on sphere, one view for each viewport representation
  In this contribution
    Views = window on sphere, several views
    Render sphere once, consider the effect of several views using weight function.

## Slide 11: Pixel Impact in the proposed Methodology
Pixel
Impact
0
90
180
270
360=0
x
x
x
x
x
FOV
Window=FOV + Separation

## Slide 12: Pixel Impact in JVET-E0070
Pixel
Impact
0
90
180
270
360=0
x
x
x
x
x
FOV
Window=FOV + Separation

## Slide 13: Pixel Impact (6 viewport representations)
JVET-E0107
JVET-E0070
Chart: Pixel grid
Chart: Pixel grid

## Slide 14: Pixel Impact (3 viewport representations)
JVET-E0107
JVET-E0070
Chart: Pixel grid
Chart: Pixel grid

## Slide 15: Pixel Impact (2 viewport representations)
JVET-E0107
JVET-E0070
Chart: Pixel grid
Chart: Pixel grid

## Slide 16: Thanks!