## Slide 1
Muhammed Coban, Geert Van der Auwera, Marta Karczewicz (Qualcomm)
AHG8: Adjusted cubemap projection for 360-degree video (JVET-F0025)

## Slide 2: Introduction
Adjusted cubemap projection (ACMP)
  Target uniform sphere sampling with limited texture deformation
  Simple packing (same as CMP packing schemes)
  Perturb cubemap lookup vector
  Leverage existing cubemap hardware lookup for efficient rendering

## Slide 3: Cubemap projection
Non-uniformly samples the sphere resulting in inefficient representation of 360-degree video for coding
Solution: Adjust the mapping such that equal spacing on a cubemap face results in equal spacing on the sphere and vice-versa.

## Slide 4: Adjustment function
Approximate uniform sphere sampling by adjustment functions
Forward (2D to 3D) conversion adjustment function
Inverse (3D to 2D) conversion adjustment function

## Slide 5: ACMP mapping
2D to 3D conversion
  Start with CMP (m,n) position on a cube face to (u’,v’) mapping
  ACMP: modify (u’,v’) to (u,v) using f(x) mapping
  Map (u,v) to (X,Y,Z) mapping using CMP mapping
3D to 2D conversion
  Start with CMP (x,y,z) to (u’,v’) mapping
  ACMP: modify (u’,v’) to (u,v) using g(x) mapping
  Map (u,v) to (m,n) position on a cube face using CMP mapping
)
)

## Slide 6: ACMP vs CMP
Example 3x2 packing
CMP
ACMP

## Slide 7: Results
BD-rates (RA) for ACMP (3x2) comparison with ERP following common test conditions for 360-degree video (JVET-E1030)
Thanks Samsung (JVET-F0092) and Interdigital for cross checking.
Sequence | Face width | Face height
Trolley | 1184 | 1184
GasLamp | 1184 | 1184
Skateboarding_in_lot | 1184 | 1184
Chairlift | 1184 | 1184
KiteFlite | 1184 | 1184
Harbor | 1184 | 1184
PoleVault | 960 | 960
AerialCity | 960 | 960
DrivingInCity | 960 | 960
DrivingInCountry | 960 | 960
Metric |  | Y | U | V
End-to-end | SPSNR-NN | -11.3% | -6.3% | -6.4%
 | SPSNR-I | -11.2% | -6.4% | -6.6%
 | CPP-PSNR | -11.2% | -6.4% | -6.6%
 | WS-PSNR | -11.3% | -6.3% | -6.4%
Cross Format | SPSNR-NN | -34.2% | -3.9% | -4.2%
 | SPSNR-I | -11.0% | -6.2% | -6.4%
 | CPP-PSNR | -10.8% | -6.7% | -7.0%
Dynamic Viewport | Viewport0 | -18.8% | -11.1% | -11.0%
 | Viewport1 | -15.4% | -6.3% | -7.1%

## Slide 8: Conclusion
Adjusted cubemap projecting with 3×2 packing was proposed
Reported coding gain is -11.3% (e2e WS-PSNR) compared with ERP for RA conditions
Request to include ACMP into the next version of 360Lib for further exploration of 360-degree video coding