## Slide 1: AHG8: Equatorial Cylindrical Projection for 360-Degree Video (JVET-F0026)
Geert Van der Auwera, Muhammed Coban, Marta Karczewicz
(Qualcomm)

## Slide 2: Introduction
The equatorial cylindrical projection (ECP) is proposed for efficient compression of 360-degree video:
projecting equatorial region of the sphere using the Lambert cylindrical equal-area projection
  latitude interval of the equatorial region is , which is chosen such that the equatorial region is 2/3 of the total sphere area, hence, one pole area is 1/6 of the sphere area
projecting the poles of the sphere onto square faces in the video frame to avoid inactive pixels

## Slide 3: Coded Frame
ECP coded frame similar to 3x2 CMP
ECP coded frame has 2/3 equatorial samples, 1/3 pole samples
Active samples only
ERP
ECP
‘PoleVault’

## Slide 4: Experimental Results
BD-rates (RA) for ECP comparison with ERP following common test conditions for 360-degree video (JVET-E1030)
Thanks to Samsung, InterDigital for cross-check

## Slide 5: Experimental Results
BD-rates obtained with two horizontal tiles enabled and filtering across tile boundaries disabled.

## Slide 6: Conclusion
Equatorial Cylindrical Projection and 3×2 coded frame was proposed
Reported coding gain is -11.4% (e2e WS-PSNR) compared with ERP for RA conditions
Requested to include ECP into the next version of 360Lib for further exploration of 360-degree video coding

## Slide 7: Backup Slides