## Slide 1: JVET-F0032 EE3: Enhanced FRUC Template Matching Mode
Yongbing Lin, Xu Chen, Jicheng An, Jianhua Zheng

## Slide 2: Summary
Two aspects proposed in JVET-E0035
  1) Bi-directional template matching
  2) Selection between bi-prediction and uni-prediction
EE Test1:
  Combination of the two aspects
  coding gain: 0.36%(RA), 0.14%(LDB)
EE Test2:
  Only the aspect 2)
  coding gain: 0.32%(RA), 0.08%(LDB)

## Slide 3: EE Test1
Set the reference list with smaller initial distortion (according to the starting point MV) as listX (X=0 or 1)
Use current template Tc to find a matched template T0 from listX
Update the current template : T’C = 2*TC – T0
Use the updated template T’C to find another matched template T1 from list(1-X)
Select the bi- or uni-prediction according to the min (costBi, 1.1xcostUni)

## Slide 4: EE Test2
Use current template Tc to find a matched template T0 from list0
Use the current template Tc to find another matched block T1 from list1
Select the bi-, uni-L0-, or uni-L1-prediction according to the min (1.1xcost0, 1.1xcost1, costBi)
Can be performed in parallel

## Slide 5: Results for EE Test1
Table 1. BD rate saving under RA configuration
Table 2. BD rate saving under LDB configuration
Anchor: JEM-5.0.1, CTC
Tested: combination of the two aspects
0.36% BD rate saving for RA
0.14% BD rate saving for LDB
Thanks to Hulu for crosscheck!
 | Over HM-16.6-JEM-5.0.1 (parallel, vs2015) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.45% | -0.39% | -0.35% | 100% | 103%
Class A2 | -0.54% | -0.48% | -0.63% | 99% | 101%
Class B | -0.28% | -0.09% | -0.20% | 99% | 102%
Class C | -0.33% | -0.43% | -0.46% | 98% | 102%
Class D | -0.20% | -0.18% | -0.29% | 99% | 100%
Class E |  |  |  |  | 
Overall (Ref) | -0.36% | -0.30% | -0.38% | 99% | 102%
Class F (optional) | -0.27% | -0.35% | -0.31% | 99% | 103%
 | Over HM-16.6-JEM-5.0.1 (parallel, vs2015) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.13% | -0.15% | -0.65% | 100% | 102%
Class C | -0.10% | -0.32% | -0.36% | 100% | 102%
Class D | -0.07% | -0.04% | -0.80% | 100% | 101%
Class E | -0.30% | -0.46% | 0.10% | 100% | 103%
Overall (Ref) | -0.14% | -0.23% | -0.48% | 100% | 102%
Class F (optional) | -0.18% | -0.16% | -0.07% | 100% | 103%

## Slide 6: Results for EE Test2
Table 3. BD rate saving under RA configuration
Table 4. BD rate saving under LDB configuration
Anchor: JEM-5.0.1, CTC
Tested: aspect 2) only
0.32% BD rate saving for RA
0.08% BD rate saving for LDB
Thanks to Hulu for crosscheck!
 | Over HM-16.6-JEM-5.0.1 (parallel, vs2015) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.41% | -0.28% | -0.37% | 100% | 102%
Class A2 | -0.51% | -0.54% | -0.64% | 99% | 101%
Class B | -0.18% | -0.19% | -0.16% | 99% | 101%
Class C | -0.31% | -0.52% | -0.58% | 99% | 102%
Class D | -0.21% | -0.20% | -0.27% | 99% | 100%
Class E |  |  |  |  | 
Overall (Ref) | -0.32% | -0.34% | -0.39% | 99% | 101%
Class F (optional) | -0.26% | -0.35% | -0.33% | 99% | 103%
 | Over HM-16.6-JEM-5.0.1 (parallel, vs2015) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.10% | -0.06% | 100% | 100%
Class C | -0.03% | -0.12% | -0.26% | 100% | 101%
Class D | -0.08% | -0.31% | -0.32% | 100% | 100%
Class E | -0.24% | 0.64% | -0.39% | 100% | 102%
Overall (Ref) | -0.08% | 0.04% | -0.24% | 100% | 101%
Class F (optional) | -0.29% | -0.23% | -0.29% | 100% | 102%

## Slide 7
Thank You
www.hisilicon.com