## Slide 1: AHG8: adaptive QP for 360 video coding
JVET-F0038
April 2017
F. Racapé, F. Galpin, G. Rath, E. François

## Slide 2: Outlines
    Adaptive QP based on active pixels density
    Experimental results
    Discussion

## Slide 3: Adaptive QP based on active pixels density
  Active pixel density is not stationary on projected frames
  Tested with ERP, QP is vertically adapted following:
    QP= QP0 at the equator
    QPy computed at CTU level. y = middle of current CTU.

## Slide 4: Adaptive QP based on active pixels density
vertically adaptive QP on the sequence AerialCity with base QP0=27

## Slide 5: Experimental results
AQ_ERP vs. ANCHOR_ERP |  |  | S-PSNR-NN |  |  | WS-PSNR |  |  | S-PSNR-I |  |  | CPP-PSNR |  |  | PSNR(Encoder) |  | 
 | FW | FH | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Trolley | 4096 | 2048 | -1.0% | -2.2% | -3.9% | -1.1% | -2.2% | -3.9% | -1.2% | -2.2% | -3.9% | -1.3% | -2.2% | -3.9% | 11.2% | 10.6% | 4.2%
GasLamp | 4096 | 2048 | -1.6% | -1.0% | 2.9% | -1.7% | -1.0% | 2.9% | -1.6% | -1.0% | 2.9% | -1.7% | -1.0% | 2.9% | 11.0% | 13.9% | 24.5%
Skateboarding_in_lot | 4096 | 2048 | -8.6% | -12.7% | -10.5% | -8.5% | -12.7% | -10.5% | -8.3% | -12.7% | -10.4% | -8.3% | -12.7% | -10.4% | 9.8% | -6.0% | 0.9%
Chairlift | 4096 | 2048 | -8.9% | -8.2% | -9.0% | -8.9% | -8.2% | -9.0% | -8.8% | -8.1% | -8.9% | -8.7% | -8.1% | -8.9% | 15.9% | 14.3% | 9.5%
KiteFlite | 4096 | 2048 | -2.8% | -2.8% | -2.2% | -2.9% | -2.9% | -2.3% | -3.0% | -2.8% | -2.2% | -3.1% | -2.9% | -2.3% | 14.5% | 15.0% | 14.8%
Harbor | 4096 | 2048 | -0.8% | -2.3% | -2.2% | -0.9% | -2.3% | -2.2% | -0.8% | -2.3% | -2.1% | -0.9% | -2.3% | -2.1% | 18.7% | 15.4% | 13.6%
PoleVault | 3840 | 1920 | -6.4% | -7.0% | -7.3% | -6.4% | -7.0% | -7.4% | -6.4% | -7.0% | -7.4% | -6.5% | -7.0% | -7.5% | 13.0% | 10.4% | 8.4%
AerialCity | 3840 | 1920 | -4.1% | -4.6% | -4.3% | -4.1% | -4.6% | -4.4% | -4.2% | -4.6% | -4.3% | -4.2% | -4.7% | -4.3% | 11.9% | 12.7% | 12.4%
DrivingInCity | 3840 | 1920 | 0.0% | 3.8% | 3.9% | 0.0% | 3.9% | 3.9% | 0.0% | 3.9% | 4.0% | 0.0% | 3.9% | 4.0% | 6.3% | 18.1% | 19.8%
DrivingInCountry | 3840 | 1920 | -9.0% | -10.8% | -11.5% | -9.0% | -10.9% | -11.6% | -8.9% | -10.9% | -11.5% | -9.0% | -11.0% | -11.6% | 8.6% | 0.3% | 1.9%
Overall |  |  | -4.3% | -4.8% | -4.4% | -4.4% | -4.8% | -4.4% | -4.3% | -4.8% | -4.4% | -4.4% | -4.8% | -4.4% | 12.1% | 10.5% | 11.0%
    HM-16.15
    Random access
    ERP
    CTU-based delta-QP

## Slide 6: Discussion
  Observation:
    Adaptive QP can easily bring consistent gains for several projections including ERP
  Recommendation
    Include adaptive QP in CTC for fair comparison between projections

## Slide 7: Thank you!