## Slide 1: JVET-F0044 AHG5: Performance evaluation of Adaptive Search Range on JEM-5.0.1
Yukinobu Yasugi, Tomohiro Ikai SHARP Corporation

## Slide 2: Introduction
Evaluation of coding performance of ASR on JEM
  Impact of the minimum and maximum range settings
    --MinSearchWindow
    --SearchRange
  ASR on JEM-5.0.1
    Implemented in SVN repository (r459)
    We ported it from HM-16.15 for this evaluation.

## Slide 3: Tested Conditions
Based on CTC
  RandomAccess Main10
  a variety of combinations of --MinSearchWindow and –SearchRange values
 | 32 | 64 | 128 | 256 | 512
64 | C0 | C1 (ASR=0) |  |  | 
128 | C2 | C3 | C4 (ASR=0) |  | 
256 | C5 | C6 (HM-CTC) | C7 | C8 (JEM-CTC) | 
512 | C9 | C10 | C11 | - | -
MinSearchWindow→
Search Range↓

## Slide 4: Summary of results
C7 and C10 seem relatively balanced between BDR and EncTime.  Additional experiment: C14 (96_384)
 | C0 | C1 | C2 | C3 | C4 | C5 | C6 HM CTC | C7 | C8 JEM CTC | C9 | C10 | C11
 | 32_64 | 64_64 | 32_128 | 64_128 | 128_128 | 32_256 | 64_256 | 128_256 | 256_256 | 32_512 | 64_512 | 128_512
Class A1 | 0.64% | 0.30% | 0.17% | 0.05% | -0.04% | 0.00% | -0.05% | -0.06% | 0.00% | -0.03% | -0.06% | -0.03%
Class A2 | 7.11% | 3.70% | 3.91% | 2.85% | 1.43% | 0.55% | 0.49% | 0.31% | 0.00% | -0.26% | -0.26% | -0.26%
Class B | 0.48% | 0.21% | 0.14% | 0.04% | 0.00% | 0.03% | -0.01% | -0.02% | 0.00% | 0.01% | 0.00% | 0.01%
Class C | 0.83% | 0.29% | 0.14% | 0.05% | -0.02% | -0.02% | -0.07% | -0.05% | 0.00% | -0.02% | -0.01% | -0.01%
Class D | 0.09% | -0.02% | -0.10% | -0.08% | -0.08% | -0.05% | -0.04% | -0.03% | 0.00% | 0.02% | 0.02% | 0.00%
Class E |  |  |  |  |  |  |  |  |  |  |  | 
Overall (Ref) | 1.76% | 0.86% | 0.82% | 0.55% | 0.24% | 0.10% | 0.06% | 0.03% | 0.00% | -0.05% | -0.06% | -0.06%
EncTime | 95.3% | 95.5% | 95.2% | 95.1% | 96.1% | 95.8% | 96.2% | 96.7% | 100.0% | 100.6% | 100.4% | 100.6%

## Slide 5: EncTime/BDRate Trade-off
Chart: EncTime [%]
| 95.5 | 96.1 | 100
constant | 0.0086328 | 0.0024494 | 0
adaptive (ASR) | 0.0081972 | 0.0055417 | 0.00096763 | 0.00060551 | 0.00027137 | -0.0005 | -0.00057216 | -0.00056531

## Slide 6: Conclusion
Evaluated coding performance of ASR on JEM-5.0.1
  TrafficFlow and RollerCoaster show significant loss at that SearchRange is less than 256.
  In the results of some cases, ASR provides time reduction with gain in average.
Suggested configuration for the next CTC: minimum search range=96 maximum search range=384
Crosscheck by ITRI