## Slide 1: AHG 8: EAP-based Segmented Sphere Projection with Padding
Ya-Hsuan Lee, Jian-Liang Lin, Shen-Kai Chang, and Chi-Cheng Ju

## Slide 2: Overall Summary
Propose an EAP-based SSP using Equal-Area Projection on the equatorial segment
  Better quality consistency
  Smoother WS-PSNR weighting variance
Apply padding on the north and south poles
  Reduce visual artifacts
Compared to ERP
  11.33%, 11.21%, 11.28% and 11.35% gain in E2E S-PSNR-NN, S-PSNR-I, CPP-PSNR, WS-PSNR, respectively

## Slide 3: Introduction: SSP
Use ERP as the projection format for the equatorial segment
North Pole
South Pole
ERP
0°
θ
-θ
r
8r
2r
ERP

## Slide 4: Visual artifacts in SSP Segment Boundary
Visual artifacts along the latitude of ±45° due to
  Quality Inconsistency in SSP
  Coding error: DCT transform and quantization

## Slide 5: Quality Inconsistency in SSP
WS-PSNR weighting:
  A gap exists at latitude=±45°
Chart: Latitude
| -90 | -89 | -88 | -87 | -86 | -85 | -84 | -83 | -82 | -81 | -80 | -79 | -78 | -77 | -76 | -75 | -74 | -73 | -72 | -71 | -70 | -69 | -68 | -67 | -66 | -65 | -64 | -63 | -62 | -61 | -60 | -59 | -58 | -57 | -56 | -55 | -54 | -53 | -52 | -51 | -50 | -49 | -48 | -47 | -46 | -45 | -44 | -43 | -42 | -41 | -40 | -39 | -38 | -37 | -36 | -35 | -34 | -33 | -32 | -31 | -30 | -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90
sPole | 0.0059947 | 0.0059938 | 0.0059923 | 0.0059902 | 0.0059874 | 0.0059841 | 0.0059801 | 0.0059756 | 0.0059704 | 0.0059646 | 0.0059583 | 0.0059513 | 0.0059437 | 0.0059356 | 0.0059268 | 0.0059174 | 0.0059075 | 0.0058969 | 0.0058858 | 0.005874 | 0.0058617 | 0.0058488 | 0.0058353 | 0.0058213 | 0.0058066 | 0.0057914 | 0.0057756 | 0.0057592 | 0.0057423 | 0.0057248 | 0.0057068 | 0.0056882 | 0.005669 | 0.0056493 | 0.0056291 | 0.0056083 | 0.005587 | 0.0055651 | 0.0055427 | 0.0055198 | 0.0054963 | 0.0054724 | 0.0054479 | 0.0054229
nPole | 0.0054229 | 0.0054479 | 0.0054724 | 0.0054963 | 0.0055198 | 0.0055427 | 0.0055651 | 0.005587 | 0.0056083 | 0.0056291 | 0.0056493 | 0.005669 | 0.0056882 | 0.0057068 | 0.0057248 | 0.0057423 | 0.0057592 | 0.0057756 | 0.0057914 | 0.0058066 | 0.0058213 | 0.0058353 | 0.0058488 | 0.0058617 | 0.005874 | 0.0058858 | 0.0058969 | 0.0059075 | 0.0059174 | 0.0059268 | 0.0059356 | 0.0059437 | 0.0059513 | 0.0059583 | 0.0059646 | 0.0059704 | 0.0059756 | 0.0059801 | 0.0059841 | 0.0059874 | 0.0059902 | 0.0059923 | 0.0059938 | 0.0059947

## Slide 6: EAP-based SSP
Use Equal-Area Projection (EAP) as the projection format for the equatorial segment
North Pole
South Pole
EAP
0°
θ
-θ
r
8r
2r
EAP

## Slide 7: WS-PSNR weighting in EAP-based SSP
Chart: Latitude
| -90 | -89 | -88 | -87 | -86 | -85 | -84 | -83 | -82 | -81 | -80 | -79 | -78 | -77 | -76 | -75 | -74 | -73 | -72 | -71 | -70 | -69 | -68 | -67 | -66 | -65 | -64 | -63 | -62 | -61 | -60 | -59 | -58 | -57 | -56 | -55 | -54 | -53 | -52 | -51 | -50 | -49 | -48 | -47 | -46 | -45 | -44 | -43 | -42 | -41 | -40 | -39 | -38 | -37 | -36 | -35 | -34 | -33 | -32 | -31 | -30 | -29 | -28 | -27 | -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90
sPole | 0.0059877 | 0.0059868 | 0.0059853 | 0.0059832 | 0.0059804 | 0.0059771 | 0.0059731 | 0.0059686 | 0.0059634 | 0.0059577 | 0.0059513 | 0.0059443 | 0.0059368 | 0.0059286 | 0.0059199 | 0.0059105 | 0.0059006 | 0.00589 | 0.0058789 | 0.0058672 | 0.0058549 | 0.005842 | 0.0058285 | 0.0058144 | 0.0057998 | 0.0057846 | 0.0057688 | 0.0057525 | 0.0057356 | 0.0057181 | 0.0057001 | 0.0056815 | 0.0056624 | 0.0056427 | 0.0056225 | 0.0056017 | 0.0055804 | 0.0055586 | 0.0055362 | 0.0055133 | 0.0054899 | 0.005466 | 0.0054415 | 0.0054166 | 0.0053911
nPole | 0.0053911 | 0.0054166 | 0.0054415 | 0.005466 | 0.0054899 | 0.0055133 | 0.0055362 | 0.0055586 | 0.0055804 | 0.0056017 | 0.0056225 | 0.0056427 | 0.0056624 | 0.0056815 | 0.0057001 | 0.0057181 | 0.0057356 | 0.0057525 | 0.0057688 | 0.0057846 | 0.0057998 | 0.0058144 | 0.0058285 | 0.005842 | 0.0058549 | 0.0058672 | 0.0058789 | 0.00589 | 0.0059006 | 0.0059105 | 0.0059199 | 0.0059286 | 0.0059368 | 0.0059443 | 0.0059513 | 0.0059577 | 0.0059634 | 0.0059686 | 0.0059731 | 0.0059771 | 0.0059804 | 0.0059832 | 0.0059853 | 0.0059868 | 0.0059877
Better quality consistency
Smoother WS-PSNR weighting

## Slide 8: Padding
Apply padding on the boundary of the pole
To reduce the effect from the non-active pixels before encoding
The padding region with size maps to the pixel on the boundary of the pole
Blend the padding region with the non-active pixels

## Slide 9: Sample Layout of EAP-based SSP with Padding

## Slide 10: Subjective Quality Comparison
Reconstructed YUV encoded by Qp = 37
Viewport setting: FOV = 80°x80°
Padding size = 32 pixels
  Trade-off between the bit-rate and the quality of the reconstructed viewport frame

## Slide 11: AerialCity (yaw = -90°, pitch = 45°)
Original SSP
Proposed

## Slide 12: DrivingInCity (yaw = -120°, pitch = 45°)
Original SSP
Proposed

## Slide 13: KiteFlite (yaw = 0°, pitch = 45°)
Original SSP
Proposed

## Slide 14: Trolley (yaw = -120°, pitch = 45°)
Original SSP
Proposed

## Slide 15: DrivingInCountry (yaw = 0°, pitch = -45°)
Original SSP
Proposed

## Slide 16: Gaslamp (yaw = 0°, pitch = -45°)
Original SSP
Proposed

## Slide 17: Experimental Results
Count the padding samples as active samples
Reduce the face size for 4K sequences due to the constraint on the amount of the active pixels
 | 4K |  | 8K | 
 | Width | Height | Width | Height
Size in SSP | 1008 | 1008 | 1216 | 1216
Size in EAP-based SSP with padding | 992 | 992 | 1216 | 1216

## Slide 18: Number of Active Pixels including the Padding Samples
 | Original SSP |  |  | ERP |  | Ratio
 | Radius | ERP Width | ERP Height | Width | Height | 
8K | 608 | 1216 | 4864 | 4096 | 2048 | 0.982
4K | 504 | 1008 | 4032 | 3328 | 1664 | 1.022
 | Proposed |  |  | ERP |  | Ratio
 | Radius | ERP Width | ERP Height | Width | Height | 
8K | 640 | 1216 | 4864 | 4096 | 2048 | 1.012
4K | 528 | 992 | 3968 | 3328 | 1664 | <1.027

## Slide 19: Experimental Results
HM-16.15 + 360Lib-2.1
Anchor: ERP format
 | SSP vs. ERP |  |  | Proposed vs. ERP |  | 
Quality Metric | Y | U | V | Y | U | V
S-PSNR-NN (E2E) | -10.24% | -4.06% | -4.61% | -11.33% | -6.53% | -6.96%
S-PSNR-I (E2E) | -10.06% | -4.21% | -4.69% | -11.21% | -6.61% | -7.02%
CPP-PSNR (E2E) | -10.17% | -4.39% | -4.87% | -11.28% | -6.72% | -7.12%
WS-PSNR (E2E) | -10.28% | -4.02% | -4.61% | -11.35% | -6.58% | -7.00%
Thanks to InterDigital for crosscheck (JVET-F0077)

## Slide 20: Conclusions
Propose an EAP-based SSP with padding
  Better quality consistency
  Reduce visual artifacts along the latitude of ±45°
Efficiently reduce the virtual artifacts
Enhanced coding efficiency in BD-rate reduction
  Compared to ERP: 11.33%, 11.21%, 11.28% and 11.35% gain in E2E S-PSNR-NN, S-PSNR-I, CPP-PSNR, WS-PSNR, respectively