## Slide 1: MS-SSIM as an additional metric to PSNR for future video coding
JVET-F0064
M. Pettersson, R. Sjöberg, P. Wennersten, K. Andersson, J. Ström and J. Enhorn

## Slide 2: Background
PSNR has successfully been used during video codec standardization development for many years
However, PSNR does not correlate very well with perceptual quality. Decisions in the standardization process may be suboptimal
A metric which correlates better with perceptual quality is thus desired

## Slide 3: Metric requirements
We believe that a metric to be used for video codec standardization should have the following requirements:
  High correlation with perceptual quality
  Perceptual responsiveness to various types of video coding artifacts
  Ability to capture small quality differences
  Thoroughly tested and accepted by the video community

## Slide 4: MS-SSIM
Calculate luminance, contrast and structure comparison measures for signals x an y:
µx = mean of x
σx = variance of x
σxy = covariance of x and y
L = range of pixel values
K1 = 0.01, K2 = 0.03
Aggregation for SSIM
Aggregation for MS-SSIM

## Slide 5: Correlation to MOS Table from JVET-C0030 from Huawei

## Slide 6: MS-SSIM on small quality differences
BD-rates for PSNR and MS-SSIM for the luma component when comparing JEM 4.0 to JEM 3.1 and JEM 5.0.1 to JEM 4.0
Comment in meeting notes for JVET-C0030:
  “results might be very different depending on whether fundamentally different coding algorithms are compared, and what the quality differences are. If the comparison is just made for a tool-on/tool-off experiment, it might be questionable how much we could conclude from that.”
The differences between JEM versions are small and can be compared to turning a tool on or off. Results indicate that MS-SSIM is as stable as PSNR on capturing small quality differences.

## Slide 7: JEM vs HM CTC
BD-rates for PSNR and MS-SSIM for the luma component comparing JEM 5.0.1 to HM 16.15 for CTC

## Slide 8: JEM vs HM CfE
BD-rates for PSNR and MS-SSIM for the luma component comparing JEM 5.0.1 to HM 16.15 for CfE

## Slide 9: MS-SSIM IN JVET
  MS-SSIM has high correlation with perceptual quality. Subjective results show that MS-SSIM outperforms PSNR
  MS-SSIM emulates the HVS and it is easy to comprehend. It does not include any hidden features prone to overtraining
  Our results comparing different versions of JEM indicate that MS-SSIM can capture small differences in compression efficiency to the same extent as PSNR
  MS-SSIM has been around since 2003 and has been evaluated and used as benchmark numerous times in the video community
  Ericsson is one of the leading providers of video compression solutions. During encoder product development, we find MS-SSIM much more useful than PSNR
  We believe using MS-SSIM during FVC development can help creating a more efficient standard. Reaching a goal of 50% bitrate reduction for the same visual quality should be helped by a metric that is better at measuring visual improvements.
We believe that MS-SSIM is appropriate to use as metric in future video coding development since:

## Slide 10: Proposal
We propose that MS-SSIM should be used as a mandatory additional metric to PSNR
  For the CfE on future video coding
  In the JVET CTC
MS-SSIM code patches for JEM-5.0.1 and HM-16.15, a CTC excel template including MS-SSIM and proposed text changes for the CfE is provided with the contribution