## Slide 1: A simplified method to sao_type_idx coding of Sample Adaptive Offset (SAO)
Xianguo Zhang, Zheng Zhu, Juanting Fan, Xing Jin, Erli Zhang

## Slide 2: Outline
sao_type_idx Coding in JEM
Problems
Proposed Method
Results
Notes: This presentation includes 4 parts, sao_type_idx coding in JEM, existing problems, proposed method and experimental results.

## Slide 3: sao_type_idx Coding In JEM
sao_type_idx_luma and sao_type_idx_chroma
Binarization of SKIP/BO/EO
Context Model for sao_type_idx_luma/chroma
  Only used for the first bin
    1 context model for each initType
sao_type_idx_luma/chroma | Binarizatiom | SAO Type
0 | 0 | SKIP
1 | 10 | BO
2 | 11 | EO

## Slide 4: Problems
EO is utilized more but binarized long
  Test results for JEM and KSC265 both show
    EO is utilized much more than BO, and still more than SKIP
    Especially at larger QP/ faster speed level/ low-efficiency structure like IPPP
    KSC265: https://github.com/ksvc/ks265codec
The context model should be re-designed.
  Context models are utilized to diff SKIP/NON-SKIP
  No context model are utilized to diff EO/BO
  The context model brings complexity, especially for decoder,
  importance of SAO might be waken by ALF and other tools.

## Slide 5: Proposed Method
Binarizing EO at least length
  To improve the coding efficiency
Do not apply any context model
  To reduce the decoding complexity
sao_type_idx_luma/chroma | Binarizatiom | SAO Type
0 | 0 | EO
1 | 10 | BO
2 | 11 | SKIP

## Slide 6: Proposed Method
WD changes
  Syntax change
  Context model
  Others are deleting for context models
if( SaoTypeIdx[ cIdx ][ rx ][ ry ] != 2 ) { | 
for( i = 0; i < 4; i++ ) | 
sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] | ae(v)
if( SaoTypeIdx[ cIdx ][ rx ][ ry ] = = 1 ) { | 
for( i = 0; i < 4; i++ ) | 
if( sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] != 0 ) | 
sao_offset_sign[ cIdx ][ rx ][ ry ][ i ] | ae(v)
sao_band_position[ cIdx ][ rx ][ ry ] | ae(v)
} else { | 
if( cIdx = = 0 ) | 
sao_eo_class_luma | ae(v)
if( cIdx = = 1 ) | 
sao_eo_class_chroma | ae(v)
} | 
} | 
sao_type_idx_luma | bypass | bypass | na | na | na | na
sao_type_idx_chroma | bypass | bypass | na | na | na | na

## Slide 7: Results
AI and RA (crosschecked by Hisilicon’s JVET-H0066)
 | All Intra Main10 |  | 
 | Over 7.0CTC |  | 
 | Y | U | V
Class A1 | 0.00% | -0.05% | -0.01%
Class A2 | 0.00% | -0.04% | -0.04%
Class B | 0.00% | -0.01% | -0.03%
Class C | 0.00% | -0.02% | -0.02%
Class D | 0.00% | -0.02% | -0.01%
Class E | 0.00% | -0.02% | -0.02%
Overall | 0.00% | -0.02% | -0.02%
Class F (optional) | 0.00% | 0.01% | 0.02%
 | Random Access Main 10 |  | 
 | Over 7.0CTC |  | 
 | Y | U | V
Class A1 | #VALUE! | #VALUE! | #VALUE!
Class A2 | #VALUE! | #VALUE! | #VALUE!
Class B | -0.03% | -0.24% | -0.15%
Class C | -0.02% | -0.19% | -0.03%
Class D | 0.00% | -0.14% | -0.04%
Class E |  |  | 
Overall (Ref) | #VALUE! | #VALUE! | #VALUE!
Class F (optional) | 0.02% | -0.06% | -0.01%

## Slide 8: Results
LDP and LDB
  Up to 0.7% for UV
 | Low delay B Main10 |  | 
 | Over 7.0CTC |  | 
 | Y | U | V
Class A1 |  |  | 
Class A2 |  |  | 
Class B | -0.04% | -0.66% | -1.01%
Class C | -0.06% | -0.54% | -0.15%
Class D | 0.00% | -0.49% | -0.93%
Class E | 0.22% | 0.16% | -0.97%
Overall (Ref) | 0.01% | -0.43% | -0.77%
Class F (optional) | #VALUE! | #VALUE! | #VALUE!
 | Low delay P Main10 |  | 
 | Over 7.0CTC |  | 
 | Y | U | V
Class A1 |  |  | 
Class A2 |  |  | 
Class B | -0.07% | -0.61% | -0.72%
Class C | -0.07% | -0.58% | -0.69%
Class D | 0.01% | -0.45% | -0.63%
Class E | 0.12% | -1.06% | -0.66%
Overall (Ref) | -0.02% | -0.65% | -0.68%
Class F (optional) | -0.09% | -0.13% | -0.30%