## Slide 1: AHG5: On worst case memory bandwidth
Tomohiro Ikai*1
Ryoji HASHIMOTO*2
Seiji Mochizuki*2
*1: Sharp Corporation
*2: Renesas Electronics Corporation
JVET 8th Meeting: Macao, CN, 18–25 Oct. 2017

## Slide 2: Motivation
HEVC memory bandwidth model (analytical method)
Cache aware memory bandwidth (software method)
  a software valgrind can detect the number of cache miss
wherein the size of the prediction block is M×N, the length of the interpolation filter is L and the memory access pattern is m×n.
Which kind of relationship exists between analytical method and software method?
=> firstly we check the result of check software method

## Slide 3: Valgrind setting
Practical cache size for smart phone is used in valgrind experiment
 | Valgrind setting | Note: Arm® Cortex®-A73 [3]
1st Level cache | 64 KB | 32 KB or 64 KB
Last level cache | 4 MB | 256KB, 512KB, 1MB, 2MB, 4MB or 8MB

## Slide 4: Example1: Implementation dependency
The valgrind result may show SAO increases external access. i.e. DLmr: last level cache miss
However,
  the cache miss is mainly due to memcpy and offsetBlock (a clipping table)
    not necessarily needed in practical implementation
Valgrind result can be said "very implementation dependent"
Chart: Last level cache miss (DLmr) difference between SAO on and off
| PROGRAM | __memcpy_sse2 _unaligned | filter<8 | filter<4 | xEdgeFilterLuma | offsetBlock | xCalcVarPerPixel
sao on | 40803216 | 7670503 | 4346016 | 3674882 | 3465721 | 2879366 | 2507827
sao off | 30937242 | 773276 | 4362181 | 3710678 | 3472490 | 2444992

## Slide 5: Example2: Tool dependency
If tools off, cache miss in tool specific function disappears (of course).
  but Overall effect may differ
 | JEM7 | SAO off | ALF off | FRUC off | BIO off | ATMVP off
PROGRAM | 40803216 | 30937242 | 35861854 | 36627067 | 40835741 | 40432928
offsetBlock i.e. clipping table | 2879366 | 0 | 2876321 | 2856401 | 2871137 | 2890603
xCalcVarPerPixel | 2507827 | 2444992 | 0 | 2492485 | 2517540 | 2487466
initFRUCMVP | 1839774 | 1843712 | 1840083 | 0 | 1844537 | 1798523
subfilterFrame | 1662024 | 1662024 | 0 | 1662028 | 1679147 | 1627750
xGradFilterY | 1303554 | 1295446 | 1331489 | 1382135 | 0 | 944260
getInterMergeSubPUTmvpCandidate | 1053165 | 1058454 | 1075920 | 824042 | 1049538 | 0
Note1: the above table is abberediated. i.e. remove un-related rows and cols.
Note2: Please do not too much rely on / care about valgrind example data here since there is a lot of implementation dependency and sequence dependency.
Table 2 (Example of last level cache miss, DLmr, BQTerrace ra10 qp 22 49 frames)

## Slide 6: Example3: Sequence dependency
Average, min, and max DLmr value ratio (= Drmr of Tool off / Drmr of JEM70) in CTC sequences
  Valgrind result varies between sequences

## Slide 7: Bottleneck analysis is important
According to the valgrind data, the followings are found.
  Number of memory access itself may not correspond to the worst case memory access
  Implementation dependency and sequence dependency is very large
Thus, instead of just checking the valgrind data,
  1) We need to analyze which kind of memory access can be bottleneck
  2) We need to calculate the worst case memory bandwidth by analysis (e.g. HEVC style memory model)

## Slide 8: Where Bottleneck?
The following may not raise memory bandwidth bottleneck.
  Deblocking filter and SAO (straight forward scan order for memory access)
  Neighbouring access (should be in cache)
  Small constant / table access (should be in cache)
On the other hand, the following memory access may raise memory bandwidth bottleneck.
  Motion compensation using arbitrary motion vector and reference pictures.
  Constant / table data access (if those data is too large to be stored in cache)

## Slide 9: Recommendation
Check memory size of constant / table data which should be always used in CTU level
Calculate HEVC style memory bandwidth for motion compensation related tools
More generic software implementation rather than valgrind is also desirable (see JVET-H0043)

## Slide 10: Additional thought
Subblock based tools (Affine, FRUC, …),
  There should be relatively small variances in motion vector in sub-block level.
  So, block based HEVC style worst memory band calculation may not correspond to the overall worst case
  PU based approach can be suggested

## Slide 11: Backup
 | JEM7 | SAO off | ALF off | FRUC off | BIO off | ATMVP off | AFFINE off | OBMC off
PROGRAM | 40803216 | 30937242 | 35861854 | 36627067 | 40835741 | 40432928 | 40813784 | 40190377
__memcpy_sse2_ unaligned | 7670503 | 773276 | 6998631 | 7683121 | 7649070 | 7725122 | 7686865 | 7708349
filter<8 | 4346016 | 4362181 | 4360713 | 4439345 | 5372887 | 4560362 | 4340272 | 4066269
filter<4 | 3674882 | 3710678 | 3736597 | 3328587 | 3751122 | 3597050 | 3686933 | 3540643
xEdgeFilterLuma | 3465721 | 3472490 | 3534496 | 3430670 | 3473933 | 3528281 | 3476832 | 3440587
offsetBlock | 2879366 |  | 2876321 | 2856401 | 2871137 | 2890603 | 2874484 | 2924455
xCalcVarPerPixel | 2507827 | 2444992 |  | 2492485 | 2517540 | 2487466 | 2492196 | 2464096
initFRUCMVP | 1839774 | 1843712 | 1840083 |  | 1844537 | 1798523 | 1843572 | 1836110
subfilterFrame | 1662024 | 1662024 |  | 1662028 | 1679147 | 1627750 | 1662016 | 1662018
xGradFilterY | 1303554 | 1295446 | 1331489 | 1382135 |  | 944260 | 1295642 | 1254973
xDeblockCU | 1270630 | 1259895 | 1283624 | 1233885 | 1281113 | 1313585 | 1276130 | 1256269
filterCopy | 1265428 | 1265574 | 1333880 | 1601230 | 1322045 | 1576800 | 1248908 | 1183411
getInterMergeSub PUTmvpCandidate | 1053165 | 1058454 | 1075920 | 824042 | 1049538 |  | 1057534 | 1039048
filter<2 | 880399 | 906747 | 915288 |  | 1037370 | 727634 | 904726 | 946282
Please do not too much rely on / care about valgrind example data here since there is a lot of implementation dependency and sequence dependency.
Table 2 (Example of last level cache miss, DLmr, BQTerrace ra10 qp 22 49 frames)