## Slide 1: Further work on top of Tencent’s CfP response (JVET-J0047)
X. Li, X. Xu, X. Zhao, J. Ye, L. Zhao,
S. Liu, M. Xu, G. Li
2018/04

## Slide 2: Introduction
Improvements over Tencent’s CfP response
Normative changes
  Block structure
  Intra block copy
  Merge candidate list construction
Encoder only
  Adaptive chroma QP offset

## Slide 3: Improvement of block structure
A new tree type – SplitToSquare
  A block is split into largest same-size square sub-blocks
  Same as quad-tree for square input blocks
  In this proposal, it is only allowed when the width to height ratio is 1:1, 1:4 and 4:1
Signaling cost reduction
  Split flag is inferred as true if the current block is partially outside picture boundary
  Split direction is inferred as along the picture boundary when the current is partially outside picture boundary either vertically or horizontally

## Slide 4: Intra block copy with further modifications
Unification of IBC and inter
  Same concept as SCM
  IBC is aligned with inter
  BVD resolution: 1-pel integer and 4-pel integer
Skip flag
Merge idx
PredMode
yes
no
End of CU
Residue coding
Intra coding
intra
inter
merge flag
yes
no
Merge idx
IBC flag
yes
no
BVD
BVPIdx
4-Pel Flag
Inter
AMVP

## Slide 5: Improvement of merge candidate list construction
Improved merge candidate list construction
  Additional merge
  candidates extended
  from spatial numbers
  A, B, C, D, E
  Max candidate number
  is reduced from 23 to 10

## Slide 6: Adaptive Chroma QP offset
Increasing chroma QP for better R-D tradeoff for content with rich chroma texture
Slice level chroma QP adjustment (encoder only)
Activation condition: PSNRL+TH<PSNRC in a previously coded picture
Desired chroma QP after scaling: Qpw=(w*qPi+(8-w)*Qpc)>>3
Search for min dQP satisfying f(qPi+dQP)>=Qpw
Signal dQP in slide header
qPi | < 30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | > 43
QpC | = qPi | 29 | 30 | 31 | 32 | 33 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | = qPi − 6
qPi
Qpc
QpW
qPi+dQP

## Slide 7: Simulation Results
-7.67% luma BD-rate reduction over JEM anchor for random access
 | Constraint Set 1 |  |  |  |  |  |  | Constraint Set 1 |  |  |  |  | 
 | Over HM16.16 |  |  |  |  |  |  | Over JEM7.0 |  |  |  |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V) |  | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-PSNR(Y) | BD-PSNR(U) | BD-PSNR(V)
FoodMarket4 | -36.61% | -46.51% | -50.33% | 1.85 | 1.37 | 1.62 |  | -5.13% | -5.31% | -6.73% | 0.20 | 0.11 | 0.15
CatRobot1 | -42.69% | -56.38% | -49.50% | 1.69 | 1.05 | 1.44 |  | -5.74% | -10.02% | -7.87% | 0.15 | 0.10 | 0.15
DaylightRoad2 | -44.07% | -60.70% | -45.60% | 1.25 | 1.35 | 0.87 |  | -6.39% | -10.19% | -8.49% | 0.12 | 0.12 | 0.11
ParkRunning3 | -38.51% | -21.07% | -25.57% | 1.29 | 0.34 | 0.35 |  | -10.77% | 6.17% | 3.13% | 0.31 | -0.08 | -0.04
Campfire | -45.78% | -28.91% | -54.07% | 1.41 | 1.04 | 1.70 |  | -17.74% | 8.15% | -8.62% | 0.39 | -0.25 | 0.18
BQTerrace | -35.89% | -51.94% | -60.06% | 1.10 | 0.99 | 1.18 |  | -8.02% | -13.38% | -13.74% | 0.19 | 0.17 | 0.15
RitualDance | -31.38% | -42.63% | -46.33% | 1.71 | 1.27 | 1.58 |  | -5.71% | -9.92% | -10.21% | 0.27 | 0.21 | 0.25
MarketPlace | -32.73% | -53.08% | -50.50% | 1.17 | 0.97 | 0.95 |  | -5.21% | -11.48% | -10.79% | 0.15 | 0.14 | 0.15
BasketballDrive | -35.51% | -51.43% | -48.79% | 1.30 | 1.18 | 1.52 |  | -6.49% | -11.61% | -9.64% | 0.18 | 0.17 | 0.22
Cactus | -38.45% | -49.61% | -45.98% | 1.61 | 0.82 | 1.24 |  | -5.53% | -8.71% | -9.32% | 0.17 | 0.09 | 0.17
Average SDR-A | -41.53% | -42.72% | -45.01% | 1.50 | 1.03 | 1.20 |  | -9.15% | -2.24% | -5.72% | 0.24 | 0.00 | 0.11
Average SDR-B | -34.79% | -49.74% | -50.33% | 1.38 | 1.04 | 1.29 |  | -6.19% | -11.02% | -10.74% | 0.19 | 0.16 | 0.19
Average all | -38.16% | -46.23% | -47.67% | 1.44 | 1.04 | 1.25 |  | -7.67% | -6.63% | -8.23% | 0.21 | 0.08 | 0.15
Enc Time[%] | 2247% |  |  |  |  |  |  | 282% |  |  |  |  | 
Dec Time[%] | 880% |  |  |  |  |  |  | 115% |  |  |  |  | 
Max Delta Rate[%] | 0.14% |  |  |  |  |  |  |  |  |  |  |  | 
Min Delta Rate[%] | -16.66% |  |  |  |  |  |  |  |  |  |  |  | 
Max Delta PSNR (YUV) | 2.16 |  | 1.64 |  | 1.89 |  |  | 0.23 |  | 0.22 |  | 0.28 | 
Min Delta PNSR (YUV) | 0.74 |  | 0.16 |  | 0.21 |  |  | 0.07 |  | -0.82 |  | -0.18 | 

## Slide 8: Conclusions
Following modules are improved/proposed on top of Tencent’s CfP response
  Block structure
  Intra block copy
  Merge candidate list construction
  Adaptive chroma QP offset (encoder only)
Compared to anchors
  7.67% luma BD-rate saving over JEM for constraint set 1
  38.16% luma BD-rate saving over HM for constraint set 1