## Slide 1: JVET-J0056 Multi-Dimensional Filter Selection for Deblocking
Jie Dong, Yung-Hsuan Chao, Wei-Jung Chien, Li Zhang, Marta Karczewicz
10th JVET Meeting
April 10 – 20, 2018
San Diego, U.S.

## Slide 2: General Idea
15 pre-defined 11-tap filters
  15 filters for BS = 1
  4 filters for BS = 2
Filter selection for a sample: differentiate Blocks P and Q
  Average local activities (levelave : 0 to 6)
  Difference of the local activities of P and Q (leveldiff : 0 to 6)
  Type (0 or 1): the smoother or the more complicated of the two blocks
  Distance to the boundary (0 to 3)
Filtering
Clipping

## Slide 3: Four-Dimensional Filter Selection
Calculate the absolute value of the 2nd derivative for each sample in the dashed boxes
and
and
Local Activity Calculation

## Slide 4: Four-Dimensional Filter Selection
Quantize the average of PA and QA
levelave =
Clip3(0, 6, floor ( log2( (PA + QA) / 2 + 2) ) – 1)
Quantize the difference of PA and QA
leveldiff =
Clip3(0, 6, floor ( log2( |PA - QA| / 2 + 2) ) – 1)
28 possible combinations of (levelave, leveldiff) correspond to 28 categories
Segment Classification Base on Local Activities

## Slide 5: Four-Dimensional Filter Selection
Determine the block types based on the different local activities in P and Q
Determine the sample positions (pos : 0 to 3)
4-D LUT signaled in bitstream: (levelave , leveldiff , Type, pos )

## Slide 6: Pre-Defined Filters
 | Filter Index | Filter Coefficients |  |  |  |  |  |  |  |  |  | 
For BS = 1 and BS = 2 | 0 | 0 | 0 | 0 | 0 | 512 | 0 | 0 | 0 | 0 | 0 | 0
 | 1 | -4 | 13 | -26 | 31 | 481 | 40 | -33 | 18 | -10 | 2 | 0
 | 2 | -21 | -14 | 6 | 264 | 130 | 56 | 138 | -22 | -18 | 7 | -14
 | 3 | -11 | 24 | -185 | 456 | 95 | 106 | 63 | -37 | 1 | 3 | -3
 | 4 | -2 | 12 | -94 | 208 | 293 | 119 | -9 | -17 | 1 | 6 | -5
For BS = 1 Only | 5 | 9 | -46 | -6 | 235 | 108 | 314 | -154 | 105 | -87 | 55 | -21
 | 6 | -12 | 14 | -3 | -17 | 547 | -29 | 18 | -5 | -2 | 4 | -3
 | 7 | -13 | 31 | -69 | 132 | 305 | 225 | -164 | 120 | -80 | 35 | -10
 | 8 | -18 | 46 | -142 | 318 | 149 | 222 | -67 | 8 | -4 | 7 | -7
 | 9 | -64 | 96 | -55 | 188 | 327 | -119 | 106 | 67 | 20 | -50 | -4
 | 10 | -10 | -41 | -16 | 348 | 34 | 157 | 102 | -29 | -52 | 45 | -26
 | 11 | -46 | -40 | 128 | 315 | -66 | 48 | 207 | 49 | -115 | 87 | -55
 | 12 | -32 | 18 | 63 | -39 | 365 | 255 | -208 | 130 | -24 | -28 | 12
 | 13 | -3 | 4 | -7 | 3 | 492 | 58 | -71 | 72 | -54 | 27 | -9
 | 14 | 17 | -57 | 90 | -105 | 631 | -110 | 73 | -29 | -1 | 14 | -11
 | 15 | -40 | 124 | -99 | -25 | 685 | -268 | 185 | -57 | 13 | -33 | 27

## Slide 7: Clipping
Two clipping values are signaled in the picture level
  tC,VER is used in clipping the magnitude change for the vertical boundaries
  p' = p + Clip3 (-tC,VER , tC,VER , Δp)
  tC,HOR is used in clipping the magnitude change for the horizontal boundaries
  p' = p + Clip3 (-tC,HOR , tC,HOR , Δp)

## Slide 8: Experimental Results
Anchor: HM+QTBT (implemented on JEM7.0 with structure only)
Tested: Anchor with the proposed deblocking replacing the JEM deblocking
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.56% | 0.03% | 0.02% | 101% | 124%
Class A2 | -1.38% | 0.04% | 0.03% | 100% | 123%
Class B | -1.32% | 0.04% | 0.04% | 100% | 124%
Class C | -0.88% | 0.09% | 0.10% | 102% | 117%
Class D | -0.83% | 0.16% | 0.16% | 103% | 108%
Class E | -1.64% | 0.15% | 0.15% | 100% | 112%
Overall | -1.25% | 0.08% | 0.08% | 101% | 118%
Random Access Main 10 |  |  |  | 
Y | U | V | EncT | DecT
-1.98% | 0.05% | 0.06% | 99% | 117%
-1.82% | 0.13% | 0.05% | 100% | 115%
-1.51% | 0.11% | 0.03% | 100% | 112%
-0.80% | 0.08% | 0.18% | 100% | 106%
-0.66% | 0.23% | 0.09% | 102% | 103%
-1.77% | 0.21% | 0.17% | 100% | 105%
-1.41% | 0.13% | 0.09% | 100% | 110%

## Slide 9: Conclusion
Propose four-dimension filter selection for deblocking
  Determine the values of four arguments used to find the right filter index in a 4-D LUT
  Filtering
  Clipping
BD-rate reduction
  AI: overall -1.25%, HD and above -1.42%
  RA: overall -1.41%, HD and above -1.77%
Suggest to study this contribution in deblocking CE