## Slide 1: Merge mode modification on top of Tencent’s software in response to CfP
JVET-J0058
J. Ye, X. Li, S. Liu

## Slide 2: Introduction
In JEM or Next software, The inter merge candidate list are constructed by spatial candidates, temporal candidates, ATMVP, STMVP, TMVP, and artificial merge candidates.
Among them the spatial candidates are from left, above, left bottom, above right, and top left reference blocks as illustrated in the figure below:
The maximum number of merge candidates is 7

## Slide 3: Proposed method
Extending the current spatial merge candidates (JEM/NEXT) to an outer region of the reference blocks (-96, -96) to the current block
The maximum number of merge
candidates is set to 10.
The searching step is 16 luma
samples along the corresponding
Direction.
Checking the neighbors that
are closed to the current block first.

## Slide 4: Simulation results (1)
Anchor: Tencent CfP(JCTVC-J0029)
Tested: Proposed method
 | Random Access Over Tencent CfP |  |  |  | 
 | Y | U | V | EncT | DecT
Class UHD | -0.08% | -0.07% | -0.04% | 98% | 107%
Class HD | -0.05% | 0.06% | 0.12% | 97% | 107%
Overall (Ref) | -0.06% | -0.01% | 0.04% | 98% | 107%
 | Low delay B Over Tencent Cfp |  |  |  | 
 | Y | U | V | EncT | DecT
HD | 0.00% | 0.50% | -0.07% | 100% | 99%
Overall (Ref) | 0.00% | 0.50% | -0.07% | 100% | 99%

## Slide 5: Simulation results (2)
Anchor: Disable the proposed method
Tested: proposed method
 | Random Access Over Disable Tool |  |  |  | 
 | Y | U | V | EncT | DecT
Class UHD | -0.91% | -1.04% | -1.22% | 109% | 101%
Class HD | -0.92% | -0.92% | -0.85% | 108% | 100%
Overall (Ref) | -0.92% | -0.98% | -1.03% | 108% | 101%
 | Low Delay B Over Disable Tool |  |  |  | 
 | Y | U | V | EncT | DecT
HD | -0.81% | -0.62% | -0.84% | 100% | 100%
Overall (Ref) | -0.81% | -0.62% | -0.84% | 100% | 100%

## Slide 6: Conclusions
The proposed method shows benefits when adding additional merge candidates that are from an outer region of the reference block.
Suggest to further study in Core Experiment.

## Slide 7: Thank you!

## Slide 9: Back up
The merge mode in Tencent CfP(J0029)
  Max candidate number is increased to 23
  New candidates are
  inserted after TMVP
  Grid (16x16) based scan
  from close to far away
  until (-96,-96)
    From bottom to top
    From right to left
    Above region first, then left
    region, then above left region