## Slide 1: JVET-J0062 Non-Separable Secondary Transform Implementations with Reduced Memory via Hierarchically Structured Matrix-based Transforms
Amir Said, Hilmi Eğilmez, Vadim Seregin, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Introduction
Non-separable transforms
  Significant gains if several transforms are used
  Transform parameters require significant amounts of memory
Two memory reduction techniques employed in JEM-7 (JVET-D0120)
  Used as secondary transforms (NSST), and re-used for several cases
  Computed using HyGT (parallel Givens rotations in hypercube arrangement)
  Memory requirements significantly reduced
  Practically no B-D rate loss
Alternative computation methods
  Full matrices
    Large memory requirements
  “Zeroed-out” matrices
    Substantial loss (not the same as separable AMT)

## Slide 3: This proposal
Computation of 8×8 NSST using arrays of 8×8 matrices
  Similar to separable transform
  Hierarchical arrangement
Fewer transforms
  Reduced from 35×3 to 13×3 transforms with dimension 64
Less memory used for transforms of dimension 64
  Reduced from 685 Kbits to 554 Kbits
Practically no difference in performance (JEM-7.1)
  AI: -0.02%
  RA: 0.01%

## Slide 4: Transform computation
Hierarchical structure
Easy to parallelize
Only block rotations as permutations
Final sorting when output is copied
Memory/multiplications reduced to ~40% of full matrix

## Slide 5: CTC simulation results – JEM-7.1
 | All Intra Main10 |  |  |  | 
 | Over HM-16.6-JEM-7.1 |  |  |  | 
 | Y | U | V | EncT* | DecT*
Class A1 | -0.14% | -0.49% | -0.44% | 105% | 101%
Class A2 | 0.25% | -0.20% | -0.23% | 106% | 101%
Class B | -0.15% | -0.74% | -0.79% | 105% | 100%
Class C | 0.22% | -0.18% | -0.21% | 105% | 102%
Class D | -0.26% | -0.44% | -0.57% | 105% | 101%
Class E | -0.01% | -0.50% | -0.76% | 104% | 102%
Overall | -0.02% | -0.43% | -0.50% | 105% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over HM-16.6-JEM-7.1 |  |  |  | 
 | Y | U | V | EncT* | DecT*
Class A1 | -0.02% | -0.77% | -0.47% | 103% | 101%
Class A2 | 0.16% | 0.08% | -0.04% | 103% | 100%
Class B | -0.08% | -0.94% | -0.64% | 103% | 101%
Class C | 0.06% | -0.20% | -0.24% | 102% | 101%
Class D | -0.06% | 0.01% | -0.27% | 102% | 100%
Class E |  |  |  |  | 
Overall (Ref) | 0.01% | -0.39% | -0.34% | 102% | 101%
*Integer computation, but not optimized on JEM-7.1

## Slide 6: Conclusions
Memory requirements of non-separable transforms need to be limited
Three memory economization solutions that can minimize loss
  Secondary transform on sub-blocks
  Computation based on Givens rotations (HyGT)
  Computation based on other matrix factorizations (this proposal)
Those solutions need to be further studied