## Slide 1: JVET-J0072 SW for technology proposal by Samsung, Huawei, GoPro, and HiSilicon – mobile application scenario (JVET-J0024)
April 15, 2018

## Slide 2: Motivation
SW has been provided
  For better understanding details J0024 tools
  Demonstrating different operation points
Tool no/off results for selected tools from J0024
 | Tool-On test |  |  |  |  | Tool-Off test |  |  |  | 
 | BD-rate |  |  | time |  | BD-rate |  |  | time | 
Tools | Y | U | V | Enc | Dec | Y | U | V | Enc | Dec
AFFINE | -5.8% | -5.0% | -5.0% | 113% | 103% | 2.9% | 3.0% | 2.9% | 110% | 99%
ALF | -3.1% | -4.3% | -4.0% | 126% | 203% | 2.2% | 1.6% | 1.8% | 94% | 78%
AMVR | -5.0% | -6.8% | -7.3% | 182% | 97% | 1.5% | 2.3% | 2.6% | 92% | 100%
DMVR | -6.4% | -5.1% | -5.4% | 113% | 137% | 2.4% | 2.3% | 2.4% | 109% | 91%
BIO | -3.3% | -1.0% | -0.8% | 113% | 150% | 1.8% | 0.7% | 0.7% | 95% | 89%
IPR (~LIC) | -0.7% | -0.5% | -0.4% | 130% | 116% | 0.4% | 0.3% | 0.2% | 92% | 95%
Multiple TR | -1.4% | -0.8% | -0.3% | 113% | 101% | 0.6% | 0.2% | 0.0% | 92% | 99%
Noise Sup Filter | -1.4% | -1.7% | -1.9% | 100% | 164% | 0.8% | 1.2% | 1.5% | 99% | 83%
TD-RSP | -1.1% | -0.9% | -0.8% | 105% | 108% | 0.7% | 0.4% | 0.4% | 95% | 97%
Secondary TR | -2.2% | -0.2% | 0.1% | 108% | 101% | 1.2% | 0.2% | 0.3% | 95% | 100%
UMVE | -7.0% | -6.4% | -7.0% | 165% | 102% | 1.0% | 0.4% | 0.5% | 105% | 99%

## Slide 3: Brief SW overview
Difference from SW in CfP response streams generation
  Same tools set
  Bug-fixes
  Early termination during Encoder search
Main factor affecting decoder speed
  Considering complexity as key factor for tools selection
    No template matching
    No int64
Over HM 16.16 | JVET-J0024 CfP response |  |  | J0072 software |  | 
 | BD-rate(Y) | BD-rate(U) | BD-rate(V) | BD-rate(Y) | BD-rate(U) | BD-rate(V)
Average SDR-A | -41.2% | -35.2% | -37.1% | -40.2% | -35.0% | -37.0%
Average SDR-B | -32.8% | -36.7% | -37.7% | -31.3% | -37.3% | -37.9%
Average all | -37.0% | -36.0% | -37.4% | -35.8% | -36.2% | -37.4%
Enc Time[%] | 902% |  |  | 494% |  | 
Dec Time[%] | 274% |  |  | 292% |  | 

## Slide 4: Different operation points for J0072
Chart: 
| 2.1800000000000002 | 2.1616666666666666 | 1.2566666666666668 | 1.1616666666666666 | 1.1833333333333333 | 0.93166666666666664 | 3.0399999999999996 | 0.61499999999999988 | 0.625 | 0.66 | 0.66833333333333333 | 0.8716666666666667 | 1.6283333333333332 | 1.5933333333333335 | 3.2733333333333334 | 3.1833333333333336 | 3.7866666666666666
 | 0.3441 | 0.34305 | 0.2998 | 0.2931 | 0.29085 | 0.253 | 0.359 | 0.12638 | 0.13025 | 0.17884 | 0.18591 | 0.23741 | 0.32064 | 0.32403 | 0.35861 | 0.35736 | 0.36967
SW from J0072 vs HM16.16 | BD-rate Y | BD-rate Cb | BD-rate Cr | EncTime | DecTime
“minimal set of tools” | -12.5% | -13.5% | -13.7% | 0.8 | 0.6
“×1 HM encoder speed” | -18.6% | -18.6% | -18.8% | 1.0 | 0.6
“×2 HM encoder speed” | -29.2% | -30.1% | -30.5% | 2.0 | 1.0
“J0024 set of tools” | -35.8% | -36.2% | -37.4% | 4.9 | 2.9
Complexity = (EncTim + 5*DecTime)/6
Benefit
=(18*BD-rateY=BD-rateCb+BD-rateCr)/20

## Slide 5: Some details for operation points
Category | Minimal tools set 13%  0.8  0.6 | “×1 HM encoder” 13%  0.8  0.6 | “×2 HM encoder” 29%  2.0  1.0 | “J0024 full set” 36%  4.9  2.9
Block structure | QT & BT & BT no separate tree 88  CU  128128 |  | + separate tree | 
Intra prediction | 65 angular + DC+ Planar; 2-taps filter; 3 MPM + 6 bits No reference filter |  | “LM-Chroma” | + DWDIP & MIP
Inter prediction | 8/4-tap L/Ch DCT-IF Simplified motion Merge and AMVP | +Affine | +AMVR +DMVR +UMVE | + BIO + IPR (~LIC)
Transform | DCT-II, 8b, 4 / 128 | + Secondary TR | +Multiple TR | + SVT
Entropy | 16-bits arithmetic coder, 1 window | 16-bits arithmetic coder, 2 windows |  | 
Coefficient coding | SRCC (in SW can be reverted to run-length coding) One scan order |  |  | + Sign Hiding + RSP
In-Loop | HEVC de-block |  | +SAO | + ALF + Noise Suppress + Long de-block

## Slide 6: Conclusion
Consider complexity as key-factor during tools selection
Straight forward extension of well (long time) known tools are preferred as start point for new standard development
The proponents suggest considering the provided SW as the basis for tools
testing during Test Model selection