## Slide 1: JVET-J0088: Proposed Test Model toolset
Jill Boyce, Sam Wong, Zhipin Deng
Apr 2018, San Diego

## Slide 2: Two proposal options
  Preferred option for Test Model
HEVC + QTBT + TT
JEM tools, with the following changes
    Remove: FRUC, BIO, DMVR, OBMC, LIC
    Simplify: Limit to 64x64 transform
  Alternative, less preferred, solution: Two tiers
Test Model: HEVC + QTBT + TT
Core Experiment Model: All of the JEM tools listed above for the single-tier option

## Slide 3: Alternate option: Two Tier solution discussion
Initial version of reference software will support both Test Model and Core Experiment Model
  Core Experiment Model in a separate branch
Only the Test Model would be described in the test model text description output document
New coding tools demonstrate higher gains when compared with a lower coding efficiency anchor than when compared against a higher coding efficiency anchor, because not all coding gains are additive

## Slide 4: Core Experiment Discussion for Two Tier Alternative
In order to expedite development of the new standard, it is proposed to use a higher coding efficiency anchor for CEs
When each CE is defined, coding tools contained in the Core Experiment Model that are not directly being studied in the CE will be enabled
Coding tools in the Core Experiment Model that are direct related to the tools being studied in the CE will not be included in the anchor for that CE
Presence of a particular variant of a tool in the Core Experiment Model is not intended to be an endorsement when being considered for adoption to the Test Model

## Slide 5: Reference Software
Set of tools proposed for inclusion in the Test Model, and for the alternative solution in the Core Experiment Model, could be supported using reference software derived by modifying either the Qualcomm software in JVET-J0021 or the HHI software in JVET-J0035
For tools present in both the JEM and the reference software, the reference software would match the JEM behavior, except for the minimum necessary changes to add support for TT
  For example, bitstreams generated with this software with the TT tool off would be decodable by the JEM 7.0

## Slide 6: JEM tools removal, simplification
Proposed to not include in the test model several tools that are already included in the JEM: FRUC, BIO, DMVR, OBMC, LIC.
These tools have significant decoder complexity requirements. In several CfP responses, proposals were made to simplify these tools.
Recommend that these tools be studied in Core Experiments before a decision is made whether or not to include them in the test model
Propose to limit transform size to 64x64 because of complexity of large transforms