## Slide 1: JVET-K0042 A Study on the overlap in functionality between SAO and ALF
S. Sethuraman, Nijil K.
Ittiam Systems
10th July 2018

## Slide 2: Motivation
Number of in-loop filtering stages are increasing
  Bilateral filter
  Horizontal edge deblocking
  Vertical edge deblocking
  SAO (CTB-level currently)
  ALF
  NSF
Each stage typically has its own parameter determination stage and then the correction/processing stage
  E.g. Deblocking requires boundary strength determination before filtering
  E.g. SAO pixel classification for EO mode before applying offset
  E.g. ALF requires block classification before filtering
Increasing the number of stages leads to higher internal memory requirements

## Slide 3: SAO
Very low decoder complexity
  Edge offset and band offset modes
  CTB level signaling of offsets and ON/OFF
  Encoder uses the original samples and degraded samples to determine the optimal offsets for a CTB; performs RDO based ON/OFF as well as merge mode vs. explicit offset signaling.
  Recent proposals have extended SAO for additional BDRATE gains with slight increase in computational complexity
    SAO palette (JVET-J0022 – CE2.3.2)
    Additional 3 edge offset categories (JVET-J0018 – CE2.3.1)
    A threshold during the comparison for category determination (JVET-J0024 – CE2.3.4)
VTM contains the base SAO present in HEVC
We have taken these 3 SAO improvements – called as SAO_EXT

## Slide 4: ALF
In BMS, 2x2 level classification is performed based on gradients and activity
Encoder derives optimum Wiener filters for a class using the original and degraded samples; attempts merging of filters in an RDO sense.
A 10x10 diamond-shaped filter is applied
Provides very good BDRATE gains (from a PSNR sense)
  Tool ON gains in VTM and Tool OFF drops in BMS are in the 5% range
While current BMS applies ALF on samples already corrected by SAO, this study aims to see how ALF performs when SAO is disabled
  Fixed filters are disabled for this reason as they may be tuned with post-SAO samples
  If VTM+ALF and VTM-SAO+ALF show the same performance, then SAO can be removed in the presence of ALF
  Since these tools have subjective improvements that may not be captured well by PSNR, we had to subjectively view the clips as well

## Slide 5: SAO – Tool OFF drop in VTM
 | VTM vs VTM-SAO |  | 
 | Y | U | V
Class A1 | 1.10% | 0.97% | 1.13%
Class A2 | 1.86% | 2.60% | 1.65%
Class B | 1.72% | 2.58% | 2.47%
Class C | 0.60% | 1.63% | 2.48%
Class E |  |  | 
Overall | 1.33% | 2.01% | 2.04%
Class D | 0.12% | 0.96% | 0.72%

## Slide 6: BDRATE gains with the 3 SAO extensions
 | VTM vs VTM+SAO_Ext |  | 
 | Y | U | V
Class A1 | -0.88% | -1.81% | -2.01%
Class A2 | -0.85% | -0.70% | -0.95%
Class B | -0.81% | -2.04% | -1.21%
Class C | -0.39% | -0.29% | -0.35%
Class E |  |  | 
Overall | -0.72% | -1.26% | -1.09%
Class D | -0.25% | 0.03% | 0.05%

## Slide 7: Tool ON gains of SAO with extensions over VTM-SAO
 | VTM-SAO vs VTM+SAO_Ext |  | 
 | Y | U | V
Class A1 | -1.95% | -2.78% | -3.14%
Class A2 | -2.65% | -3.22% | -2.56%
Class B | -2.47% | -4.43% | -3.54%
Class C | -0.98% | -1.87% | -2.72%
Class E |  |  | 
Overall | -2.00% | -3.18% | -3.05%
Class D | -0.37% | -0.92% | -0.66%

## Slide 8: Tool OFF drop when SAO is disabled in the presence of ALF
 | VTM+SAO_Ext+ALF vs VTM – SAO + ALF |  | 
 | Y | U | V
Class A1 | 0.55% | 1.35% | 2.92%
Class A2 | 1.27% | 4.05% | 4.01%
Class B | 1.12% | 3.77% | 3.71%
Class C | 0.53% | 2.77% | 3.19%
Class E |  |  | 
Overall | 0.88% | 3.07% | 3.47%
Class D | 0.36% | 1.51% | 1.54%
Luma BDRATE gain of 2% has shrunk to 0.88% in the presence of ALF indicating a good overlap between SAO and ALF
Chroma BDRATE gains are nearly intact as BMS-ALF has a single fixed 5x5 diamond-shaped filter for chroma

## Slide 9: Subjective Viewing – Example-1
VTM + ALF
VTM – SAO + ALF
SAO cleans up some motion trails

## Slide 10: Subjective Viewing – Example-2
VTM + ALF
VTM – SAO + ALF
In the presence of SAO, some trails are not cleaned up; ALF by itself does not have these

## Slide 11: Subjective Viewing – Example-3
VTM + ALF
VTM – SAO + ALF
SAO both cleans up and introduces some artifacts

## Slide 12: Conclusions
Because of the CTB-level adaptation of offsets when compared to picture level computation of class-specific Wiener filters, SAO is still able to provide 0.88% average luma BDRATE gains even when ALF is present
SAO’s chroma BDRATE gains are not having much overlap with ALF as the chroma handling of ALF is not very adaptive
The methods still have some complementary functionalities
The study may have to repeated after further improvements to ALF