## Slide 1: CE3: Simplified PDPC (Test 2.4.1) JVET-K0063
Geert Van der Auwera, Vadim Seregin, Amir Said, Adarsh K. Ramasubramonian Marta Karczewicz
Qualcomm Inc.

## Slide 2: Introduction
Position dependent intra prediction combination (PDPC) combines intra predictionwith position dependent weighting of reference samples.
PDPC is applied to the following intra modes: planar, DC, horizontal/vertical, diagonals (2, 66), and 4 (VTM) or 8 (BMS) adjacent modes (3-10 and 58-65). Applied to luma and chroma blocks.
Additional across (secondary) boundary filters are not needed.
PDPC predicted sample is calculated as follows:
For DC mode, the weights are given by:
For the horizontal mode wTL = wT and for vertical mode wTL = wL; for planar mode wTL = 0
For diagonal modes 2 and 66: 0
For adjacent modes 3-10: 0
For adjacent modes 58-65: 0
The PDPC weights can be calculated with adds and shifts only. The value of P(x,y) can be computed in a single step.

## Slide 3: PDPC Reference Samples
Reference samples for planar, DC, horizontal and vertical modes:
pred(x’,y’)
x = x’
y = x’

## Slide 4: PDPC Reference Samples
Reference samples for diagonal modes 2 and 66
Mode 2
x = x’ + y’ + 1
y = x’ + y’ + 1
Mode 66
x = x’ + y’ + 1
y = x’ + y’ + 1

## Slide 5: PDPC Reference Samples
Adjacent 4 (VTM) or 8 (BMS) angular modes next to modes 2 (3-10) and 66 (58-65):
Reference sample coordinates x and y are computed using the tables that are already used for angular mode intra prediction (inverse angle). No additional tables are required in the implementation of simplified PDPC. Linear interpolation of the reference samples is used if fractional reference sample coordinates are calculated.
Modes (3-10) adjacent to diagonal mode 2
Modes (58-65) adjacent to diagonal mode 66

## Slide 6: Results
Test condition ‘All-Intra’ (JVET CTC)
Test condition ‘Random Access’ (JVET CTC)
 | All Intra Main10 |  |  |  | 
 | Over BMS-VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.76% | -0.31% | 0.05% | 111% | 111%
Class A2 | -0.84% | -0.64% | -0.32% | 111% | 109%
Class B | -1.01% | 0.02% | 0.17% | 110% | 107%
Class C | -0.87% | 0.51% | 0.43% | 106% | 105%
Class E | -1.36% | -0.60% | -0.66% | 109% | 105%
Overall | -0.97% | -0.14% | -0.01% | 109% | 107%
Class D | -0.81% | 0.63% | 1.02% | 105% | 107%
 | Random Access Main 10 |  |  |  | 
 | Over BMS-VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.43% | -0.38% | -0.12% | 101% | 103%
Class A2 | -0.37% | 0.13% | 0.53% | 102% | 102%
Class B | -0.53% | 0.62% | 0.46% | 102% | 101%
Class C | -0.55% | 0.85% | 0.84% | 101% | 99%
Overall | -0.48% | 0.39% | 0.46% | 101% | 101%
Class D | -0.44% | 1.03% | 1.20% | 102% | 100%
 | All Intra Main10 |  |  |  | 
 | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.35% | -1.96% | -1.44% | 103% | 108%
Class A2 | -1.44% | -1.20% | -1.20% | 104% | 106%
Class B | -1.43% | -0.88% | -0.76% | 103% | 102%
Class C | -0.93% | -0.16% | -0.07% | 102% | 106%
Class E | -1.70% | -0.81% | -0.87% | 102% | 104%
Overall | -1.35% | -0.94% | -0.81% | 103% | 105%
Class D | -0.78% | 0.28% | 0.51% | 103% | 106%
 | Random Access Main 10 |  |  |  | 
 | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.73% | -1.22% | -1.12% | 101% | 100%
Class A2 | -0.65% | -0.40% | -0.39% | 102% | 102%
Class B | -0.82% | -0.28% | -0.48% | 102% | 101%
Class C | -0.58% | 0.01% | -0.36% | 102% | 100%
Overall | -0.70% | -0.41% | -0.56% | 102% | 101%
Class D | -0.42% | 0.03% | 0.10% | 103% | 101%

## Slide 7: Results
Test condition ‘Low-delay B’ (JVET CTC)
 | Low delay B Main10 |  |  |  | 
 | Over BMS-VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.31% | -0.41% | -0.43% | 102% | 101%
Class C | -0.23% | 0.04% | 0.02% | 102% | 99%
Class E | -0.14% | 2.14% | 0.60% | 102% | 100%
Overall | -0.24% | 0.38% | -0.02% | 102% | 100%
Class D | -0.23% | 0.52% | 0.29% | 101% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.37% | -0.97% | -0.11% | 102% | 100%
Class C | -0.29% | -0.27% | -0.78% | 101% | 102%
Class E | -0.42% | 0.15% | 0.22% | 101% | 99%
Overall | -0.36% | -0.46% | -0.25% | 101% | 100%
Class D | -0.15% | 0.23% | -0.24% | 101% | 102%

## Slide 8: Conclusion
Simplified PDPC is proposed for following intra modes:
  Planar
  DC
  H/V
  Diagonal modes 2 and 66
  Adjacent diagonal modes (3-10 and 58-65)
PDPC weights are computed using shifts
Additional across (secondary) boundary filters are not needed
Angular intra prediction tables are reused, no additional tables required for PDPC
PDPC can be applied together with prediction in single step
Coding gains:
  AI: 0.97% 109%/107% (BMS-VTM-1.0), 1.35% 103%/105% (BMS-1.0)
  RA: 0.48% 101%/101% (BMS-VTM-1.0), 0.7% 102%/101% (BMS-1.0)
  LB: 0.24% 102%/100% (BMS-VTM-1.0), 0.36% 101%/100% (BMS-1.0)
Requested to integrate simplified PDPC into VTM or BMS source codes