## Slide 1: JVET-K0068 CE2 related: Hadamard Transform Domain Filter
Victor Stepin
Sergey Ikonin
Roman Chernyak
Jianle Chen

## Slide 2
Proposed filter is applied at same place and at similar conditions as JEM bilateral filter.
Additional condition: 4x4 blocks are excluded.
Filtering parameters depend only on QP value.
The filtering is performed in domain of 1D Hadamard transform of size 4.
1D Hadamard Transform Domain Filter

## Slide 3
Scan
Hadamard transform
Filtering
Inverse Hadamard transform
Place to accumulation buffer
B | D | 
C | A | 
A | B | C | D
r(0) | r(1) | r(2) | r(3)
R(0) | R(1) | R(2) | R(3)
F(0) | F(1) | F(2) | F(3)
f(0) | f(1) | f(2) | f(3)
A’ | B’ | C’ | D’
A – current pixel
BCD – neighboring pixels
After completing filtering of all pixels in CU accumulated values are normalized by number of processing groups used for each pixel filtering. The normalization is implemented as add-and-shift method excluding divisions and multiplications.
Hadamard Transform Domain Filtering

## Slide 4
// scan pixels
const int x0 = pIn[p0];
const int x1 = pIn[p1];
const int x2 = pIn[p2];
const int x3 = pIn[p3];
// forward transform
const int y0 = x0 + x2;
const int y1 = x1 + x3;
const int y2 = x0 - x2;
const int y3 = x1 - x3;
const int t0 = y0 + y1;
const int t1 = y0 - y1;
const int t2 = y2 + y3;
const int t3 = y2 - y3;
// filtration
const int z0 = pTbl[t0];
const int z1 = pTbl[t1];
const int z2 = pTbl[t2];
const int z3 = pTbl[t3];
// backward transform
const int iy0 = z0 + z2;
const int iy1 = z1 + z3;
const int iy2 = z0 - z2;
const int iy3 = z1 - z3;
pOut[p1_out] += (iy0 - iy1);
pOut[p0_out] += (iy0 + iy1);
pOut[p2_out] += (iy2 + iy3);
pOut[p3_out] += (iy2 - iy3);
Multiplications are excluded by using lookup table. Only addition and subtraction operations are involved
Source code of filtering:
Multiplication free implementation

## Slide 5: LUT details
, Thr=128
Filtering formula:
Observations:
Filtering coefficient G is always less than 1
At high values of R filtering coefficient G is close to 1
So filtering can be implemented as:
In current implementation Thr is set to 128 that requires ROM storage of 128 int32 entries per QP

## Slide 6
Coding performance
 | All Intra Main10 |  |  |  | 
 | Over BMS-1.0 with VTM config |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.42% | -0.02% | 0.04% | 105% | 115%
Class A2 | -0.42% | -0.15% | 0.14% | 106% | 112%
Class B | -0.35% | 0.06% | -0.10% | 106% | 112%
Class C | -0.32% | -0.08% | -0.23% | 105% | 108%
Class E | -0.14% | -0.29% | -0.44% | 105% | 113%
Overall | -0.33% | -0.08% | -0.13% | 105% | 112%
Class D | -0.29% | -0.04% | -0.03% | 106% | 109%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  | 
 | Over BMS-1.0 with VTM config |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.34% | -0.05% | -0.08% | 106% | 104%
Class A2 | -0.57% | -0.19% | -0.12% | 105% | 103%
Class B | -0.62% | -0.04% | -0.31% | 105% | 104%
Class C | -0.43% | -0.23% | -0.32% | 104% | 106%
Class E |  |  |  |  | 
Overall | -0.50% | -0.12% | -0.23% | 105% | 104%
Class D | -0.34% | -0.18% | -0.38% | 103% | 109%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 7: Conclusion
The 1D Hadamard transform domain in-loop filter is proposed
The design of the filter allows to avoid multiplications and divisions
ROM requirement is 128 of int32 entries per QP
The filter demonstrates 0.50% of luma gain with 105% encoding and 104% decoding times compared to VTM 1.0.
It is proposed to study this filter in Core Experiments