## Slide 1: JVET-K0071
CE7: Transform Coefficient Coding
and Dependent Quantization
(Tests 7.1.2, 7.2.1)

## Slide 2: Overview
Test CE7-1.2.: Transform Coefficient Coding
Modified coding order and binarization (relative to HEVC / VTM)
Modified context modelling (relative to HEVC / VTM)
Test CE7-2.1.: Dependent Scalar Quantization
Two scalar quantizers with different reconstruction levels
Quantizer switch using state machine with four states (using parity of levels)
Coding of transform coefficient levels: Approach of test CE7-1.2. with one addition

## Slide 3: Test 7.1.2: Transform Coefficient Coding
Modifications relative to HEVC / VTM-1
Context modelling for Cr-Cbf: Probability model is selected based on value of Cb-Cbf (see also JVET-K0281)
Coding order of bins in a sub-block: All bins for an absolute value are coded successively (before any bin for next position)
Binarization of absolute values: First five bins are coded in regular mode (sig, gt1, gt2, gt3, gt4)
Context modelling for bins of absolute values: Use absolute values in local neighbourhood
Note: Coding order is suitable for a combination with dependent quantization

## Slide 4: Test 7.1.2: Transform Coefficient Coding
for( scanId … ) {
sig_coeff_flag[ scanId ]
if( sig_coeff_flag[ scanId ] ) {
abs_level_gt1_flag[ scanId ]
if( abs_level_gt1_flag[ scanId ] ) {
abs_level_gt2_flag[ scanId ]
if( abs_level_gt2_flag[ scanId ] ) {
abs_level_gt3_flag[ scanId ]
if( abs_level_gt3_flag[ scanId ] ) {
abs_level_gt4_flag[ scanId ]
if( abs_level_gt4_flag[ scanId ] )
abs_level_remaining[ scanId ] // bypass
}
}
}
}
}
Coding Order and Binarization
No changes above sub-block level
Two passes inside sub-block:
  absolute values
  signs (bypass mode)
Binarization
  sig_coeff_flag
  abs_level_gt1_flag
  abs_level_gt2_flag
  abs_level_gt3_flag
  abs_level_gt4_flag
  abs_level_remaining (bypass)

## Slide 5: Test 7.1.2: Transform Coefficient Coding
Context Modelling
Uses already coded absolute values in local neighbourhood as well as diagonal position diag = x + y
sig_coeff_flag (30 models):
  ctxId = f( diag, sumAbs )
abs_level_gt1/2/3/4_flag (64 models):
  ctxId = f( diag, sumAbs − numSig, last )
Rice parameter for binarization of abs_level_remaining
  GoRice = f( sumAbs − numSig )
sumAbs = sum of absolute values in local neighbourhood (template)
numSig = number of absolute levels not equal to 0 in local neighbourhood

## Slide 6: Test 7.1.2: Transform Coefficient Coding

## Slide 7: Test 7.2.1: Dependent Scalar Quantization
Basic Concept
Two scalar quantizers (Q0, Q1) for all coefficients
Quantizer used: determined by state machine
  4 states (unique mapping to quantizer)
  State transition determined by parity of previous level k
Normative Change in Decoder
Additional mapping (in coding order)
for( state = 0; scanIdx = last; scanIdx >= 0; scanIdx-- ) {
k = transCoeffLevel[ scanIdx ];
qIdx[ scanIdx ] = ( k << 1 ) – ( state > 1 ? sign(k) : 0 );
state = stateTransTable[ state ][ k & 1 ];
}

## Slide 8: Test 7.2.1: Dependent Scalar Quantization
Encoder: Quantization
Determine 4 candidate levels for each transform coefficient
  2 for quantizer Q0
  2 for quantizer Q1
Viterbi Algorithm
  find minimum cost path through 4-state trellis structure
  check two connections for each node
  in implementation:
    special “state state”
    special check for skipped subblocks

## Slide 9: Test 7.2.1: Dependent Scalar Quantization
Coding of Transform Coefficient Levels
Re-use coefficient coding of test 7.1.2
Addition: for sig_coeff_flag and abs_level_gt1_flag, use different contexts sets for Q0 and Q1
  (2×30 + 2×32 + 32) models for sig_coeff_flag, abs_level_gt1_flag, abs_level_gt2/3/4_flag
Simple switch between conventional and dependent quantization
  16-bit value (32040 or 0) representing state transition table
state = 0
for( subblocks ... ) {
for( scanId ... ) {
encode/decode absLevel
state = ( 32040 >> ( ( state << 2 ) + ( ( absLevel & 1 ) << 1 ) ) ) & 3 absLevel & 1 ]
}
}

## Slide 10: Test 7.2.1: Dependent Scalar Quantization

## Slide 11: Gain by Dependent Quantization (on top of coeff. coding)
comparison
to sign data
hiding

## Slide 12: Gain by Dependent Quantization (on top of coeff. coding)
comparison
to sign data
hiding

## Slide 13: Summary
Transform Coefficient Coding (test 7.1.2)
Changes binarization of absolute values and coding order of bins (inside sub-block)
Context modelling using local neighbourhood (5 neighbours)
Average results relative to VTM:
  AI: −1.7%, RA: −1.2%, LB: −0.9% (encoder ~101%, decoder ~100%)
Dependent Scalar Quantization (test 7.2.1)
Switching between two scalar quantizers using state machine (4 states)
Transform coding of test 7.1.2 with different context sets for different quantizers
Average results relative to VTM:
  AI: −5.0%, RA: −3.4%, LB: −2.7% (encoder ~110-115%, decoder ~96-100%)
Version with alternative entropy coding: JVET-K0072