## Slide 1: JVET-K0072
Non-CE7: Alternative Entropy Coding
for Dependent Quantization

## Slide 2: Introduction
JVET-K0071: Dependent Scalar Quantization (CE7-2.1)
Two scalar quantizers with different reconstruction levels
Quantizer switch using state machine with four states (using parity of levels)
Good coding gains (AI: −5.0%, RA: −3.4%, LB: −2.7%)
Issues for high-throughput hardware decoder implementations
  EP bins mixed with regular coded bins (inside sub-block)
  bin-to-bin dependencies; number of regular coded bins
Goal of this proposal
Reduce issues for high-throughput hardware implementations
Keep coding gains

## Slide 3: Overview
Dependent Scalar Quantization
  Same approach as in JVET-K0071 (no changes)
Entropy Coding: Changes relative to JVET-K0071
Coding of absolute values using three passes (for each sub-block)
Separation of regular coded bins and EP bins
Dedicated parity_flag in first pas
Reduction of bin-to-bin dependencies

## Slide 4: Binarization and Coding Order of Bins (in sub-block)
JVET-K0071 (test 7.2.1):
for( k … ) { // single pass over all coeffs
sig_flag[ k ]
if( sig_flag[ k ] ) {
gt1_flag[ k ]
if( gt1_flag[ k ] ) {
gt2_flag[ k ]
if( gt2_flag[ k ] ) {
gt3_flag[ k ]
if( gt3_flag[ k ] ) {
gt4_flag[ k ]
if( gt4_flag[ k ] )
remainder[ k ]
}
}
}
}
}
New Version (this proposal):
for( k … ) { // first pass
sig_flag[ k ] // ctx depends on prev. par_flag’s
if( sig_flag[ k ] ) {
par_flag[ k ]
gt1_flag[ k ] // ctx does NOT depend on par_flag
}
}
for( k … ) { // second pass
if( gt1_flag[ k ] )
gt2_flag[ k ] // ctx does NOT depend on other gt2_flag’s
}
for( k … ) { // third pass (EP bins)
if( gt2_flag[ k ] )
remainder[ k ]
}

## Slide 5: Context Modelling
significance flag (54 + 36 models):
  ctxIdSig = f( diag, sumAbs1, state )
parity flag (21 + 11 models):
  ctxIdPar = f( diag, sumAbs1 − numSig, last )
greater1 flag (21 + 11 models):
  ctxIdGt1 = ctxIdPar
greater2 flag (21 + 11 models):
  ctxIdGt2 = ctxIdPar
Rice parameter for binarization remainder
  GoRice = f( sumAbs − numSig )
diag = x + y
sumAbs = sum of absolute values in local neighbourhood (template)
sumAbs1 = sum of partially reconstructed absolute levels after first pass
numSig = number of transform coefficients with sig_coeff_flag == 1

## Slide 6: Switch between Conventional and Dependent Quantization
Same Approach for Coding of Transform Coefficient Levels
Conventional quantization: Special case where state is always equal to 0
Switch between conventional and dependent quantization
  16-bit value (32040 or 0) representing state transition table
Current implementation: Parameter in SPS
  Alternatives: PPS or slice header switch
state = 0
for( subblocks ... ) {
for( scanId ... ) {
encode/decode absLevel
state = ( 32040 >> ( ( state << 2 ) + ( ( absLevel & 1 ) << 1 ) ) ) & 3 absLevel & 1 ]
}
}

## Slide 7: Coding Efficiency: Coefficient Coding Only (VTM Config.)

## Slide 8: Coding Efficiency: Coefficient Coding Only (BMS Config.)

## Slide 9: Coding Efficiency: Dependent Quantization (VTM Config.)

## Slide 10: Coding Efficiency: Dependent Quantization (BMS Config.)

## Slide 11: Summary
Alternative Entropy Coding for Dependent Quantization
Multiple passes over scan positions of a sub-block
Dedicated parity flag transmitted in first pass
Reduction of bin-to-bin dependencies
Separation of regular-coded bins and EP bins
Better suitable for hardware implementations
Average results relative to VTM:
  AI: −4.8%, RA: −3.2%, LB: −2.6% (encoder ~113-119%, decoder ~100%)
Loss relative to JVET-K0071: 0.1-0.2%