## Slide 1: JVET-K0072
Non-CE7: Alternative Entropy Coding
for Dependent Quantization

## Slide 2: Introduction
JVET-K0071: Dependent Scalar Quantization (CE7-2.1)
Two scalar quantizers with different reconstruction levels
Quantizer switch using state machine with four states (using parity of levels)
Good coding gains (AI: −5.0%, RA: −3.4%, LB: −2.7%)
Issues for high-throughput hardware decoder implementations
  EP bins mixed with regular coded bins (inside sub-block)
  bin-to-bin dependencies; number of regular coded bins
Goal of this proposal
Reduce issues for high-throughput hardware implementations
Keep coding gains

## Slide 3: Overview
Dependent Scalar Quantization
  Same approach as in JVET-K0071 (no changes)
Entropy Coding: Changes relative to JVET-K0071
Coding of absolute values using three passes (for each sub-block)
Separation of regular coded bins and EP bins
Dedicated parity_flag in first pas
Reduction of bin-to-bin dependencies

## Slide 4: Dependent Scalar Quantization
Basic Concept
Two scalar quantizers (Q0, Q1) for all coefficients
Quantizer used: determined by state machine
  4 states (unique mapping to quantizer)
  State transition determined by parity of previous level k
Normative Change in Decoder
Additional mapping (in coding order)
for( state = 0; scanIdx = last; scanIdx >= 0; scanIdx-- ) {
k = transCoeffLevel[ scanIdx ];
qIdx[ scanIdx ] = ( k << 1 ) – ( state > 1 ? sign(k) : 0 );
state = stateTransTable[ state ][ k & 1 ];
}

## Slide 5: Dependent Scalar Quantization
Encoder: Quantization
Determine 4 candidate levels for each transform coefficient
  2 for quantizer Q0
  2 for quantizer Q1
Viterbi Algorithm
  find minimum cost path through 4-state trellis structure
  check two connections for each node
  in implementation:
    special “state state”
    special check for skipped subblocks

## Slide 6: Binarization and Coding Order of Bins (in sub-block)
JVET-K0071 (test 7.2.1):
for( k … ) { // single pass over all coeffs
sig_flag[ k ]
if( sig_flag[ k ] ) {
gt1_flag[ k ]
if( gt1_flag[ k ] ) {
gt2_flag[ k ]
if( gt2_flag[ k ] ) {
gt3_flag[ k ]
if( gt3_flag[ k ] ) {
gt4_flag[ k ]
if( gt4_flag[ k ] )
remainder[ k ]
}
}
}
}
}
New Version (this proposal):
for( k … ) { // first pass
sig_flag[ k ] // ctx depends on prev. par_flag’s
if( sig_flag[ k ] ) {
par_flag[ k ]
gt1_flag[ k ] // ctx does NOT depend on par_flag
}
}
for( k … ) { // second pass
if( gt1_flag[ k ] )
gt2_flag[ k ] // ctx does NOT depend on other gt2_flag’s
}
for( k … ) { // third pass (EP bins)
if( gt2_flag[ k ] )
remainder[ k ]
}

## Slide 7: Context Modelling
significance flag (90 = 54 + 36 models):
  ctxIdSig = f( diag, sumAbs1, state )
parity flag (32 = 21 + 11 models):
  ctxIdPar = f( diag, sumAbs1 − numSig, last )
greater1 flag (32 = 21 + 11 models):
  ctxIdGt1 = ctxIdPar
greater2 flag (32 = 21 + 11 models):
  ctxIdGt2 = ctxIdPar
Rice parameter for binarization remainder
  GoRice = f( sumAbs − numSig )
diag = x + y
sumAbs = sum of absolute values in local neighbourhood (template)
sumAbs1 = sum of partially reconstructed absolute levels after first pass
numSig = number of transform coefficients with sig_coeff_flag == 1

## Slide 8: Switch between Conventional and Dependent Quantization
Same Approach for Coding of Transform Coefficient Levels
Conventional quantization: Special case where state is always equal to 0
Switch between conventional and dependent quantization
  16-bit value (32040 or 0) representing state transition table
Current implementation: Parameter in SPS
  Alternatives: PPS or slice header switch
state = 0
for( subblocks ... ) {
for( scanId ... ) {
encode/decode absLevel
state = ( 32040 >> ( ( state << 2 ) + ( ( absLevel & 1 ) << 1 ) ) ) & 3 absLevel & 1 ]
}
}

## Slide 9: Coding Efficiency: Coefficient Coding Only (VTM Config.)

## Slide 10: Coding Efficiency: Coefficient Coding Only (BMS Config.)

## Slide 11: Coding Efficiency: Dependent Quantization (VTM Config.)

## Slide 12: Coding Efficiency: Dependent Quantization (BMS Config.)

## Slide 13: Summary
Alternative Entropy Coding for Dependent Quantization
Multiple passes over scan positions of a sub-block
Dedicated parity flag transmitted in first pass
Reduction of bin-to-bin dependencies
Separation of regular-coded bins and EP bins
Better suitable for hardware implementations
Average results relative to VTM:
  AI: −4.8%, RA: −3.2%, LB: −2.6% (encoder ~113-119%, decoder ~100%)
Loss relative to JVET-K0071: 0.1-0.2%