## Slide 1: Temporal motion data storage reduction (JVET-K0086)
Hyeongmun Jang (hm.jang@lge.com)

## Slide 2: Summary
Propose temporal motion data storage reduction method
  Compress temporal motion data based on spatial candidates
Simulate suggest modification.
  Proposed storage reduction method in unit of 16x16 block
  Proposed storage reduction method in unit of 32x32 block
  Proposed storage reduction method in unit of 64x64 block
Experimental results
Crosscheck : Qualcomm(JVET-K0530) and Tencent
Random access main10 | over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
16x16 | -0.09% | -0.09% | -0.08% | 100% | 105% | 0.28% | 0.25% | 0.20% | 101% | 102%
32x32 | 0.11% | 0.08% | 0.13% | 101% | 105% | 0.59% | 0.48% | 0.51% | 101% | 101%
64X64 | 0.56% | 0.45% | 0.53% | 102% | 105% | 0.98% | 0.86% | 0.90% | 102% | 100%

## Slide 3: Introduction
Temporal motion data
  In HEVC : 74bit for 16x16 unit
  In VTM : 74bit for 16x16 unit
  In BMS : 74bit for 4x4 unit due to ATMVP
    For 16 reference picture = about 73MByte = (3840*2160*74/16)*16
Temporal motion data storage reduction method
  In HEVC standard
    Temporal motion data storage reduction is adopted.
    Reduction as a factor of 16 resolution .
    0.4% and 0.6% BD-rate loss is observed for RA and LD configuration respectively.

## Slide 4: Proposed method
Compress temporal motion data based on spatial candidates
Experiment various memory compression unit size (16x16, 32x32, 64x64)
①
②
③
④
⑤

## Slide 5: Experimental results
Tool-on test in VTM
 | Random access main10 |  |  |  |  | Low delay B main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.09% | -0.05% | 101% | 105% |  |  |  |  | 
Class A2 | -0.07% | -0.04% | -0.04% | 101% | 105% |  |  |  |  | 
Class B | -0.06% | -0.07% | -0.08% | 100% | 105% | -0.04% | 0.08% | 0.16% | 101% | 106%
Class C | -0.17% | -0.15% | -0.14% | 100% | 104% | -0.09% | -0.20% | -0.12% | 101% | 106%
Class E |  |  |  |  |  | -0.05% | -0.09% | 0.17% | 101% | 108%
Overall | -0.09% | -0.09% | -0.08% | 100% | 105% | -0.06% | -0.06% | 0.07% | 101% | 106%
Class D | -0.14% | 0.00% | -0.20% | 100% | 105% | -0.17% | -0.09% | -0.29% | 100% | 104%
 | Random access main10 |  |  |  |  | Low delay B main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.01% | 0.02% | 102% | 105% |  |  |  |  | 
Class A2 | 0.04% | 0.06% | 0.10% | 101% | 104% |  |  |  |  | 
Class B | 0.11% | 0.01% | 0.11% | 101% | 105% | 0.29% | 0.40% | 0.54% | 101% | 106%
Class C | 0.23% | 0.25% | 0.27% | 101% | 105% | 0.60% | 0.55% | 0.67% | 101% | 103%
Class E |  |  |  |  |  | 0.35% | 0.00% | -0.07% | 100% | 106%
Overall | 0.11% | 0.08% | 0.13% | 101% | 105% | 0.41% | 0.35% | 0.43% | 101% | 105%
Class D | 0.44% | 0.35% | 0.40% | 101% | 103% | 0.57% | 0.43% | 0.37% | 101% | 103%
 | Random access main10 |  |  |  |  | Low delay B main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.29% | 0.18% | 0.30% | 101% | 105% |  |  |  |  | 
Class A2 | 0.43% | 0.44% | 0.49% | 101% | 104% |  |  |  |  | 
Class B | 0.55% | 0.38% | 0.44% | 102% | 105% | 0.88% | 0.95% | 1.20% | 101% | 105%
Class C | 0.87% | 0.76% | 0.85% | 103% | 106% | 1.47% | 1.49% | 1.58% | 101% | 102%
Class E |  |  |  |  |  | 1.08% | 0.80% | 0.77% | 101% | 105%
Overall | 0.56% | 0.45% | 0.53% | 102% | 105% | 1.13% | 1.09% | 1.22% | 101% | 104%
Class D | 1.25% | 1.10% | 1.01% | 102% | 103% | 1.37% | 1.28% | 1.31% | 101% | 102%
16x16
32x32
64x64

## Slide 6: Conclusion
It is suggested to study proposed temporal motion data reduction in CE.