## Slide 1: Reduced Secondary Transform (RST)
LG ELECTRONICS
JVET-K0099

## Slide 2: Introduction
Current Secondary Transform
  Hypercube-Givens Transform (HyGT) is used for non-separable secondary transform (in BMS 4x4 NSST and in JEM both 4x4 and 8x8 used )
  Issues:
    Data should go through 9 ( 4*2 +1) layers for 4x4 and 25 (6*4+1) layers for 8x8
    Multiplication complexity
Proposal
  Direct matrix multiplication is proposed for applying secondary transform for both 4x4 and 8x8 NSST, with reduction for 8x8 case
  Modification in NSST index coding, where NSST index is not coded depending on the residual block.

## Slide 3: Transform Kernels
  For blocks with min(width, height) = 4, a 16x16 direct matrix multiplication is applied (4x4 NSST).
  For blocks with min(width, height) = 8, Reduced Secondary Transform (RST) is proposed based on an Rx64 direct matrix multiplication, where the results for R = 16 and 32 are reported (8x8 NSST).
  Transform kernels are trained and derived based on a simplified RD cost definition (in contrast to usual KLT derivation)

## Slide 4: NSST Index Coding
Forward 8x8 RST with R =16 uses 16×64 matrices
Produces non-zero coefficients only in the lower 4×4 region within the given 8×8 region
The 8×8 region except the lower 4×4 region is called ROI region (Fig 1)
If RST16 is applied ROI will only have zero coefficients
NSST index is not coded when any non-zero element is detected within the ROI region
It implies NSST index = 0.
Similarly for R =32 the non-zero coefficient could only be in the 2 top 4x4 corner, and we could exploit the above technique for the new ROI
Fig1. Scanning the position 17 to 64

## Slide 5: Results: VTM + RST (R=32)
Anchor: VTM 1.1
 | AI |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -5.72% | -6.06% | -7.41% | 245% | 106%
Class A2 | -4.14% | -4.51% | -5.07% | 251% | 107%
Class B | -4.55% | -4.79% | -4.31% | 253% | 105%
Class C | -6.31% | -4.98% | -5.43% | 267% | 104%
Class E | -6.81% | -5.61% | -5.48% | 228% | 101%
Overall | -5.44% | -5.13% | -5.40% | 250% | 105%
Class D | -5.67% | -4.28% | -4.43% | 280% | 105%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -3.23% | -5.35% | -6.58% | 133% | 102%
Class A2 | -1.96% | -2.59% | -2.64% | 122% | 102%
Class B | -2.64% | -3.88% | -3.67% | 126% | 102%
Class C | -3.34% | -3.25% | -3.74% | 126% | 102%
Class E |  |  |  |  | 
Overall | -2.81% | -3.75% | -4.07% | 127% | 102%
Class D | -2.44% | -2.23% | -2.85% | 127% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 6: Results: VTM + AMT ON + RST (R=32)
Anchor: VTM 1.1
 | AI |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -6.94% | -6.81% | -7.93% | 529% | 122%
Class A2 | -5.73% | -5.36% | -5.33% | 571% | 120%
Class B | -6.24% | -5.48% | -5.43% | 592% | 120%
Class C | -7.68% | -5.02% | -5.80% | 636% | 112%
Class E | -8.52% | -6.92% | -6.91% | 493% | 114%
Overall | -6.97% | -5.82% | -6.16% | 569% | 118%
Class D | -6.98% | -4.38% | -4.62% | 698% | 111%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4.18% | -5.35% | -6.28% | 282% | 111%
Class A2 | -3.40% | -2.49% | -2.20% | 234% | 108%
Class B | -4.26% | -4.26% | -4.31% | 255% | 109%
Class C | -4.51% | -3.06% | -3.64% | 259% | 105%
Class E |  |  |  |  | 
Overall | -4.14% | -3.80% | -4.10% | 257% | 108%
Class D | -3.56% | -2.16% | -2.79% | 257% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 7: BMS + NO BMS NSST + RST(R=32)
Anchor: BMS 1.1
 | AI |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.87% | -0.57% | -0.86% | 98% | 98%
Class A2 | -1.06% | -0.26% | -0.41% | 97% | 101%
Class B | -1.19% | -0.72% | -0.65% | 97% | 100%
Class C | -2.22% | -1.43% | -1.39% | 95% | 99%
Class E | -1.72% | -1.13% | -0.70% | 96% | 101%
Overall | -1.60% | -0.84% | -0.82% | 97% | 100%
Class D | -1.40% | -1.29% | -1.21% | 94% | 99%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.13% | -0.67% | -1.04% | 101% | 100%
Class A2 | -0.66% | -0.12% | -0.24% | 101% | 100%
Class B | -0.82% | -0.46% | -0.53% | 101% | 101%
Class C | -1.20% | -0.82% | -1.07% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.95% | -0.53% | -0.72% | 101% | 101%
Class D | -0.63% | -0.76% | -0.62% | 101% | 102%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 8: Results: VTM + RST (R=16)
Anchor: VTM 1.1
 | AI |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -5.10% | -5.12% | -6.43% | 242% | 104%
Class A2 | -3.72% | -4.05% | -4.69% | 247% | 105%
Class B | -4.07% | -4.16% | -3.70% | 247% | 104%
Class C | -5.86% | -4.52% | -4.91% | 258% | 101%
Class E | -6.42% | -5.11% | -4.96% | 222% | 103%
Overall | -4.97% | -4.54% | -4.80% | 244% | 103%
Class D | -5.29% | -3.82% | -3.91% | 271% | 104%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -2.89% | -4.42% | -5.73% | 133% | 102%
Class A2 | -1.81% | -2.21% | -2.33% | 122% | 102%
Class B | -2.36% | -3.08% | -2.95% | 124% | 100%
Class C | -3.01% | -2.92% | -3.03% | 124% | 97%
Class E |  |  |  |  | 
Overall | -2.53% | -3.13% | -3.40% | 125% | 100%
Class D | -2.29% | -2.05% | -2.57% | 125% | 98%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 9: Results: VTM + AMT ON + RST (R=16)
Anchor: VTM 1.1
 | AI |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -6.47% | -5.96% | -7.06% | 516% | 120%
Class A2 | -5.42% | -4.98% | -5.03% | 547% | 118%
Class B | -5.90% | -4.91% | -4.85% | 567% | 121%
Class C | -7.32% | -4.59% | -5.35% | 610% | 108%
Class E | -8.23% | -6.58% | -6.43% | 475% | 115%
Overall | -6.62% | -5.31% | -5.62% | 547% | 116%
Class D | -6.66% | -3.73% | -4.13% | 667% | 109%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -3.93% | -4.52% | -5.58% | 277% | 111%
Class A2 | -3.30% | -2.28% | -2.09% | 229% | 108%
Class B | -4.05% | -3.51% | -3.70% | 248% | 107%
Class C | -4.25% | -2.56% | -3.04% | 252% | 103%
Class E |  |  |  |  | 
Overall | -3.93% | -3.21% | -3.58% | 250% | 107%
Class D | -3.44% | -1.37% | -2.24% | 251% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 10: BMS + NO BMS NSST + RST(R=16)
Anchor: BMS 1.1
 | AI |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.38% | -0.09% | -0.44% | 95% | 98%
Class A2 | -0.78% | 0.10% | -0.20% | 94% | 99%
Class B | -0.86% | -0.30% | -0.21% | 93% | 99%
Class C | -1.84% | -1.04% | -1.05% | 91% | 97%
Class E | -1.41% | -0.84% | -0.37% | 92% | 98%
Overall | -1.24% | -0.45% | -0.46% | 93% | 98%
Class D | -1.11% | -0.74% | -0.89% | 91% | 98%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.89% | -0.12% | -0.55% | 100% | 100%
Class A2 | -0.56% | 0.31% | -0.09% | 100% | 100%
Class B | -0.64% | 0.08% | -0.01% | 99% | 100%
Class C | -0.98% | -0.33% | -0.60% | 99% | 100%
Class E |  |  |  |  | 
Overall | -0.77% | -0.03% | -0.29% | 99% | 100%
Class D | -0.46% | -0.34% | -0.27% | 99% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 11: Complexity Analysis
Multiplication:
  For 4x4 NSST : 16*16 = 256
  For 8x8 NSST (R=16): 16*64 = 1024
  For 8x8 NSST (R=32): 32*64 = 2048
Addition:
  For 4x4 NSST : 16*15 = 240
  For 8x8 NSST (R=16): Encoder: 16*63 = 1008 | Decoder: 15*64 = 960
  For 8x8 NSST (R=32): Encoder: 32*63 = 2016 | Decoder: 31*64 = 1984
Memory:
  For 4x4 NSST : 16*16 *9 = 0.28 KB
  For 8x8 NSST (R=16): 16*64*9 = 1.125 KB
  For 8x8 NSST (R=32): 32*64*9 = 2.25 KB
  The above result is per kernel, multiply with 35*3 for total kernels memory
Number of the iterations:
  No iteration, transform is done in one round.

## Slide 12: CONCLUSIONS
A direct matrix multiplication NSST, called RST is proposed
It improves the performance significantly
Meanwhile reduces the multiplication and multilayer complexity
Therefore it is recommended adopting the proposed RST in next VTM update.