## Slide 1: CE6-Related : Matrix multiplication based NSST with reduced memory map
Seung-Hwan Kim
JVET-K0100

## Slide 2: Transform Kernels
  Direct matrix multiplication is proposed for applying secondary transform for both 4x4 and 8x8 NSST, with reduction for 8x8 case
  For 4x4 NSST, a 16x16 direct matrix multiplication is applied.
  For 8x8 NSST, reduced secondary transform (RST) is proposed based on an Rx64 direct matrix multiplication, where the results for R = 16 and 32 are reported.

## Slide 3: Memory Reduction Map
  Proposed Memory Map reduced required # of transform set from 35 set to 6 set.

## Slide 4: Results
 |  | All Intra - Over VTM1.1 |  |  |  |  | Random Access - Over VTM1.1 |  |  |  | 
Test | # Kernel | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
BMS 4x4 | 55 | -2.99% | -3.58% | -3.68% | 256% | 107% | -1.31% | -3.09% | -3.06% | 129% | 105%
K0084 4x4 | 55 | -3.28% | -4.00% | -4.11% | 244% | 102% | -1.44% | -3.41% | -3.48% | 124% | 99%
K0084 4x4 | 22 | -3.12% | -3.86% | -3.93% | 244% | 101% | -1.39% | -3.36% | -3.39% | 126% | 100%
Proposed 4x4 | 55 | -3.67% | -4.20% | -4.34% | 245% | 105% | -1.65% | -3.58% | -3.57% | 125% | 101%
Proposed 4x4 | 16 | -3.45% | -3.81% | -3.90% | 243% | 104% | -1.53% | -3.16% | -3.11% | 125% | 102%
Proposed 4x4, 8x8 | 55 | -4.97% | -4.54% | -4.80% | 244% | 103% | -2.53% | -3.13% | -3.40% | 125% | 100%
Proposed 4x4, 8x8 | 16 | -4.32% | -3.81% | -3.95% | 248% | 106% | -2.14% | -2.58% | -2.85% | 125% | 101%
Proposed 4x4, 8x8 (RST32) | 55 | -5.44% | -5.13% | -5.40% | 250% | 105% | -2.81% | -3.75% | -4.07% | 127% | 102%
Over AMT on Anchor (RST32) | 55 | -3.60% | -4.33% | -4.69% | 270% | 97% | -2.00% | -3.77% | -3.98% | 152% | 99.%
  Proposed 4x4 NSST provides about 0.7% coding gain over BMS 4x4 NSST
  Proposed 8x8 NSST provides about 5% and 2.5% bit-rate savings for AI and RA

## Slide 5: Results (Secondary

## Slide 6: Complexity Analysis
Multiplication:
  For 4x4 NSST : 16*16 = 256
  For 8x8 NSST (R=16): 16*64 = 1024
Addition:
  For 4x4 NSST : 16*15 = 240
  For 8x8 NSST (R=16): Encoder: 16*63 = 1008 | Decoder: 15*64 = 960
Memory:
  For 4x4 NSST : 16*16 *9 = 0.28 KB
  For 8x8 NSST (R=16): 16*64*9 = 1.125 KB
  The above result is per kernel
No iteration, transform is done in one round.

## Slide 7: CONCLUSIONS
A direct matrix multiplication NSST, called RST is proposed
It improves the performance
Meanwhile reduces the multiplication and multilayer complexity

## Slide 8: NSST Index Coding
Forward 8x8 RST with R =16 uses 16×64 matrices
Produces non-zero coefficients only in the lower 4×4 region within the given 8×8 region
The 8×8 region except the lower 4×4 region is called ROI region (Fig 1)
If RST16 is applied ROI will only have zero coefficients
NSST index is not coded when any non-zero element is detected within the ROI region
It implies NSST index = 0.
Similarly for R =32 the non-zero coefficient could only be in the 2 top 4x4 corner, and we could exploit the above technique for the new ROI
Fig1. Scanning the position 17 to 64