## Slide 1: Affine Motion Vector Difference Coding
LG ELECTRONICS
JVET-K0101

## Slide 2: Introduction
Current Affine MVD Coding
  Affine MVD coding uses Left (LT) and Right (RT) control point motion vectors (CPMV).
  Each control point coded separately.
Proposal
  There exists a strong correlation between LT & RT MVDx and LT and RT MVDy.
  Statistical analysis shows, MVD combinations occurring with similar frequencies can be grouped together to form a Layer.
  Within each Layer, an Index is used to identify the exact combination of the MVD LT and RT.

## Slide 3: Layer and Index
Fig.1: Layer Concept
Fig. 2: Layers 0 and 1
Fig.1 Shows the distribution of MVDs into four Layers.
Fig.2 Shows, the MVD combinations (i.e., LT & RT) that correspond to Layers 0 and 1.
Data analysis suggests that approximately, 80% of all Affine MVD data lies within these four Layers.
Exploit MVD (LTx, RTx) and similarly MVD (LTy, RTy).

## Slide 4: Frequency Analysis
Freq. Distr. (MVD: LTx = 0 & RTx = 0) has the highest frequency.
MVDs within each Layer have similar frequency distribution.
Number of Layers used can be increased if required.
Larger MVDs occur less frequently.
Similar behavior observed for MVD: LTy and RTy.
Fig. 3: Frequency Distribution

## Slide 5: Decoder Structure
  Decoder initiates the decoding process by parsing information whether, the target Layer is greater than zero i.e., (Layerx_GT0).
  Once parsed, the flag indicates if Layer Id is greater than zero. If false, then the decoding proceeds to the decoding of y-MVD components.
Fig. 3: Decoder Structure MVDx.

## Slide 6: Algorithm Description
  If the Layerx_GT0 flag is true, then another flag is parsed indicating if the Layer Id is greater than one i.e., Layerx _GT1.
  If Layerx _GT1 is false, then the Layer Id is 1. Then the index is parsed and the MVD combination is deciphered.
  If the Layerx_GT1 flag is true, this implies that the smallest Layer under consideration is 2.
  The remaining Layer information is parsed and the Layer Id is determined. Following this, the index is parsed and the MVD combination is deciphered. The Layer Id coded using EG(1) and index represented using TB.

## Slide 7: RESULTS & CONCLUSIONS
 | Over BMS-1.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.33% | -0.12% | 100% | 99%
Class A2 | -0.16% | -0.20% | -0.12% | 101% | 100%
Class B | -0.14% | -0.31% | 0.22% | 101% | 101%
Class C | -0.04% | -0.02% | -0.21% | 101% | 101%
Overall | -0.09% | -0.08% | -0.03% | 101% | 101%
Anchor BMS 1.1
Number of frames is 33.
Observed gain of 0.09%.
We propose to further study this topic.