## Slide 1: Energy Assessment for Video Decoding (JVET-K0106)

## Slide 2: Introduction
Use of energy measurements for evaluation
Especially interesting for portable solutions
WiFi Receiver
Video Decoder
Display

## Slide 3: Measurement Methods
Power Meter
Performance Counters (e.g. RAPL for Intel)
  /sys/class/powercap/intel-rapl/intel-rapl:0/energy_uj (complete package) /sys/class/powercap/intel-rapl/intel-rapl:0/intel-rapl:0:0/energy_uj (CPU) /sys/class/powercap/intel-rapl/intel-rapl:0/intel-rapl:0:1/energy_uj (RAM)

## Slide 4: Measurement Method
Dynamic Decoding Energy
Power [W]

## Slide 5: Measurement Results
Rate-distortion and energy performance for BQTerrace
Sequence | Software | QP | YUV-PSNR | File size | Decoding Energy
BQTerrace | HM-16.18 | 22 | 39.32 dB | 3388451 Bytes | 17.58 J
 |  | 27 | 37.08 dB | 934539 Bytes | 11.59 J
 |  | 32 | 35.49 dB | 380594 Bytes | 9.23 J
 |  | 37 | 33.79 dB | 190716 Bytes | 8.64 J
 | JEM-7.0 | 22 | 39.45 dB | 3158360 Bytes | 104.85 J
 |  | 27 | 37.37 dB | 852039 Bytes | 73.32 J
 |  | 32 | 35.99 dB | 362688 Bytes | 69.95 J
 |  | 37 | 34.42 dB | 183538 Bytes | 77.49 J
 | VTM-1.0 | 22 | 39.36 dB | 3371320 Bytes | 27.78 J
 |  | 27 | 37.15 dB | 927732 Bytes | 14.14 J
 |  | 32 | 35.64 dB | 382417 Bytes | 10.42 J
 |  | 37 | 33.99 dB | 189886 Bytes | 9.25 J
Hardware: RaspberryPi 3B+ (released March 2018)

## Slide 6: Measurement Results
Rate-distortion and energy-distortion diagram
Sequence | Software | BDR | BDE
BQTerrace | JEM-7.0 | -22.79% | 561.76%
 | VTM-1.0 | -5.36% | 20.68%
Reference: HM-16.18
BDR: Bjontegaard-Delta Rate
BDE: Bjontegaard-Delta Energy

## Slide 7: Measurement Results
Rate-energy diagram
BDR: Bjontegaard-Delta Rate
BDE: Bjontegaard-Delta Energy

## Slide 8: Conclusions
Decoding energy may increase by more than 5x
Proposal to use energy for evaluation

## Slide 9: Backup
Relation between energy and processing time
Broadcom BCM2837B0 (2012)
ARM Cortex-A53 quad-core processor

## Slide 10: Backup
Relation between energy and processing time
Intel Core i7 3770 (eight cores, 2012)
DRAM energy

## Slide 11: Backup
Relation between energy of HM and FFmpeg-decoding

## Slide 12: Backup
Relation between energy ARM and Intel decoding

## Slide 13: Backup
Relation between energy and processing time
TI-OMAP4430 (2011)
ARM Cortex-A9 dual core processor