## Slide 1: Energy Modeling for Video Decoding (JVET-K0107)

## Slide 2: Introduction
Energy modeling based on coding tools
Simplifies energy analysis

## Slide 3: Energy Modeling
Feature based model:
A feature relates to coding tools, e.g., intra prediction

## Slide 4: Energy Modeling
Considered features for I-frames
Block size handling:
Feature f | Explanation | Block sizes
OFFSET | Offset energy | -
FRAME | Frame-wise energy | -
INTRA_PRED | Intra predicted blocks | 4x4 up to 128x128
COEFF | Nonzero coefficients | -
VAL | Coefficient value | -
TRANS | Inverse transforms | 4x4 up to 128x128

## Slide 5: Model Training
Training framework for specific energies

## Slide 6: Estimation Accuracy
Mean absolute estimation error
4.57%

## Slide 7: Training Results
Coding-tool specific energies
Feature | Trained specific energy [µJ]
OFFSET | 25808
FRAME | 30497
INTRA_PRED_4x4 | 1.833
INTRA_PRED_8x8 | 3.283
INTRA_PRED_16x16 | 9.141
INTRA_PRED_32x32 | 22.81
INTRA_PRED_64x64 | 80.28
INTRA_PRED_128x128 | 99.42
COEFF | 0.1155
VAL | -0.09176
TRANS_4x4 | 0.005478
TRANS_8x8 | 1.627
TRANS_16x16 | 2.892
TRANS_32x32 | 9.941
TRANS_64x64 | 25.94
TRANS_128x128 | 285.0
Feature | 
OFFSET | 25808
FRAME | 30497
INTRA_PRED_4x4 | 1.833
INTRA_PRED_8x8 | 3.283
INTRA_PRED_16x16 | 9.141
INTRA_PRED_32x32 | 22.81
INTRA_PRED_64x64 | 80.28
INTRA_PRED_128x128 | 99.42
COEFF | 0.1155
VAL | -0.09176
TRANS_4x4 | 0.005478
TRANS_8x8 | 1.627
TRANS_16x16 | 2.892
TRANS_32x32 | 9.941
TRANS_64x64 | 25.94
TRANS_128x128 | 285.0

## Slide 8: Conclusions
Energy model for detailed energy assessment
Energy measurement not necessary