## Slide 1: Decoding-Energy-Rate-Distortion Optimization (JVET-K0108)

## Slide 2: Introduction
Energy consumption critical for portable devices
Decoding-energy-rate-distortion optimization encodes bit streams requiring less decoding energy

## Slide 3: Extended RDO
Cost function
additional Lagrange
multiplier
feature based model
(see JVET-K0107)

## Slide 4: Lagrange Multiplier
Memoryless Gaussian source [Berger71]:
High-rate approximation [Gish68]:
High-level relation between rate and energy [Raoufi13]:

## Slide 5: Lagrange Multiplier
With
we obtain a relation between the distortion and the Lagrange multipliers
Introducing a two new parameters

## Slide 6: Rate-Energy Control
We can calculate the Lagrange multipliers with
QP is related to distortion
determines the rate-energy trade-off

## Slide 7: Evaluation Results
Savings reported for HEVC [HHK17]
- FFmpeg decoding
- ARM-CortexA9 dual core processor

## Slide 8: Evaluation Results
Specific energy values for JEM-5.1 all intra coding
Feature | Explanation | Normalized value
E0 | Offset energy | 25808
SLICE | Energy to decode one slice | 30497
INTRA_L0 | Intra prediction (4x4 pixels) | 1.833
INTRA_L1 | Intra prediction (8x8 pixels and smaller) | 3.283
INTRA_L2 | Intra prediction (16x16 pixels and smaller) | 9.141
INTRA_L3 | Intra prediction (32x32 pixels and smaller) | 22.81
INTRA_L4 | Intra prediction (64x64 pixels and smaller) | 80.28
INTRA_L5 | Intra prediction (128x128 pixels and smaller) | 99.42
COEFF | Decoding a single nonzero coefficient | 0.1155
VAL | Decoding the remaining value of coefficients | -0.09176
TRANS_L0 | Transform (4x4 pixels) | 0.005478
TRANS_L1 | Transform (8x8 pixels and smaller) | 1.627
TRANS_L2 | Transform (16x16 pixels and smaller) | 2.892
TRANS_L3 | Transform (32x32 pixels and smaller) | 9.941
TRANS_L4 | Transform (64x64 pixels and smaller) | 25.94
TRANS_L5 | Transform (128x128 pixels and smaller) | 285.0
 | Explanation | Normalized value
E0 | Offset energy | 25808
SLICE | Energy to decode one slice | 30497
INTRA_L0 | Intra prediction (4x4 pixels) | 1.833
INTRA_L1 | Intra prediction (8x8 pixels and smaller) | 3.283
INTRA_L2 | Intra prediction (16x16 pixels and smaller) | 9.141
INTRA_L3 | Intra prediction (32x32 pixels and smaller) | 22.81
INTRA_L4 | Intra prediction (64x64 pixels and smaller) | 80.28
INTRA_L5 | Intra prediction (128x128 pixels and smaller) | 99.42
COEFF | Decoding a single nonzero coefficient | 0.1155
VAL | Decoding the remaining value of coefficients | -0.09176
TRANS_L0 | Transform (4x4 pixels) | 0.005478
TRANS_L1 | Transform (8x8 pixels and smaller) | 1.627
TRANS_L2 | Transform (16x16 pixels and smaller) | 2.892
TRANS_L3 | Transform (32x32 pixels and smaller) | 9.941
TRANS_L4 | Transform (64x64 pixels and smaller) | 25.94
TRANS_L5 | Transform (128x128 pixels and smaller) | 285.0

## Slide 9: Encoding Results Cactus
Rate-distortion and decoding-energy-distortion
Bjøntegaard-Delta:
 | BDR (%) | BDE (%)
0 | 0 | 0
0.25 | 0.02 | -0.34
0.5 | 7.62 | -6.69
0.75 | 25.64 | -6.67
1 | 28.80 | -6.35
 | BDR (%) | BDE (%)
0 | 0 | 0
0.25 | 0.02 | -0.34
0.5 | 7.62 | -6.69
0.75 | 25.64 | -6.67
1 | 28.80 | -6.35

## Slide 10: Conclusions
Extended RDO can generate energy saving bit streams
Potential savings of at least 20% expected

## Slide 11: Literature
[Berger71]: T. Berger and T. Kailath. Rate Distortion Theory - A Mathematical Basis for Data Compression. Prentice-Hall Electrical Engineering Series, 1971.
[Gish68]: H. Gish and J. Pierce. Asymptotically efficient quantizing. IEEE Transactions on Information Theory, 14(5):676–683, Sep 1968.
[Raoufi13]: P. Raoufi and J. Peters. Energy-efficient wireless video streaming with H.264 coding. In Proc. IEEE International Conference on Multimedia and Expo Workshops (ICMEW), pages 1–6, Jul 2013.
[HHK17]: C. Herglotz, A. Heindel, A. Kaup, „Decoding-Energy-Rate-Distortion Optimization for Video Coding“, IEEE Transactions on Circuits and Systems for Video Technology, preprint, DOI: 10.1109/TCSVT.2017.2771819, Nov 2017.
[HSRSK18]: C. Herglotz, D. Springer, M. Reichenbach, B. Stabernack, and A. Kaup, “Modeling the energy consumption of the HEVC decoding process,” IEEE Transactions on Circuits and Systems for Video Technology, 28:217–229, Jan 2018.

## Slide 12: Rate-Energy Diagram
Summary for JEM-5.1 intra coding