## Slide 1: JVET-K0126: Simplified multiple-core transform for intra residual coding
Yongbing Lin, Quanhe Yu, Jianhua Zheng (HiSilicon)
Xiaoqiang Cao, Ce Zhu (UESTC)

## Slide 2: Summary
Simplified AMT (Intra only) for better trade-off between performance and complexity
  Unification of transform core for intra and inter residual coding (DCT2, DST7, DCT8)
  number of transform cores: 5 -> 3
  Number of transform pairs: 5 -> 3
  No transform subset concept
  Encoding speedup: ~15% (AI) with negligible performance loss
Test results
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 (proposal) | -3.23% | -1.68% | -1.64% | 196% | 113%
VTM+V2 (proposal) | -3.10% | -1.79% | -1.80% | 177% | 113%
VTM+AMT | -3.46% | -1.55% | -1.53% | 209% | 115%
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 (proposal) | -1.43% | -0.53% | -0.57% | 121% | 102%
VTM+V2 (proposal) | -1.39% | -0.65% | -0.76% | 116% | 103%
VTM+AMT | -1.53% | -0.50% | -0.63% | 125% | 103%
Performance under AI configuration on top of VTM-1.0
Performance under RA configuration on top of VTM-1.0

## Slide 3: Introduction
Background: AMT in BMS1.0
  3%+ gain with 2X encoding time (AI)
  Usage of 5 kinds of transform cores
  RDO based transform pair selection from maximum 5 ones
  Concept of transform subset
Proposal: simplified AMT for intra residual coding
  Tradeoff between performance and complexity
  Reduced number of transform cores
  Reduced number of transform pairs to be signaled
  no transform subset

## Slide 4: Proposed versions of simplified AMT
1st proposed version
  3 kinds of transform cores
  4 transform pairs to be signaled
2nd proposed version further reduces number of transform pairs
AMT flag | Transform pair（V, H） | Transform pair index | Code
0 | ( DCT-2，DCT-2 ) | N/A | N/A
1 | ( DST-7，DST-7 ) | 0 | 0
 | ( DCT-8，DST-7 ) | 1 | 10
 | ( DST-7，DCT-8 ) | 2 | 11
AMT flag | Transform pair（V, H） | Transform pair index | Code
0 | ( DCT-2，DCT-2 ) | N/A | N/A
1 | ( DST-7，DST-7 ) | 0 | 0
 | ( DST-7，DCT-8 ): if IntraPredMode <= N ( DCT-8，DST-7 ): if IntraPredMode > N | 1 | 1
#1 proposed version: transform pair and signaling
#2 proposed version: transform pair and signaling

## Slide 5: Test results (AI) for the proposals
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 | -3.23% | -1.68% | -1.64% | 196% | 113%
VTM+V2 | -3.10% | -1.79% | -1.80% | 177% | 113%
VTM+AMT | -3.46% | -1.55% | -1.53% | 209% | 115%
Comparison of coding performance between proposals and AMT, for AI case on top of VTM-1.0
Figure 1. Trade-off between performance (BDR-Y) and complexity (EncTime+5*DecTime)
Chart: EncTime+5*DecTime
| 1.2683333333333333
VTM+V1 | -0.0323
VTM+V2 | -0.031
VTM+AMT | -0.0346

## Slide 6: Test results (RA) for the proposals
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 | -1.43% | -0.53% | -0.57% | 121% | 102%
VTM+V2 | -1.39% | -0.65% | -0.76% | 116% | 103%
VTM+AMT | -1.53% | -0.50% | -0.63% | 125% | 103%
Comparison of coding performance between proposals and AMT, for RA case on top of VTM-1.0
Figure 2. Trade-off between performance (BDR-Y) and complexity (EncTime+5*DecTime)
Chart: EncTime+5*DecTime
| 1.0516666666666667
VTM+V1 | -0.0143
VTM+V2 | -0.0139
VTM+AMT | -0.0153

## Slide 7: Conclusion
The proposals with better trade-off than the existing AMT
  Unification of transform cores for Intra and inter residuals
  Lower decoder complexity with reduced number of transform cores
  Encoding speedup with reduced number of transform pairs
  No transform subset concept
recommend to inclusion of the proposals in next VTM/BMS

## Slide 8
Thank You
www.hisilicon.com

## Slide 9: Test results for the 1st version
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -3.05% | -1.38% | -1.28% | 191% | 118% | 0.25% | -0.06% | -0.06% | 95% | 98%
Class A2 | -2.95% | -1.70% | -1.52% | 195% | 113% | 0.21% | -0.05% | -0.09% | 95% | 97%
Class B | -3.21% | -1.58% | -1.50% | 200% | 114% | 0.26% | -0.14% | -0.09% | 94% | 97%
Class C | -2.95% | -1.09% | -1.27% | 204% | 107% | 0.18% | -0.19% | -0.11% | 93% | 100%
Class E | -4.12% | -2.92% | -2.82% | 187% | 113% | 0.29% | -0.19% | -0.17% | 95% | 97%
Overall | -3.23% | -1.68% | -1.64% | 196% | 113% | 0.24% | -0.13% | -0.10% | 94% | 98%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.31% | -0.53% | -0.45% | 126% | 104% | 0.11% | -0.04% | 0.10% | 96% | 98%
Class A2 | -1.04% | -0.30% | -0.16% | 118% | 102% | 0.09% | -0.03% | -0.14% | 97% | 99%
Class B | -1.64% | -0.72% | -0.78% | 121% | 103% | 0.15% | -0.06% | 0.20% | 97% | 99%
Class C | -1.55% | -0.48% | -0.71% | 120% | 101% | 0.05% | 0.01% | 0.00% | 97% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -1.43% | -0.53% | -0.57% | 121% | 102% | 0.11% | -0.03% | 0.06% | 97% | 99%
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.23% | -1.43% | -2.05% | 203% | 110% | 0.32% | 0.31% | 0.13% | 94% | 97%
Class A2 | -2.16% | -1.79% | -1.54% | 208% | 108% | 0.26% | 0.22% | -0.05% | 93% | 99%
Class B | -2.09% | -1.59% | -1.79% | 214% | 106% | 0.24% | 0.12% | 0.13% | 93% | 98%
Class C | -1.69% | -1.11% | -1.39% | 221% | 103% | 0.12% | 0.03% | 0.07% | 91% | 100%
Class E | -2.39% | -2.64% | -2.64% | 203% | 104% | 0.22% | 0.01% | -0.04% | 93% | 96%
Overall | -2.09% | -1.67% | -1.85% | 211% | 106% | 0.23% | 0.13% | 0.06% | 93% | 98%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.10% | -0.98% | -1.57% | 149% | 102% | 0.15% | 0.16% | 0.20% | 93% | 99%
Class A2 | -0.73% | -1.14% | -0.54% | 135% | 97% | 0.11% | 0.16% | 0.04% | 94% | 98%
Class B | -1.12% | -1.29% | -1.12% | 141% | 99% | 0.11% | 0.18% | 0.28% | 94% | 98%
Class C | -0.93% | -0.90% | -0.94% | 144% | 100% | 0.08% | 0.23% | 0.00% | 94% | 101%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.99% | -1.09% | -1.04% | 142% | 100% | 0.11% | 0.18% | 0.14% | 94% | 99%

## Slide 10: Test results for the 2nd version
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.89% | -1.51% | -1.39% | 174% | 119% | 0.42% | -0.20% | -0.17% | 86% | 98%
Class A2 | -2.77% | -1.77% | -1.68% | 177% | 114% | 0.40% | -0.11% | -0.25% | 86% | 98%
Class B | -3.08% | -1.69% | -1.65% | 181% | 115% | 0.39% | -0.25% | -0.23% | 84% | 98%
Class C | -2.79% | -1.24% | -1.52% | 182% | 106% | 0.34% | -0.35% | -0.36% | 82% | 99%
Class E | -4.07% | -3.00% | -2.97% | 170% | 114% | 0.34% | -0.27% | -0.33% | 86% | 97%
Overall | -3.10% | -1.79% | -1.80% | 177% | 113% | 0.38% | -0.24% | -0.27% | 85% | 98%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.28% | -0.68% | -0.65% | 120% | 105% | 0.14% | -0.20% | -0.10% | 92% | 99%
Class A2 | -1.04% | -0.45% | -0.26% | 114% | 103% | 0.10% | -0.18% | -0.23% | 94% | 100%
Class B | -1.58% | -0.72% | -1.03% | 116% | 104% | 0.21% | -0.06% | -0.05% | 93% | 100%
Class C | -1.47% | -0.68% | -0.87% | 116% | 102% | 0.13% | -0.20% | -0.16% | 93% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -1.39% | -0.65% | -0.76% | 116% | 103% | 0.15% | -0.15% | -0.13% | 93% | 100%
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.08% | -1.51% | -2.05% | 191% | 112% | 0.48% | 0.24% | 0.13% | 88% | 98%
Class A2 | -1.96% | -1.90% | -1.60% | 192% | 109% | 0.47% | 0.11% | -0.11% | 86% | 100%
Class B | -1.96% | -1.66% | -1.81% | 196% | 107% | 0.37% | 0.05% | 0.11% | 85% | 100%
Class C | -1.57% | -1.18% | -1.43% | 200% | 103% | 0.24% | -0.05% | 0.03% | 82% | 100%
Class E | -2.37% | -2.67% | -2.65% | 187% | 107% | 0.25% | -0.02% | -0.05% | 86% | 99%
Overall | -1.96% | -1.74% | -1.87% | 194% | 107% | 0.36% | 0.06% | 0.03% | 85% | 99%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.05% | -0.79% | -1.58% | 139% | 103% | 0.20% | 0.35% | 0.20% | 87% | 100%
Class A2 | -0.72% | -1.04% | -0.63% | 128% | 99% | 0.12% | 0.26% | -0.06% | 90% | 99%
Class B | -1.06% | -1.20% | -1.20% | 132% | 101% | 0.17% | 0.27% | 0.20% | 88% | 100%
Class C | -0.89% | -0.98% | -0.91% | 134% | 100% | 0.12% | 0.15% | 0.03% | 88% | 101%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.95% | -1.03% | -1.08% | 133% | 101% | 0.15% | 0.25% | 0.10% | 88% | 100%