## Slide 1: JVET-K0126: Simplified multiple-core transform for intra residual coding
Yongbing Lin, Quanhe Yu, Jianhua Zheng (HiSilicon)
Xiaoqiang Cao, Ce Zhu (UESTC)

## Slide 2: Introduction
Background: AMT in BMS1.0
  3%+ gain with 2X encoding time (AI)
  Usage of 5 transform types
  Selection from maximum 5 Transform pair candidates
  transform subset selection depending on Intra mode
Proposal: simplified AMT for intra residual coding
  Reduced transform types
  Reduced transform pair candidates
  no transform subset selection

## Slide 3: AMT approach discussed in CE6
Only DCT-2, DST-7, DCT8
Restriction on larger transform size
Signaled transform pairs for AMT
  0: (DST-7, DST-7)
  1: (DST-7, DCT-8)
  2: (DCT-8, DST-7)
  3: (DCT-8, DCT-8)
Very similar to JVET-K0171

## Slide 4: Proposed versions of simplified AMT
Transform types: DCT-2, DCT8, DST-7
removal of (DCT-8, DCT-8), only other 3 transform pairs used
Proposed 2 methods for signalling transform pairs
AMT flag | Transform pair（H, V） | Transform pair index | Codeword
0 | ( DCT-2，DCT-2 ) | N/A | N/A
1 | ( DST-7，DST-7 ) | 0 | 0
 | ( DCT-8，DST-7 ) | 1 | 10
 | ( DST-7，DCT-8 ) | 2 | 11
AMT flag | Transform pair（H, V） | Transform pair index | Codeword
0 | ( DCT-2，DCT-2 ) | N/A | N/A
1 | ( DST-7，DST-7 ) | 0 | 0
 | ( DST-7，DCT-8 ): if IntraPredMode <= N ( DCT-8，DST-7 ): if IntraPredMode > N * | 1 | 1
#1 proposed version: transform pair and signaling
#2 proposed version: transform pair and signaling
* N=18 for VTM; N=34 for BMS

## Slide 5: Test results (AI) for the proposals
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+AMT | -3.46% | -1.55% | -1.53% | 209% | 115%
JVET-K0171 (4 trans. pairs) | -3.29% | -1.60% | -1.60% | 207% | 122%
VTM+V1 | -3.23% | -1.68% | -1.64% | 196% | 113%
VTM+V2 | -3.10% | -1.79% | -1.80% | 177% | 113%
Comparison of coding performance between proposals and AMT, for AI case on top of VTM-1.0
Figure 1. performance (BDR-Y) v.s. complexity (EncTime)
Chart: EncTime
| 1.96
VTM+V1 | -0.0323
VTM+V2 | -0.031
JVET-K0171 | -0.032906
VTM+AMT | -0.0346

## Slide 6: Conclusion
The proposed versions
  Unification of transform types for Intra and inter residuals
  Lower decoder complexity with reduced transform types
  10~30% encoding time reduction
Recommend
  No signaling transform pair (DCT-8, DCT-8)

## Slide 7
Thank You
www.hisilicon.com

## Slide 8: Test results (RA) for the proposals
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 | -1.43% | -0.53% | -0.57% | 121% | 102%
VTM+V2 | -1.39% | -0.65% | -0.76% | 116% | 103%
VTM+AMT | -1.53% | -0.50% | -0.63% | 125% | 103%
Comparison of coding performance between proposals and AMT, for RA case on top of VTM-1.0
Figure 2. Trade-off between performance (BDR-Y) and complexity (EncTime+5*DecTime)/6
Chart: (EncTime+5*DecTime)/6
| 1.0516666666666667
VTM+V1 | -0.0143
VTM+V2 | -0.0139
VTM+AMT | -0.0153

## Slide 9: Summary
Simplified AMT (Intra only) for better trade-off between performance and complexity
  Unification of transform types for intra and inter residual coding (DCT2, DST7, DCT8)
  number of transform types: 5 -> 3
  Number of transform pair candidates: 5 -> 3
  No transform subset concept
  Encoding speedup: 10~30% (AI) with negligible performance loss
Test results
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 (proposal) | -3.23% | -1.68% | -1.64% | 196% | 113%
VTM+V2 (proposal) | -3.10% | -1.79% | -1.80% | 177% | 113%
VTM+AMT | -3.46% | -1.55% | -1.53% | 209% | 115%
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 (proposal) | -1.43% | -0.53% | -0.57% | 121% | 102%
VTM+V2 (proposal) | -1.39% | -0.65% | -0.76% | 116% | 103%
VTM+AMT | -1.53% | -0.50% | -0.63% | 125% | 103%
Performance under AI configuration on top of VTM-1.0
Performance under RA configuration on top of VTM-1.0

## Slide 10: Test results for the 1st version
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -3.05% | -1.38% | -1.28% | 191% | 118% | 0.25% | -0.06% | -0.06% | 95% | 98%
Class A2 | -2.95% | -1.70% | -1.52% | 195% | 113% | 0.21% | -0.05% | -0.09% | 95% | 97%
Class B | -3.21% | -1.58% | -1.50% | 200% | 114% | 0.26% | -0.14% | -0.09% | 94% | 97%
Class C | -2.95% | -1.09% | -1.27% | 204% | 107% | 0.18% | -0.19% | -0.11% | 93% | 100%
Class E | -4.12% | -2.92% | -2.82% | 187% | 113% | 0.29% | -0.19% | -0.17% | 95% | 97%
Overall | -3.23% | -1.68% | -1.64% | 196% | 113% | 0.24% | -0.13% | -0.10% | 94% | 98%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.31% | -0.53% | -0.45% | 126% | 104% | 0.11% | -0.04% | 0.10% | 96% | 98%
Class A2 | -1.04% | -0.30% | -0.16% | 118% | 102% | 0.09% | -0.03% | -0.14% | 97% | 99%
Class B | -1.64% | -0.72% | -0.78% | 121% | 103% | 0.15% | -0.06% | 0.20% | 97% | 99%
Class C | -1.55% | -0.48% | -0.71% | 120% | 101% | 0.05% | 0.01% | 0.00% | 97% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -1.43% | -0.53% | -0.57% | 121% | 102% | 0.11% | -0.03% | 0.06% | 97% | 99%
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.23% | -1.43% | -2.05% | 203% | 110% | 0.32% | 0.31% | 0.13% | 94% | 97%
Class A2 | -2.16% | -1.79% | -1.54% | 208% | 108% | 0.26% | 0.22% | -0.05% | 93% | 99%
Class B | -2.09% | -1.59% | -1.79% | 214% | 106% | 0.24% | 0.12% | 0.13% | 93% | 98%
Class C | -1.69% | -1.11% | -1.39% | 221% | 103% | 0.12% | 0.03% | 0.07% | 91% | 100%
Class E | -2.39% | -2.64% | -2.64% | 203% | 104% | 0.22% | 0.01% | -0.04% | 93% | 96%
Overall | -2.09% | -1.67% | -1.85% | 211% | 106% | 0.23% | 0.13% | 0.06% | 93% | 98%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.10% | -0.98% | -1.57% | 149% | 102% | 0.15% | 0.16% | 0.20% | 93% | 99%
Class A2 | -0.73% | -1.14% | -0.54% | 135% | 97% | 0.11% | 0.16% | 0.04% | 94% | 98%
Class B | -1.12% | -1.29% | -1.12% | 141% | 99% | 0.11% | 0.18% | 0.28% | 94% | 98%
Class C | -0.93% | -0.90% | -0.94% | 144% | 100% | 0.08% | 0.23% | 0.00% | 94% | 101%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.99% | -1.09% | -1.04% | 142% | 100% | 0.11% | 0.18% | 0.14% | 94% | 99%

## Slide 11: Test results for the 2nd version
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.89% | -1.51% | -1.39% | 174% | 119% | 0.42% | -0.20% | -0.17% | 86% | 98%
Class A2 | -2.77% | -1.77% | -1.68% | 177% | 114% | 0.40% | -0.11% | -0.25% | 86% | 98%
Class B | -3.08% | -1.69% | -1.65% | 181% | 115% | 0.39% | -0.25% | -0.23% | 84% | 98%
Class C | -2.79% | -1.24% | -1.52% | 182% | 106% | 0.34% | -0.35% | -0.36% | 82% | 99%
Class E | -4.07% | -3.00% | -2.97% | 170% | 114% | 0.34% | -0.27% | -0.33% | 86% | 97%
Overall | -3.10% | -1.79% | -1.80% | 177% | 113% | 0.38% | -0.24% | -0.27% | 85% | 98%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 +AMT |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.28% | -0.68% | -0.65% | 120% | 105% | 0.14% | -0.20% | -0.10% | 92% | 99%
Class A2 | -1.04% | -0.45% | -0.26% | 114% | 103% | 0.10% | -0.18% | -0.23% | 94% | 100%
Class B | -1.58% | -0.72% | -1.03% | 116% | 104% | 0.21% | -0.06% | -0.05% | 93% | 100%
Class C | -1.47% | -0.68% | -0.87% | 116% | 102% | 0.13% | -0.20% | -0.16% | 93% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -1.39% | -0.65% | -0.76% | 116% | 103% | 0.15% | -0.15% | -0.13% | 93% | 100%
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.08% | -1.51% | -2.05% | 191% | 112% | 0.48% | 0.24% | 0.13% | 88% | 98%
Class A2 | -1.96% | -1.90% | -1.60% | 192% | 109% | 0.47% | 0.11% | -0.11% | 86% | 100%
Class B | -1.96% | -1.66% | -1.81% | 196% | 107% | 0.37% | 0.05% | 0.11% | 85% | 100%
Class C | -1.57% | -1.18% | -1.43% | 200% | 103% | 0.24% | -0.05% | 0.03% | 82% | 100%
Class E | -2.37% | -2.67% | -2.65% | 187% | 107% | 0.25% | -0.02% | -0.05% | 86% | 99%
Overall | -1.96% | -1.74% | -1.87% | 194% | 107% | 0.36% | 0.06% | 0.03% | 85% | 99%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.0 with AMT disabled |  |  |  |  | Over BMS-1.0 (AMT Intra only) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.05% | -0.79% | -1.58% | 139% | 103% | 0.20% | 0.35% | 0.20% | 87% | 100%
Class A2 | -0.72% | -1.04% | -0.63% | 128% | 99% | 0.12% | 0.26% | -0.06% | 90% | 99%
Class B | -1.06% | -1.20% | -1.20% | 132% | 101% | 0.17% | 0.27% | 0.20% | 88% | 100%
Class C | -0.89% | -0.98% | -0.91% | 134% | 100% | 0.12% | 0.15% | 0.03% | 88% | 101%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.95% | -1.03% | -1.08% | 133% | 101% | 0.15% | 0.25% | 0.10% | 88% | 100%

## Slide 12: Test results (AI) for the proposals
Tool | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
VTM+V1 | -3.23% | -1.68% | -1.64% | 196% | 113%
VTM+V2 | -3.10% | -1.79% | -1.80% | 177% | 113%
VTM+AMT | -3.46% | -1.55% | -1.53% | 209% | 115%
Comparison of coding performance between proposals and AMT, for AI case on top of VTM-1.0
Figure 1. Trade-off between performance (BDR-Y) and complexity (EncTime+5*DecTime)/6
Chart: (EncTime+5*DecTime)/6
| 1.2683333333333333
VTM+V1 | -0.0323
VTM+V2 | -0.031
VTM+AMT | -0.0346