## Slide 1: Split Unit Coding Order
July,10, 2018
Yinji Piao
JVET-K0133
(CE1.4)

## Slide 2
Split Unit Coding Order (SUCO)
  Signaling of child tree coding order for each vertical split
    1 flag for each vertical split (SPLIT_BI_VER, SPLIT_TR_VER, SPLIT_QT)
    Same direction for above two and bottom two for SPLIT_QT
  Applied depth
    [MIN_SUCO_DEPTH, MAX_SUCO_DEPTH]
    MIN_SUCO_DEPTH: min(log2_width, log2_height)
    MAX_SUCO_DEPTH: max(log2_width, log2_height)
  Intra/Inter prediction modification according to Left/Right availability
    LR_10, LR_01, LR_11, LR_00
SUCO
Coded
Un-coded
Split Unit
BT
TT
QT
L2R
R2L
Split (QT/BT/TT)
Intra reference pixels
Inter MVP position

## Slide 3: SUCO
SUCO related tool extension
  Intra prediction
    Reference pixel, Angular prediction, Planar, DC, MPM
    DPCM, PDPC, LM_CHROMA
  Inter prediction
    Skip/Merge, AMVP
    OBMC, ATMVP, FRUC, IC, AFFINE
  Others
    Deblock
    Context derivation for flags
Tc
H
Right candidates
Left candidates
O
X
X
O
LR_10
LR_01
c
p
c
q
p
Intra angular prediction
Inter MV candidates

## Slide 4: Experimental result
BMS s/w
  VTM/BMS configuration
  CTC + Direct implementation of SUCO
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.33% | -0.50% | -0.50% | 137% | 110% | -0.09% | 0.04% | -0.16% | 131% | 105%
Class A2 | -0.25% | -0.50% | -0.34% | 135% | 114% | -0.12% | -0.24% | -0.20% | 129% | 105%
Class B | -0.19% | -0.39% | -0.45% | 136% | 114% | -0.09% | -0.11% | -0.25% | 128% | 106%
Class C | -0.14% | -0.33% | -0.44% | 132% | 114% | -0.08% | -0.07% | -0.08% | 127% | 111%
Class E | -0.30% | -0.99% | -0.98% | 135% | 111% | -0.21% | -0.30% | -0.36% | 128% | 107%
Overall | -0.23% | -0.51% | -0.53% | 135% | 113% | -0.11% | -0.13% | -0.21% | 128% | 107%
Class D | -0.09% | -0.22% | -0.13% | 133% | 116% | -0.06% | 0.01% | 0.03% | 128% | 111%
Class F (optional) | -0.05% | -0.05% | -0.15% | 139% | 116% | -0.03% | 0.01% | -0.24% | 135% | 111%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.30% | -0.14% | 115% | 108% | 0.00% | -0.05% | -0.02% | 112% | 102%
Class A2 | -0.07% | -0.35% | -0.26% | 118% | 104% | -0.04% | -0.19% | -0.14% | 115% | 102%
Class B | -0.07% | -0.30% | -0.61% | 120% | 104% | -0.05% | -0.07% | -0.34% | 117% | 102%
Class C | -0.11% | -0.32% | -0.41% | 121% | 108% | 0.00% | 0.06% | -0.36% | 119% | 103%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.08% | -0.31% | -0.39% | 119% | 106% | -0.02% | -0.05% | -0.24% | 116% | 102%
Class D | 0.02% | -0.09% | -0.26% | 121% | 107% | 0.02% | -0.08% | -0.29% | 118% | 103%
Class F (optional) | -0.18% | -0.25% | -0.24% | 132% | 107% | -0.18% | -0.01% | -0.03% | 125% | 104%

## Slide 5: Experimental result
Other configuration of SUCO
  BMS s/w: VTM configuration
  Include square size
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.81% | -1.11% | -1.23% | 239% | 113% | -1.59% | -2.24% | -2.23% | 413% | 115%
Class A2 | -0.66% | -1.34% | -1.00% | 238% | 118% | -1.23% | -2.14% | -1.82% | 406% | 119%
Class B | -0.56% | -1.07% | -1.25% | 236% | 114% | -1.18% | -2.14% | -2.62% | 406% | 118%
Class C | -0.59% | -0.96% | -1.30% | 234% | 123% | -1.07% | -1.79% | -2.26% | 399% | 117%
Class E | -0.76% | -2.27% | -2.36% | 244% | 115% | -1.67% | -3.66% | -3.78% | 410% | 118%
Overall | -0.66% | -1.30% | -1.40% | 238% | 117% | -1.31% | -2.33% | -2.54% | 406% | 118%
Class D | -0.88% | -1.14% | -1.19% | 240% | 126% | -1.18% | -1.94% | -1.89% | 397% | 116%
Class F (optional) | -0.35% | -0.35% | -0.43% | 243% | 125% | -0.69% | -0.99% | -0.95% | 414% | 120%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.37% | -0.45% | 133% | 111% | -0.33% | -1.34% | -0.94% | 162% | 115%
Class A2 | 0.10% | -0.90% | -0.28% | 140% | 108% | -0.10% | -1.31% | -0.87% | 174% | 112%
Class B | 0.13% | -0.66% | -0.93% | 154% | 119% | -0.37% | -1.54% | -2.13% | 186% | 112%
Class C | -0.08% | -0.64% | -0.63% | 164% | 122% | -0.52% | -1.11% | -1.38% | 211% | 110%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.04% | -0.64% | -0.62% | 149% | 116% | -0.35% | -1.34% | -1.44% | 184% | 112%
Class D | -0.09% | -0.23% | -0.29% | 181% | 124% | -0.43% | -0.94% | -1.20% | 240% | 109%
Class F (optional) | -0.12% | -0.24% | -0.08% | 199% | 126% | -0.25% | -0.45% | -0.47% | 261% | 116%
size64~32
size32~16

## Slide 6: Experimental result
Other configuration of SUCO
  BMS s/w: VTM configuration
  Include square size
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.58% | -2.36% | -2.35% | 451% | 113% | -2.03% | -3.27% | -3.08% | 783% | 112%
Class A2 | -1.20% | -2.31% | -1.80% | 446% | 115% |  |  |  |  | 
Class B | -1.15% | -2.19% | -2.64% | 447% | 115% | -1.44% | -2.83% | -3.54% | 758% | 115%
Class C | -1.07% | -1.79% | -2.28% | 434% | 116% | -1.22% | -2.06% | -2.58% | 717% | 122%
Class E | -1.51% | -3.70% | -4.04% | 455% | 112% | -1.68% | -4.15% | -4.58% | 775% | 124%
Overall | -1.27% | -2.40% | -2.60% | 446% | 114% |  |  |  |  | 
Class D | -1.30% | -1.86% | -2.06% | 437% | 116% | -1.47% | -2.23% | -2.41% | 719% | 119%
Class F (optional) | -1.01% | -1.35% | -1.22% | 456% | 119% | -1.33% | -1.93% | -1.74% | 777% | 123%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.22% | -1.28% | -0.97% | 167% | 111% | -0.50% | -1.81% | -1.50% | 246% | 116%
Class A2 | 0.05% | -1.44% | -0.87% | 179% | 107% | -0.08% | -1.88% | -1.10% | 263% | 110%
Class B | -0.12% | -1.40% | -1.96% | 198% | 110% | -0.35% | -2.06% | -2.62% | 291% | 114%
Class C | -0.32% | -1.00% | -1.18% | 228% | 109% | -0.39% | -1.23% | -1.41% | 339% | 111%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.16% | -1.28% | -1.33% | 195% | 109% | -0.34% | -1.75% | -1.77% | 287% | 113%
Class D | -0.20% | -0.71% | -1.05% | 259% | 108% | -0.30% | -0.92% | -1.10% | 395% | 109%
Class F (optional) | -0.37% | -0.61% | -0.61% | 287% | 115% | -0.69% | -1.29% | -1.01% | 429% | 116%
size128~16
size64~8

## Slide 7: SUCO in other S/W
Chart: Fast_SUCO
| 211 | 118 | 172 | 147 | 161 | 133 | 156
Depth65 | 1.7 | 0.6 | 1.2 | 0.9 | 1.1 | 0.8 | 1
Depth74_75 | 1.6 | 1.1 | 0 | 1.1 | 0 | 1
Depth75_74 | 1.6 | 1.1 | 1 | 1.1 | 1.1 | 1
2High4Low | 1.5 | 1.3 | 1.4 | 1.2 | 1.4 | 1.2 | 1.3 | 1.1
SUCO on IFVC (JVET-J0024)
  QBTT + SUCO (RA)

## Slide 8: SUCO in other S/W
SUCO on HM12.1
  Full: -2.1%@AI, -2.1%@RA, EncT: x7.4/x4.4@AI/RA
  Fast: -1.7%@AI, -1.7%@RA, EncT: x4.2/x1.9@AI/RA
SUCO on JEM3.1
 | RA |  |  | RA |  | 
 | Y | U | V | Y | U | V
2K | -2.3% | -3.6% | -3.9% | -1.7% | -2.8% | -3.1%
4K | -2.1% | -2.8% | -3.1% | -1.8% | -2.3% | -2.8%
8K | -2.0% | -4.1% | -3.8% | -1.6% | -3.2% | -3.0%
Overall | -2.1% | -3.4% | -3.5% | -1.7% | -2.7% | -2.9%
EncT | 445% |  |  | 195% |  | 
DecT | 104% |  |  | 102% |  | 
SUCO_full
SUCO_fast
SUCO_full
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 | -2.9% | -2.7% | -2.5% | 359% | 122%
Class B | -1.4% | -0.7% | -1.1% | 389% | 122%
Class C | -1.2% | -1.3% | -1.1% | 398% | 122%
Class D | -1.0% | -1.3% | -0.9% | 416% | 118%
Class E |  |  |  |  | 
Overall (Ref) |  |  |  |  | 
Class F | -2.2% | -3.9% | -4.5% | 409% | 113%

## Slide 9: Conclusion
SUCO in JVET-J0024 was tested on VTM/BMS
  Without SUCO fast algorithm, performance of Intra is consistent from results in
  other platforms.
  Inter prediction shows inconsistent result in the new platform.
Harmonization with VTM/BMS encoder optimization needs further investigation.
Suggest further study in CE on complexity and inter performance improvement