## Slide 1: JVET-K0146
CE10: Results on Geometric Block Partitioning (Test 3.3)
Max Bläser, Johannes Sauer, Mathias Wien
RWTH Aachen University
blaeser@ient.rwth-aachen.de

## Slide 2: Integration of Geometric Partitioning
Contribution relates to CfP submission JVET-J0023
  Geometric block partitioning (GEO) on top of JEM-7.0
    Partitioning of a block by straight line into two segments
    Additional syntax elements coded for partitioning line
    Inter- and intra-prediction of segments
    Overlapped-wedge combination of predicted segments
    Additional Shape-adaptive DCT (SA-DCT)
Integration of GEO into VTM-1.1 / BMS-1.1 for CE10-3.3
  GEO signaled as additional mode (such as Affine) on leaf of QTBT-TT
  In contrast to JVET-J0023 no SA-DCT available
  No Affine + GEO, OBMC off for GEO blocks
GEO + QTBT (JEM-7.0)

## Slide 3: CE10-3.3 Setup
Coding results have been obtained according to the Common test conditions given in JVET-J1010 and the methodology of JVET-J1005. Thus, GEO was tested in the following way:
  Tool on with VTM software against Tool off VTM reference
  Tool on with BMS software against Tool off BMS reference
Tested configurations
  Random-access and Lowdelay-B
  In accordance with JVET-J0023, GEO disabled on highest temporal id (RA), odd frames (LB)
Encoder complexity reductions
  Fast skipping of GEO in case of:
    Skip or Affine-Merge mode is best mode
    Low-textured block measured by weighted variance
  Minimum block size for GEO blocks 88 luma samples

## Slide 4: CE10-3.3 Results
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.46% | -2.02% | -1.76% | 187% | 155% | -1.40% | -1.66% | -1.58% | 133% | 136%
Class A2 | -1.63% | -2.56% | -2.17% | 253% | 158% | -1.69% | -2.82% | -2.16% | 140% | 133%
Class B | -0.39% | -0.91% | -0.85% | 241% | 113% | -0.32% | -0.66% | -0.83% | 137% | 101%
Class C | -0.18% | -0.38% | -0.44% | 320% | 141% | 0.00% | -0.21% | -0.22% | 157% | 104%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.80% | -1.32% | -1.19% | 250% | 137% | -0.73% | -1.17% | -1.08% | 142% | 114%
Class D | 0.14% | -0.04% | -0.09% | 429% | 126% | 0.09% | 0.07% | 0.02% | 174% | 106%
Class F (optional) |  |  |  |  |  |  |  |  |  | 
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.40% | -0.65% | -0.64% | 605% | 195% | -0.46% | -0.80% | -0.43% | 290% | 166%
Class C | -0.10% | -0.41% | -0.51% | 516% | 140% | -0.12% | -0.26% | -0.51% | 207% | 113%
Class E | -0.29% | 0.05% | -0.11% | 492% | 139% | -0.31% | -0.45% | -0.33% | 211% | 119%
Overall | -0.27% | -0.40% | -0.46% | 545% | 160% | -0.31% | -0.53% | -0.43% | 239% | 134%
Class D | -0.04% | -0.16% | -0.18% | 699% | 134% | -0.10% | 0.04% | -0.42% | 261% | 100%
Class F (optional) |  |  |  |  |  |  |  |  |  | 

## Slide 5: Example of GEO + QTBT-TT

## Slide 6: Summary & Conclusion
GEO + VTM-1.1 / GEO + BMS-1.1
  RA:
    Overall -0.80% ΔBD-rate for VTM, 250% encoder complexity, 137% decoder complexity
    Overall -0.73% ΔBD-rate for BMS, 142% encoder complexity, 114% decoder complexity
    Higher coding gains for classes A1/A2: -1.46% / -1.63% for VTM, -1.40% / -1.69% for BMS
  LB:
    Overall -0.27% ΔBD-rate for VTM, 545% encoder complexity, 160% decoder complexity
    Overall -0.31% ΔBD-rate for BMS, 239% encoder complexity, 134% decoder complexity
Suggestion
  Consideration of non-rectangular partitions for VVC
  Further study of GEO (performance for sub-HD)
  Specialized transform for non-rectangular partitions