## Slide 1: JVET-K0155 AHG12: Flexible Tile Partitioning
Yukinobu Yasugi Tomohiro Ikai
Sharp Corporation

## Slide 2: Background
Tile in HEVC
  Partitioning using CTU boundaries
    Coarse-grained tile
  Problems:
    Difficulty in load balancing
    Difficulty in fitting boundary to non-continuous regions
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
ctuRsAddr=
Unit of tile (CTU)

## Slide 3: Proposed tile
Tile partitioning using sub-CTU boundary
  The first CTU of each tile is always aligned to the top-left corner.
    Odd CTUs occur in the right and bottom edges of each tile.
    They are treated as same as those in picture boundary.
  Benefits:
    Better load balance
    Better fitting to frame-packed contents
0
1
2
3
4
5
6
ctuRsAddr=
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Unit of tile (sub-CTU)

## Slide 4: Experimental results
Implemented on BMS-1.0
SDR CTC
Anchor:
  BTM + VTM cfg.
  No tiles
Test:
  VTM cfg.
  2x2 tiles
  Uniform spacing
  Tile unit size:
    Test0: 128
    Test1: 4
    Test2: 8
    Test3: 16
    Test4: 32
All Intra Main 10 / Over VTM-1.0 |  |  |  |  | 
Y BD-rate | Test0 | Test1 | Test2 | Test3 | Test4
 | TileUnitSize=128 (Conventional) | 4 | 8 | 16 | 32
Class A1 | 0.38% | 0.73% | 0.73% | 0.41% | 0.40%
Class A2 | 0.24% | 0.43% | 0.43% | 0.21% | 0.25%
Class B | 0.43% | 1.24% | 0.48% | 0.46% | 0.46%
Class C | 0.86% | 0.93% | 0.93% | 0.93% | 0.84%
Class E | 1.34% | 1.86% | 1.86% | 1.41% | 1.41%
Overall | 0.64% | 1.06% | 0.84% | 0.68% | 0.66%
Enc/DecTime(%) | 101% / 104% | 100% / 107% | 101% / 104% | 101% / 104% | 102% / 107%
Class D | 1.46% | 1.96% | 1.96% | 1.54% | 1.46%
Class F (optional) | 0.87% | 1.03% | 1.03% | 0.94% | 0.96%
Random Access Main 10 / Over VTM-1.0 |  |  |  |  | 
Y BD-rate | Test0 | Test1 | Test2 | Test3 | Test4
 | TileUnitSize=128 (Conventional) | 4 | 8 | 16 | 32
Class A1 | 0.70% | 2.11% | 2.11% | 0.65% | 0.61%
Class A2 | 0.46% | 1.32% | 1.32% | 0.72% | 0.50%
Class B | 0.99% | 2.78% | 1.10% | 1.02% | 1.02%
Class C | 1.55% | 2.32% | 2.32% | 2.32% | 1.63%
Class E |  |  |  |  | 
Overall | 0.97% | 2.23% | 1.67% | 1.23% | 0.99%
Enc/DecTime(%) | 102% / 105% | 97% / 109% | 98% / 109% | 99% / 98% | 99% / 109%
Class D | 2.92% | 4.91% | 4.91% | 3.21% | 2.95%
Class F (optional) | 1.62% | 2.03% | 2.03% | 1.79% | 1.73%
Cross-check: JVET-K0408 by HHI

## Slide 5: Experimental results: All-Intra
Chart: All-Intra Main 10 / over VTM-1.0
| Class A1 | Class A2 | Class B | Class C | Class E | Overall
Test0: TileUnitSize=128 (Conventional) | 0.0038074 | 0.0024113 | 0.004307 | 0.0086181 | 0.01344 | 0.0063879
Test1: 4 | 0.0072938 | 0.0043219 | 0.012429 | 0.0093461 | 0.018589 | 0.010563
Test2: 8 | 0.0072938 | 0.0043219 | 0.0047761 | 0.0093461 | 0.018589 | 0.0084376
Test3: 16 | 0.004135 | 0.0021276 | 0.0046489 | 0.0093468 | 0.014124 | 0.0067661
Test4: 32 | 0.0039781 | 0.0024732 | 0.0046489 | 0.0084143 | 0.014124 | 0.0065904

## Slide 6: Experimental results: Random Access
Chart: RandomAccess / VTM-1.0
| Class A1 | Class A2 | Class B | Class C | Overall
Test0: TileUnitSize=128 (Conventional) | 0.0069776 | 0.0046067 | 0.0099086 | 0.015474 | 0.0097462
Test1: 4 | 0.021075 | 0.013177 | 0.027811 | 0.023201 | 0.022308
Test2: 8 | 0.021075 | 0.013177 | 0.011 | 0.023201 | 0.016704
Test3: 16 | 0.0065101 | 0.0072028 | 0.010167 | 0.023201 | 0.012319
Test4: 32 | 0.0060502 | 0.0049989 | 0.010167 | 0.016304 | 0.0099467

## Slide 7: Conclusion
Tile partitioning using sub-CTU boundary was proposed.
The proposed tile system has almost as same BD-rate performance as the conventional tile when the unit size of tile partitioning = 32.
Smaller tile unit showed relatively greater loss. However, it might be prevented by employing boundary partitioning tools.
We suggest studying the proposed tile in AhG12.