## Slide 1: JVET-K0175 CE3-related: Advanced most probable modes (MPM) based on intra reference line selection scheme
Hui-Yu Jiang, Yao-Jen Chang
Ljubljana, SI
July 2018

## Slide 2: Current most probable modes (MPM)
  VTM-1.0 : 3 MPMs
  Intra modes from left and above neighboring blocks
  Derived angular modes : -1/+1 angular mode
  Default modes : Planar, DC and 26
  BMS-1.0 : 6 MPMs
  Intra modes from left, above, left-bottom, above-right, above-left neighboring blocks
  Derived angular modes : -1/+1 angular mode
  Default modes : Planar, DC, 50, 18, 2 and 34

## Slide 3: Current MPM syntax
MPM flag indicates whether to enable MPM for each CU
MPM index flag further indicates which MPM is selected
parse MPM flag
If (MPM flag )
{
parse MPM index flag
}

## Slide 4: Motivation of this contribution
Conventional MPMs always use the nearest reference line () for prediction
It is known further reference lines () can improve the BD-rate

## Slide 5: Proposed advanced MPM (AMPM)
AMPM is proposed to signal the selected reference line for each angular MPM on CU level
The predictor P(x,y) of angular MPM could be generated from one of the reference lines

## Slide 6: The details for the proposed AMPM
RL index flag indicates the selected reference line
  Non-angular MPMs (Planar and DC) always select
  0, 10, 110, and 111 for and
Additional SATD is performed to evaluate the best angular MPMs with further reference lines
  No RD check increase
parse MPM flag
If (MPM flag )
{
parse MPM index flag
If(MPM Planar and MPM DC )
{
parse RL index flag
}
}
parse MPM flag
If (MPM flag )
{
parse MPM index flag
{
parse RL index flag
}
}

## Slide 7: All-Intra results in VTM-1.0
On top of the VTM1.0 anchor under CTC
On top of AI configuration, AMPM provides good performance in terms of bitrate reduction and coding runtime
Test 1 : AMPM with 3-MPMs method
Test 2 : 6-MPMs method
(6 MPMs of BMS applied to VTM-1.0)
Thank Tencent for crosscheck!

## Slide 8: Random-Access results in VTM-1.0
On top of the VTM1.0 anchor under CTC
Test 1 : AMPM with 3-MPMs method
On top of RA configuration, AMPM provides good performance in terms of bitrate reduction and coding runtime
Test 2 : 6-MPMs method
(6 MPMs of BMS applied to VTM-1.0)
Thank Tencent for crosscheck!

## Slide 9: Additional AI results in VTM-1.0 (1)
The proposed method provides competitive performance as compared with 6-MPMs method + Intra65Ang enabled (-1.2% with 115/102% runtime)
Simulation is on top of the VTM1.0 anchor under CTC
Test 3: AMPM with 3-MPMs method + Intra65Ang enabled
Anchor : VTM-1.0

## Slide 10: Additional AI results in VTM-1.0 (2)
Simulation is on top of the VTM1.0 anchor under CTC
Test 4: AMPM with 6-MPMs method + Intra65Ang enabled
Anchor : VTM-1.0
Anchor : VTM-1.0 + 6-MPMs method + Intra65Ang enabled
Thank Tencent for crosscheck!
The gain of AMPM is increased on top of 6-MPMs method + Intra65Ang enabled

## Slide 11: Conclusion
This contribution proposes an advanced MPM (AMPM) based on an intra reference line selection scheme
Provides good improvement in terms of bitrate reduction and coding runtime
  Compared to VTM anchor, the AMPM reaches 0.5% luma coding gain with 102%/99% coding runtime
The gain of AMPM is much more on top of 6-MPMs method + Intra65Ang
It is suggested to consider the proposed AMPM for the next version of VTM

## Slide 12: Thank you.