## Slide 1: JVET-K0203: Non-CE2: higher-precision modifications to VVC deblocking filters
JVET 11th Meeting - Ljubljana, SI, 10–18 July 2018

## Slide 2: Problem identified with VTM/BMS
HEVC was primarily studied around 8 bits content, as even the Main10 mostly relied on such content left-shifted to 10 bits.
Furthermore, VTM/BMS, and JEM, are producing content that have much lower distortion at the same input quantizer step.
We consider that VTM/and BMS suffer from the HEVC deblocking filter under the current settings, and can be simply tuned to prevent some of its negative downsides.
Note: equation numbers are relative to H.265 v5 from Feb. 2018

## Slide 3: Β and tC derivation from tabulated values
Depending of the bitdepth, the variable β is derived as follows:
  β = β′ * ( 1 << ( BitDepth Y − 8 ) ) (8-351)
Depending of the bitdepth, the variable tC is derived as follows:
  tC = tC ′ * ( 1 << ( BitDepth Y − 8 ) ) (8-353)
tc’ can be modeled (for instance) as exp(D*QP+E)
  D = 0.11 and E = -2.64 used, as tc’ is already very quantized on 5 bits

## Slide 4: 1) Proposed change related to tC
Change accounts for tc being used in feature detection (strong/weak filter decision) and correcting errors after quantization
tC = ( tC’ * scale[ BitDepth ] ) >> N
  At higher bitdepths, a good setting for 8 bits is suboptimal
  scale[ BitDepth ] = C . 2(A*bitdepth+B), with C dependent on N (6 here)
  A=1, B=-8 and C=16 in HEVC, while BMS/VTM but lower in reality and often ~0.9
Below, for JEM, multiple coding configurations and metrics
  A ~ 0.85 in JEM, while A closer to 0.9 in BMS
Scale * 16

## Slide 5: 2) Proposed change related to clipping
Clipping range modification
  At any given QP, configuration or sequence, the PSNR compared to HM16 is respectively up to 0.4/1.0/2.0dB higher for VTM1.0 / BMS1.0 / JEM7.0:
  It means that error after quantization is much lower
  Simplistic change: divide by 2 the parameter used for clipping ranges
    Relative value between e.g. weak and strong luma filters is kept
For the strong filter (use for other samples as well)
  p0 ′ = Clip3(p0 − 2*tC , p0 + 2*tC , ( p2 + 2*p1 + 2*p0 + 2*q0 + q1 + 4 ) >> 3 ) (8-391)
  p0 ′ = Clip3(p0 − tC , p0 + tC , ( p2 + 2*p1 + 2*p0 + 2*q0 + q1 + 4 ) >> 3 )
For the weak filter
  D= Clip3( −tC , tC , D ) (8-398)
  D= Clip3( −tC/2 , tC/2 , D ) (8-398)
The complete settings depend on error after quantization
  tc/2 more meaningful for JEM than VTM

## Slide 6: 3) Normative changes for Chroma
Chroma filter in HEVC
  Basically always ON for an edge with an intra neighbour, and OFF otherwise
  2 samples filtered
Observations
  Chroma filter is actually not very good as is for RA/LDP scenarios
  Visually a lot less meaningful anyway

## Slide 7: 3.1) Normative changes for Chroma
Design rationale: keep it simple
  No large additional flow control
  Limited memory I/O
Change 1: base Chroma OFF on Luma OFF decision
  Luma: d < , where d is given by equation (8-371), and can be interpreted as a flatness measure
  In particular, Chroma is always OFF when Luma is OFF, contrary to HEVC

## Slide 8: 3.2) Normative changes for Chroma
Change 2: “Longer” filter on Chroma
HEVC chroma filtering (equations 8-405 to 8-407)
  Δ = Clip3( −tC, tC, ( ( ( ( q0 − p0 ) << 2 ) + p1 − q1 + 4 ) >> 3 ) )
  p0′ = Clip1C( p0 + Δ )
  q0′ = Clip1C( q0 − Δ )
Proposal change
  Δ1 = Δ >> 1
  p1′ = Clip1C( p1 + Δ1 )
  q1′ = Clip1C( q1 – Δ1 )
  No additional input or line buffer

## Slide 9: Results
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.1_VTM |  |  |  |  | Over BMS-1.1_BMS |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0,37% | -0,97% | -0,28% | 100% | 103% | -0,83% | -2,01% | -1,10% | 103% | 102%
Class A2 | -0,37% | 0,84% | 0,74% | 100% | 99% | -0,99% | -0,86% | -1,03% | 104% | 101%
Class B | -0,34% | -0,68% | -0,11% | 100% | 101% | -0,91% | -1,84% | -1,43% | 104% | 99%
Class C | -0,26% | -0,27% | 0,08% | 100% | 102% | -0,66% | -1,93% | -1,86% | 102% | 99%
Class E | -0,13% | 0,11% | 0,98% | 100% | 101% | -0,70% | -1,20% | -0,49% | 102% | 99%
Overall | -0,29% | -0,25% | 0,23% | 100% | 101% | -0,82% | -1,62% | -1,25% | 103% | 100%
Class D | -0,21% | 0,03% | 0,25% | 99% | 103% | -0,62% | -1,37% | -1,31% | 100% | 100%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.1_VTM |  |  |  |  | Over BMS-1.1_BMS |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,04% | -3,17% | -3,32% | 101% | 104% | -0,03% | -3,03% | -3,45% | 100% | 101%
Class A2 | -0,11% | -0,29% | -0,08% | 101% | 103% | -0,37% | -1,27% | -1,40% | 101% | 102%
Class B | -0,12% | -2,74% | -2,17% | 99% | 103% | -0,41% | -2,90% | -2,44% | 104% | 101%
Class C | -0,13% | -2,18% | -2,00% | 99% | 104% | -0,26% | -2,23% | -2,26% | 100% | 101%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0,09% | -2,19% | -1,94% | 100% | 103% | -0,28% | -2,42% | -2,39% | 101% | 101%
Class D | -0,11% | -1,97% | -1,94% | 100% | 103% | -0,33% | -1,81% | -1,64% | 100% | 103%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over BMS-1.1_VTM |  |  |  |  | Over BMS-1.1_BMS |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0,27% | -2,00% | -1,87% | 99% | 105% | -0,59% | -2,83% | -2,52% | 106% | 102%
Class C | -0,23% | -0,86% | -0,60% | 99% | 100% | -0,44% | -1,68% | -1,69% | 102% | 98%
Class E | -0,49% | -0,28% | -0,59% | 98% | 104% | -1,02% | -1,24% | -1,65% | 102% | 98%
Overall | -0,32% | -1,19% | -1,13% | 99% | 103% | -0,65% | -2,05% | -2,03% | 103% | 99%
Class D | -0,30% | -0,97% | -0,88% | 100% | 102% | -0,55% | -1,89% | -0,97% | 100% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 10: Conclusion
~0.1-0.3% gain on Y for VTM1.1, 0.3-0.8% for BMS1.1
Potentially larger on a more efficient version
  The more efficient the codec, the more destructive the in-loop filter will become, potentially affecting the whole coding loop and other post-filters
Suggest to
  Further study the different aspects of this proposal in a CE on deblocking filter.
  Finding more rational settings and fixing bugs in the in-loop filter may allow better evaluation of any proposal

## Slide 11: Comparative results with CE proposals
Using BDRate YUV measure (14:1:1)
Test# | VTM | BMS
2.2.1.1.a | -0.13% | -0.10%
2.2.1.1.b | -0.12% | -0.14%
2.2.1.2 | 0.15% | 0.15%
2.2.1.3 | 0.00% | -0.02%
2.2.1.4 | -0.06% | -0.07%
2.2.1.5 | 0.04% | 0.04%
2.2.1.6.a | -0.03% | 0.00%
2.2.1.6.b | -0.20% | -0.24%
2.2.1.6.c | -0.21% | -0.23%
K0203 | -0.34% | -0.75%

## Slide 12: Thank you for your attention.