## Slide 1: JVET-K0208 – CE4.3.6 - Technicolor Unicity in motion information candidate lists
July 2018

## Slide 2: Unicity in motion information candidate lists
In all Inter modes
  Construction of lists of predictor candidates
  In VTM/BMS, some can be identical
Ensure unicity of candidates
  Check if already present or not in the list before adding in all Inter modes
  In AMVP (classical and affine), rounding and clipping performed before unicity check
  More efficient with AMVR
  Already extended to manage LIC and FRUC

## Slide 3: Unicity in motion information candidate lists
Results
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.05% | 0.04% | 101% | 100% | 0.00% | -0.19% | -0.06% | 101% | 103%
Class A2 | -0.06% | -0.02% | -0.01% | 101% | 104% | -0.04% | -0.05% | 0.01% | 100% | 104%
Class B | -0.14% | -0.16% | 0.01% | 101% | 100% | -0.11% | -0.14% | -0.08% | 101% | 102%
Class C | -0.05% | -0.04% | -0.14% | 101% | 103% | -0.03% | -0.08% | -0.10% | 101% | 103%
Overall | -0.07% | -0.08% | -0.03% | 101% | 102% | -0.05% | -0.12% | -0.06% | 101% | 103%
Class D | -0.04% | -0.02% | -0.06% | 101% | 105% | -0.04% | 0.01% | -0.02% | 101% | 104%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.09% | -0.08% | 0.10% | 100% | 102% | -0.14% | -0.23% | 0.15% | 100% | 104%
Class C | -0.03% | -0.08% | 0.14% | 101% | 92% | -0.11% | 0.03% | -0.30% | 101% | 105%
Class E | 0.15% | -0.11% | -0.21% | 101% | 93% | -0.35% | -0.44% | 0.16% | 101% | 103%
Overall | -0.01% | -0.09% | 0.04% | 101% | 96% | -0.19% | -0.20% | 0.00% | 100% | 104%
Class D | -0.07% | -0.30% | -0.05% | 100% | 102% | -0.11% | 0.34% | -0.54% | 101% | 104%

## Slide 4: Conclusion
Unicity check
  Seems like a code cleaning
  Brings BD-rate gains on all classes and configurations
    RA: -0.07% VTM and -0.05% BMS
    LDB: -0.01% VTM and -0.19% BMS
  With reduced complexity increases
    RA: 1% encoder and 2 to 3% decoder
    LDB: 1% encoder and -4 to 4% decoder