## Slide 1: JVET-K0213 – CE10.2.3 - Technicolor Generalized OBMC
July 2018

## Slide 2: Generalized OBMC
JEM-like OBMC
  A-priori decision to filter 2/4 lines/columns depending on the CU coding mode
  Same filtering strength for both horizontal and vertical directions
      → Filtering errors on bad decisions
Entire
Sub-blocks
Bad decisions

## Slide 3: Generalized OBMC
Proposed generalized OBMC
  Performed on 4x4 sub-blocks basis
  4x4 sub-block borders considered by pairs (left, right) then (top, bottom)
  On-the-fly decision of filtering strength depending on opposite MVs
      → Independent decisions for horizontal/vertical directions
      → Adaptation to motion transitions within the CU (Merge ATMVP)
      → Adaptation to thin CUs of width or height smaller than 8
1)
2)
4
2
2
1)
2)
4
4

## Slide 4: Generalized OBMC
Results
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.41% | -1.65% | -1.91% | 109% | 117% | -0.48% | -1.16% | -1.38% | 104% | 120%
Class A2 | -1.04% | -1.98% | -1.88% | 113% | 129% | -1.22% | -2.19% | -2.73% | 107% | 138%
Class B | -0.96% | -1.89% | -1.83% | 114% | 123% | -1.22% | -2.29% | -2.20% | 107% | 132%
Class C | -1.50% | -2.54% | -2.70% | 117% | 130% | -1.83% | -2.96% | -3.05% | 107% | 134%
Overall | -1.01% | -2.03% | -2.09% | 114% | 125% | -1.24% | -2.22% | -2.37% | 107% | 131%
Class D | -1.43% | -2.05% | -2.04% | 122% | 137% | -1.87% | -2.95% | -2.92% | 108% | 137%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -1.24% | -1.83% | -1.93% | 117% | 128% | -1.51% | -2.73% | -2.49% | 108% | 135%
Class C | -1.67% | -2.18% | -2.32% | 119% | 119% | -2.18% | -3.20% | -3.34% | 108% | 138%
Class E | -1.31% | -1.77% | -1.95% | 115% | 111% | -2.33% | -3.11% | -2.48% | 109% | 134%
Overall | -1.40% | -1.93% | -2.07% | 117% | 120% | -1.94% | -2.98% | -2.77% | 109% | 136%
Class D | -1.92% | -2.18% | -1.67% | 120% | 136% | -2.54% | -2.55% | -2.77% | 111% | 148%

## Slide 5: Conclusion
Generalized OBMC
  Independent horizontal/vertical decisions
  Adaptation to motion transitions in the CU and to thin CUs
  Brings BD-rate gains on all classes and configurations
    VTM: -1.01% RA and -1.40% LDB
    BMS: -1.24% RA and -1.94% LDB
  With complexity increases
    VTM: 14-17% encoder and 25-20% decoder
    BMS: 7-9% encoder and 31-36% decoder