## Slide 1: JVET-K0214 – CE9.3.4 - Technicolor Template matching from J0022
July 2018

## Slide 2: Template matching from J0022
Remove FRUC unilateral candidates (Test #1)
  Constructed for each slice by using all reference frames
      → Save complexity at encoder and especially decoder
AMVP limitation (Test #2)
  Consider only FRUC refined candidate
      → No more MVP index transmitted, reduce RDO complexity
  Limit to 2 candidates the AMVP FRUC list
      → Limit FRUC complexity in the AMVP case
Combined test (Test #3)
  Combined Test #1 and #2

## Slide 3: Template matching from J0022
Results of test #1 (unilateral cand. removal)
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -6.50% | -5.97% | -6.60% | 157% | 259% | -3.19% | -3.10% | -3.55% | 126% | 156%
Class A2 | -8.61% | -8.14% | -8.43% | 164% | 321% | -3.94% | -3.74% | -3.94% | 131% | 165%
Class B | -5.76% | -5.23% | -5.13% | 170% | 279% | -3.23% | -2.98% | -2.91% | 133% | 167%
Class C | -5.27% | -5.32% | -5.64% | 181% | 329% | -3.56% | -3.58% | -3.78% | 136% | 200%
Overall | -6.35% | -5.98% | -6.22% | 169% | 295% | -3.45% | -3.32% | -3.48% | 132% | 173%
Class D | -5.79% | -5.27% | -5.53% | 192% | 358% | -3.86% | -3.71% | -3.80% | 138% | 214%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -2.56% | -2.74% | -2.54% | 221% | 229% | -1.97% | -2.31% | -1.78% | 164% | 168%
Class C | -2.60% | -3.16% | -3.58% | 229% | 240% | -2.34% | -2.94% | -3.33% | 173% | 207%
Class E | -3.87% | -3.83% | -4.35% | 202% | 208% | -2.90% | -2.29% | -2.42% | 158% | 192%
Overall | -2.90% | -3.15% | -3.34% | 219% | 227% | -2.33% | -2.51% | -2.46% | 165% | 186%
Class D | -2.75% | -3.22% | -3.65% | 228% | 274% | -2.28% | -1.98% | -2.69% | 179% | 227%

## Slide 4: Template matching from J0022
Results of test #2 (AMVP limitation)
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -6.69% | -6.16% | -6.81% | 168% | 292% | -3.33% | -3.21% | -3.73% | 130% | 172%
Class A2 | -8.90% | -8.41% | -8.74% | 179% | 357% | -4.21% | -4.01% | -4.23% | 139% | 182%
Class B | -5.95% | -5.48% | -5.41% | 176% | 306% | -3.41% | -3.22% | -3.13% | 135% | 183%
Class C | -5.57% | -5.63% | -5.89% | 183% | 351% | -3.81% | -3.85% | -3.98% | 137% | 213%
Overall | -6.59% | -6.24% | -6.48% | 177% | 324% | -3.66% | -3.55% | -3.70% | 135% | 188%
Class D | -6.14% | -5.65% | -5.83% | 194% | 377% | -4.12% | -4.03% | -4.21% | 139% | 222%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -3.04% | -3.12% | -3.07% | 230% | 285% | -2.41% | -3.02% | -2.55% | 169% | 210%
Class C | -3.14% | -3.74% | -3.98% | 230% | 276% | -2.72% | -3.44% | -3.95% | 173% | 241%
Class E | -4.26% | -4.15% | -4.47% | 212% | 291% | -3.28% | -2.36% | -2.64% | 163% | 295%
Overall | -3.38% | -3.58% | -3.72% | 225% | 283% | -2.73% | -3.00% | -3.04% | 169% | 240%
Class D | -3.44% | -3.98% | -4.50% | 229% | 308% | -2.75% | -2.98% | -3.21% | 179% | 250%

## Slide 5: Template matching from J0022
Results of test #3 = #1 + #2
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -6.65% | -6.05% | -6.78% | 160% | 259% | -3.31% | -3.16% | -3.71% | 127% | 155%
Class A2 | -8.89% | -8.38% | -8.72% | 166% | 320% | -4.18% | -3.96% | -4.20% | 132% | 166%
Class B | -5.95% | -5.51% | -5.34% | 172% | 279% | -3.40% | -3.21% | -3.15% | 134% | 168%
Class C | -5.53% | -5.62% | -5.86% | 182% | 329% | -3.81% | -3.84% | -3.93% | 136% | 201%
Overall | -6.57% | -6.22% | -6.44% | 171% | 295% | -3.65% | -3.52% | -3.68% | 133% | 173%
Class D | -6.12% | -5.55% | -5.83% | 192% | 357% | -4.13% | -3.86% | -4.11% | 139% | 216%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -3.02% | -3.12% | -3.27% | 222% | 229% | -2.37% | -2.94% | -2.63% | 165% | 168%
Class C | -3.08% | -3.53% | -4.16% | 228% | 239% | -2.74% | -3.21% | -3.62% | 173% | 207%
Class E | -4.42% | -4.60% | -4.76% | 203% | 209% | -3.44% | -2.89% | -2.69% | 158% | 193%
Overall | -3.39% | -3.62% | -3.94% | 219% | 227% | -2.76% | -3.02% | -2.98% | 166% | 186%
Class D | -3.41% | -3.56% | -4.37% | 229% | 274% | -2.85% | -2.81% | -4.08% | 179% | 227%

## Slide 6: Conclusion
Template matching from J0022
  Test #1 RA: VTM: -6.35% 169% 295% - BMS: -3.45% 132% 173%
  Test #2 RA: VTM: -6.59% 177% 324% - BMS: -3.66% 135% 188%
  Test #3 RA: VTM: -6.57% 171% 295% - BMS: -3.65% 133% 173%
  Test #3 keeps
    BD-rate gains of Test #2,
    And encoding/decoding runtimes of Test #1
Can easily be coupled with other FRUC contributions