## Slide 1: CE2: Alf with Multiplication Replaced by Bit-Shifting (Test 4.1.3)
Semih Esenlik,
Zhijie Zhao, Jianle Chen

## Slide 2: Problems with ALF in BMS
  Predefined fixed filter predictors
    400 fixed filters with 21 filter coefficients each
    considerable amount of ROM space and additional filter estimation processes
    ~8-10 pages of text in the draft specification.
  9x9 filter size is supported in BMS1.0.
    Required Number of multiplications = 21 per pixel

## Slide 3: Proposed Changes
  Remove the predefined fixed filters completely
    0.19% (AI), 0.18% (RA) and -0.08% (LDB) coding gain impact.
  Apply logarithmic (in base 2) quantization to outlying filter coefficients
    14 of the 21 filter coefficients can be implemented as simple bit shift operation.
    Allowed filter coefficient values {–64, –32, –16, –8, –4, 0, 4, 8, 16, 32, 64}
    Allowed coefficient values are mapped to {–5, –4, –3, –2, –1, 0, 1, 2, 3, 4, 5} before binarization.

## Slide 4: Experimental Results
Simulations results w.r.t. to anchors VTM and BMS

## Slide 5: Supplementary Results
Effect of disabling predefined fixed filters only. Anchors: VTM+ALF and BMS

## Slide 6: Supplementary Results
Effect of replacing multiplication with bit-shifting only. Anchors: “VTM+ALF-Fixed filters” and “BMS-fixed filters”

## Slide 7: Conclusion
2 important issues in the ALF design in BMS1.0 are addressed
  Removal of the fixed filter predictors which do not provide a good tradeoff.
  Reducing computational complexity via replacing multiplication with bit-shifting
Proposed to be included in BMS ALF.

## Slide 8
Thank You
www.huawei.com