## Slide 1: JVET-K0218 – CE4.1.4 - Technicolor Affine mode enhancement
July 2018

## Slide 2: Affine mode enhancement
Shared modifications
  Fix divisions by zero in affine motion estimation
  Aggregate affine motion calculations into three functions
  Perform all affine motion calculations with integer precision
Performed on top of CE4.1.3
  As J0022 on top of J0021
  Affine model 4/6 params, affine MVD prediction, CU model switch, slice model switch
 | Random Access Main 10 |  |  |  | 
 | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class C | 0.05% | -0.01% | 0.16% | 100% | 99%
Class D | -0.06% | -0.12% | -0.18% | 100% | 100%
Overall | 0.00% | -0.06% | -0.01% | 100% | 99%

## Slide 3: Affine mode enhancement
Affine model storage (Test #1)
  Affine model stored at CU level
      → Correct motion in TL, TR, BL 4x4 sub-blocks for following prediction
      → Fix issue with CU of width or height equal to 4
Affine AMVP candidate derivation (Test #2)
  Spatial affine model candidates enriched with {a2, b3} positions
  Constructed affine model possible with only 2 neighboring motions
      → More possibility to get an affine model
Combined test (Test #3)
  Combined Test #1 and #2

## Slide 4: Affine mode enhancement
Results of test #1 (affine model storage)
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.61% | -2.20% | -2.30% | 135% | 111% | -1.61% | -1.20% | -1.28% | 110% | 106%
Class A2 | -8.22% | -6.67% | -6.33% | 161% | 127% | -5.60% | -4.25% | -4.11% | 118% | 108%
Class B | -4.02% | -2.79% | -2.95% | 152% | 114% | -2.82% | -2.04% | -2.03% | 114% | 106%
Class C | -1.46% | -0.92% | -1.02% | 144% | 109% | -1.26% | -0.88% | -0.97% | 112% | 107%
Overall | -3.90% | -2.95% | -2.98% | 148% | 115% | -2.72% | -2.01% | -2.02% | 113% | 107%
Class D | -1.85% | -1.11% | -1.22% | 139% | 113% | -1.69% | -1.49% | -1.13% | 109% | 108%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -2.90% | -2.11% | -1.86% | 210% | 116% | -3.03% | -2.15% | -2.19% | 138% | 109%
Class C | -1.52% | -0.58% | -0.48% | 178% | 100% | -1.52% | -0.97% | -1.43% | 129% | 110%
Class E | -2.64% | -2.17% | -2.63% | 276% | 103% | -2.47% | -2.70% | -2.72% | 170% | 108%
Overall | -2.38% | -1.61% | -1.59% | 213% | 107% | -2.39% | -1.89% | -2.07% | 142% | 109%
Class D | -2.93% | -1.96% | -2.15% | 157% | 113% | -2.99% | -2.61% | -3.05% | 124% | 113%

## Slide 5: Affine mode enhancement
Results of test #2 (affine AMVP cand. derivation)
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.59% | -2.14% | -2.31% | 134% | 110% | -1.58% | -1.24% | -1.33% | 110% | 105%
Class A2 | -8.22% | -6.69% | -6.33% | 160% | 128% | -5.59% | -4.18% | -4.10% | 118% | 109%
Class B | -4.02% | -2.74% | -2.89% | 151% | 114% | -2.81% | -2.02% | -2.01% | 114% | 105%
Class C | -1.45% | -0.95% | -0.98% | 144% | 110% | -1.25% | -0.98% | -1.08% | 112% | 106%
Overall | -3.89% | -2.93% | -2.95% | 148% | 115% | -2.71% | -2.02% | -2.05% | 113% | 106%
Class D | -1.84% | -1.01% | -1.24% | 140% | 112% | -1.71% | -1.47% | -1.27% | 110% | 107%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -2.92% | -2.03% | -2.05% | 210% | 116% | -3.01% | -2.09% | -2.50% | 139% | 109%
Class C | -1.51% | -0.65% | -0.59% | 180% | 100% | -1.55% | -1.21% | -0.96% | 129% | 110%
Class E | -2.62% | -2.00% | -2.41% | 275% | 103% | -2.48% | -2.83% | -2.66% | 171% | 111%
Overall | -2.37% | -1.56% | -1.65% | 213% | 107% | -2.39% | -1.98% | -2.03% | 143% | 110%
Class D | -2.92% | -1.69% | -2.23% | 157% | 112% | -2.99% | -2.65% | -2.88% | 125% | 110%

## Slide 6: Affine mode enhancement
Results of test #3 = #1 + #2
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.59% | -2.18% | -2.28% | 136% | 110% | -1.59% | -1.26% | -1.31% | 110% | 105%
Class A2 | -8.24% | -6.74% | -6.40% | 160% | 128% | -5.61% | -4.25% | -4.10% | 118% | 108%
Class B | -4.04% | -2.82% | -2.94% | 151% | 114% | -2.83% | -1.94% | -2.06% | 113% | 105%
Class C | -1.49% | -0.87% | -1.06% | 144% | 110% | -1.27% | -0.98% | -0.92% | 112% | 105%
Overall | -3.91% | -2.96% | -3.00% | 148% | 115% | -2.72% | -2.01% | -2.01% | 113% | 106%
Class D | -1.86% | -1.24% | -1.22% | 139% | 114% | -1.74% | -1.38% | -1.19% | 109% | 105%
Affine 1080p | -4.40% | -1.86% | -1.71% | 125% | 114% | -4.39% | -2.10% | -1.94% | 114% | 109%
Affine 720p | -15.19% | -11.28% | -11.18% | 206% | 130% | -12.96% | -9.81% | -10.41% | 129% | 110%
Overall | -8.72% | -5.63% | -5.50% | 153% | 120% | -7.82% | -5.18% | -5.33% | 120% | 109%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -2.91% | -2.03% | -2.16% | 211% | 117% | -3.03% | -2.17% | -2.03% | 139% | 109%
Class C | -1.51% | -0.64% | -0.50% | 178% | 101% | -1.54% | -1.11% | -1.22% | 129% | 108%
Class E | -2.69% | -2.10% | -2.76% | 277% | 103% | -2.57% | -2.64% | -2.37% | 170% | 107%
Overall | -2.39% | -1.59% | -1.75% | 213% | 108% | -2.42% | -1.93% | -1.85% | 142% | 108%
Class D | -2.96% | -1.83% | -2.30% | 157% | 114% | -3.11% | -2.60% | -3.01% | 124% | 109%

## Slide 7: Conclusion
Affine mode enhancement
  Brings BD-rate gains on all classes and configurations
    VTM: -3.91% RA and -2.39% LDB
    BMS: -2.72% RA and -2.42% LDB
  With complexity increases
    VTM: 48% enc. and 15% dec. RA and 113% enc. and 8% dec. LDB
    BMS: 13% enc. and 6% dec. RA and 42% enc. and 8% dec. LDB
  Up to VTM RA: -8.72% 53% 20% - BMS RA: -7.82% 20% 9% on Affine class
Can easily be coupled with other Affine contributions