## Slide 1: JVET-K0219 – CE4.2.4 - Technicolor Merge mode enhancement
July 2018

## Slide 2: Merge mode enhancement
Performed on top of CE4.2.3
  As J0022 on top of J0021
    1. Adding non-adjacent spatial merge candidate candidates, on/off test
    2. Enlarging merge list to 17 with affine
    3. Merge candidate list reordering
    4.Unified merge candidate list

## Slide 3: Merge mode enhancement
Affine model storage (Test #1)
  Affine model stored at CU level
      → Correct motion in TL, TR, BL 4x4 sub-blocks for following prediction
      → Fix issue with CU of width or height equal to 4
Add Affine merge candidates (Test #2)
  Spatial affine model candidates enriched with {b2, a2, b3} positions
  Temporal affine candidates at {curr, c}
Combined test (Test #3)
  Combined Test #1 and #2

## Slide 4: Merge mode enhancement
Results of test #1 (affine model storage)
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -3.08% | -2.73% | -2.90% | 139% | 114% | -1.81% | -1.39% | -1.43% | 117% | 98%
Class A2 | -6.73% | -5.93% | -5.64% | 145% | 127% | -4.44% | -3.60% | -3.58% | 121% | 100%
Class B | -4.67% | -3.36% | -3.40% | 148% | 115% | -3.45% | -2.61% | -2.62% | 121% | 100%
Class C | -1.93% | -1.61% | -1.57% | 150% | 113% | -1.70% | -1.33% | -1.50% | 118% | 98%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -4.03% | -3.28% | -3.26% | 146% | 117% | -2.85% | -2.22% | -2.28% | 119% | 99%
Class D | -2.16% | -1.57% | -1.78% | 153% | 115% | -1.92% | -1.74% | -1.52% | 118% | 100%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -3.19% | -2.04% | -1.75% | 174% | 105% | -3.22% | -2.21% | -2.12% | 130% | 104%
Class C | -1.59% | -0.60% | -0.61% | 167% | 97% | -1.66% | -1.19% | -1.16% | 125% | 103%
Class E | -2.55% | -1.91% | -2.55% | 213% | 97% | -2.28% | -2.04% | -2.22% | 157% | 105%
Overall | -2.50% | -1.53% | -1.57% | 181% | 100% | -2.47% | -1.83% | -1.83% | 134% | 104%
Class D | -2.86% | -2.21% | -2.18% | 159% | 108% | -2.97% | -2.72% | -2.80% | 124% | 103%

## Slide 5: Merge mode enhancement
Results of test #2 (new merge affine candidates)
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -3.00% | -2.64% | -2.86% | 140% | 117% | -1.76% | -1.22% | -1.40% | 116% | 100%
Class A2 | -6.68% | -5.89% | -5.63% | 148% | 130% | -4.36% | -3.56% | -3.57% | 120% | 102%
Class B | -4.65% | -3.35% | -3.44% | 149% | 118% | -3.39% | -2.55% | -2.60% | 120% | 102%
Class C | -2.05% | -1.56% | -1.60% | 151% | 114% | -1.67% | -1.29% | -1.41% | 113% | 101%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -4.03% | -3.24% | -3.27% | 148% | 119% | -2.80% | -2.15% | -2.24% | 117% | 101%
Class D | -2.36% | -1.78% | -1.98% | 156% | 118% | -1.98% | -1.78% | -1.46% | 112% | 100%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -3.25% | -2.16% | -1.85% | 177% | 114% | -3.27% | -2.17% | -2.63% | 133% | 105%
Class C | -1.71% | -0.80% | -0.70% | 168% | 100% | -1.74% | -1.52% | -1.38% | 126% | 105%
Class E | -2.70% | -2.23% | -2.55% | 213% | 97% | -2.32% | -2.55% | -2.18% | 157% | 107%
Overall | -2.60% | -1.72% | -1.64% | 182% | 105% | -2.52% | -2.05% | -2.10% | 136% | 105%
Class D | -3.20% | -1.96% | -2.60% | 159% | 111% | -3.24% | -2.75% | -3.34% | 123% | 103%

## Slide 6: Merge mode enhancement
Results of test #3 = #1 + #2
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -3.07% | -2.80% | -2.95% | 143% | 126% | -1.78% | -1.36% | -1.44% | 117% | 105%
Class A2 | -6.74% | -5.99% | -5.69% | 149% | 140% | -4.43% | -3.58% | -3.63% | 120% | 108%
Class B | -4.69% | -3.41% | -3.49% | 152% | 128% | -3.46% | -2.61% | -2.66% | 121% | 108%
Class C | -2.07% | -1.71% | -1.71% | 154% | 126% | -1.75% | -1.35% | -1.46% | 119% | 107%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -4.08% | -3.35% | -3.35% | 150% | 129% | -2.86% | -2.22% | -2.29% | 119% | 107%
Class D | -2.47% | -1.65% | -1.89% | 159% | 127% | -2.06% | -1.77% | -1.76% | 119% | 107%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 without affine |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -3.28% | -2.19% | -2.04% | 182% | 125% | -3.29% | -2.50% | -2.31% | 132% | 111%
Class C | -1.77% | -0.83% | -0.78% | 170% | 106% | -1.80% | -1.53% | -1.55% | 127% | 111%
Class E | -2.87% | -2.69% | -2.83% | 220% | 118% | -2.40% | -2.25% | -1.85% | 159% | 118%
Overall | -2.67% | -1.86% | -1.82% | 187% | 117% | -2.57% | -2.11% | -1.94% | 136% | 113%
Class D | -3.29% | -2.15% | -2.64% | 162% | 117% | -3.31% | -2.85% | -3.57% | 125% | 110%
Affine 1080p | -9.58% | -3.42% | -2.46% | 132% | 117% | -9.46% | -4.02% | -3.53% | 102% | 106%
Affine 720p | -15.00% | -10.58% | -12.08% | 199% | 162% | -12.92% | -9.12% | -10.13% | 125% | 114%
Overall | -11.75% | -6.29% | -6.31% | 156% | 133% | -10.85% | -6.06% | -6.17% | 111% | 109%

## Slide 7: Conclusion
Merge Affine mode enhancement
  Brings BD-rate gains on all classes and configurations
    VTM: -4.08% RA and -2.67% LDB
    BMS: -2.86% RA and -2.57% LDB
  With complexity increases
    VTM: 50% enc. and 29% dec. RA, 87% enc. and 17% dec. LDB
    BMS: 19% enc. and 7% dec. RA and 36% enc. and 13% dec. LDB
  On affine classes:
    VTM RA: -11.75%
    BMS RA: -10.85%
Can easily be coupled with other Affine contributions