## Slide 1: JVET-K0268 – CE4 related - Technicolor Affine tools from J0022
July 2018

## Slide 2: Affine tools from J0022
All affine tools in J0022
  From 4.1.3 and 4.2.3 (J0021):
    Affine model 4/6 params,
    affine MVD prediction,
    CU model switch
    Enlarging merge list to 17 with affine
    Unified merge candidate list
  From 4.1.3 and 4.1.4 (J0022):
    Affine model stored at CU level
    Spatial affine model candidates enriched with {a2, b3} positions
    Constructed affine model possible with only 2 neighboring motions
    New affine merge candidates spatial {b2, a2, b3} and temporal {curr,c}
  Added:
    Fix divisions by zero in affine motion estimation

## Slide 3: Affine tools from J0022 - Results
  BMS-1.0 software with SIMD=SSE42
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM reference |  |  |  |  | Over BMS without affine tool |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.43% | -2.07% | -2.29% | 162% | 124% |  |  |  |  | 
Class A2 | -7.79% | -6.48% | -6.07% | 172% | 139% |  |  |  |  | 
Class B | -3.97% | -2.75% | -2.94% | 176% | 127% | -2.83% | -2.06% | -2.02% | 143% | 110%
Class C | -1.51% | -0.83% | -0.97% | 173% | 123% | -1.21% | -0.92% | -0.92% | 139% | 110%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -3.77% | -2.85% | -2.91% | 171% | 128% |  |  |  |  | 
Class D | -1.97% | -1.17% | -1.24% | 176% | 125% | -1.74% | -1.25% | -1.12% | 139% | 111%
Affine 1080p | -10.04% | -3.87% | -2.99% | 157% | 125% | -10.25% | -4.33% | -3.93% | 118% | 111%
Affine 720p | -15.47% | -11.61% | -12.73% | 279% | 165% | -13.46% | -10.07% | -10.84% | 152% | 118%
Overall | -12.21% | -6.97% | -6.89% | 198% | 140% | -11.53% | -6.63% | -6.70% | 131% | 114%

## Slide 4: Conclusion
All affine tools in J0022
  Brings BD-rate gains on all classes and configurations
    VTM: -3.77% RA
  With complexity increases
    VTM: 71% enc. and 28% dec. RA
  On affine classes:
    VTM RA: -12.21%