## Slide 1: CE5-related: Implementation considerations for entropy coding engine
Frank Bossen

## Slide 2: Proposed changes
Changes are with respect to techniques studied in CE5
  Modify the constant 2b to 2b−1 (e.g., 32768 to 32767) in the probability estimate update function
  Modify the subinterval range computation for the LPS symbol to ((r >> 5) * (qLPS >> (b − 5)) >> 1) + 4

## Slide 3: Probability update
Typical update rule (from CE5)
  if (symbol) q = q + ((32768 − q) >> n) else q = q − (q >> n)
  Uses branch, which is undesirable because of possible branch misprediction
  Branchless implementation makes early use of “symbol”, which can make decoding slower:
    t = q − ((32768 − (1 << n) + 1) & symbol) q = q − (t >> n)

## Slide 4: Modified probability update
Change 32768 to 32767
  Previous implementations still realizable (if you like those)
Enables branchless implementation with late use of “symbol”, which can make decoding faster:
  q = q − (q >> n) q = q + ((32767 >> n) & symbol)

## Slide 5: Subinterval range computation
Subinterval range computation (CE5)
  rLPS = clip(((2r3 + 1) × (2q5 + 1) + 4) >> 3, 4, 32 × (r3 − 4))
  Often implemented with a table lookup (size 32x8) with indices q5 and r3
Proposed change to
  rLPS = (r3 × q5 >> 1) + 4
  4x5-bit multiplier
  Simpler formulation that preserves following properties
    rLPS can never be 0
    When renormalizing after MPS, shift by at most 1 bit

## Slide 6: Compression efficiency
Reference implementation: CE5-1.2.0, CABACEngine=4, CIPF=0, VTM config
Probability update modification
  Essentially 0% average difference
Combined modifications
  About 0.04% average loss

## Slide 7: Complexity
>20% cycle count
reduction
>10% cycle count
reduction

## Slide 8: Summary
Changes are with respect to techniques studied in CE5
  Modify the constant 2b to 2b−1 (e.g., 32768 to 32767) in the probability estimate update function
  Modify the subinterval range computation for the LPS symbol to ((r >> 5) * (qLPS >> (b − 5)) >> 1) + 4
No significant impact on compression efficiency (<0.05% average)
Can help speed up CABAC decoding in SW by 10-20%