## Slide 1: JVET-K0274 Reduced complexity bilateral filter
J. Ström, P. Wennersten, J. Enhorn, D. Liu, K. Andersson and R. Sjöberg
Ericsson Research
Jacob Ström
2018-07-09

## Slide 2: Refresher
transform coefficients
decoded residual
prediction
clip to [0, 1023]
recon- struction
bilateral filter
new recon- struction

## Slide 3: Background
The bilateral filter was included into JEM at the Hobart meeting
Feedback: predicting from filtered coefficients may put filter in critical path for hardware implementation for small intra blocks
previous block
current block
prediction

## Slide 4: Background
prediction
The bilateral filter was included into JEM at the Hobart meeting
Feedback: predicting from filtered coefficients may put filter in critical path for hardware implementation for small intra blocks
Thus filtering may need to be done in parallel for the closest pixels
previous block
current block
filtered in parallel

## Slide 5: Background
prediction
The bilateral filter was included into JEM at the Hobart meeting
Feedback: predicting from filtered coefficients may put filter in critical path for hardware implementation for small intra blocks
Thus filtering may need to be done in parallel for the closest pixels
This in turn means many instantiations of the look-up table (LUT).
previous block
current block
filtered in parallel

## Slide 6: Example JVET-F0096
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*576 | 9384
1
2
3
4

## Slide 7: Example
1
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*576 | 9384
1 edge pixel | 3 * 2202 | 1*576 | 7182
1
2
3
4
3
2

## Slide 8: Example
1
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*576 | 9384
1 edge pixel | 3 * 2202 | 1*576 | 7182
1 corner pixel | 2 * 2202 | 1*576 | 4980
1
2
3
4
3
2
2
1

## Slide 9: Examples
1
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*576 | 9384
1 edge pixel | 3 * 2202 | 1*576 | 7182
1 corner pixel | 2 * 2202 | 1*576 | 4980
4 edge pixels | 7 * 2202 | 4*576 | 17718
1
2
3
4
3
2
2
1
1
2
3
4
5
6
7

## Slide 10: This proposal
Reduces size of LUT from 2202 to 816 bytes
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*576 | 9384
1 edge pixel | 3 * 2202 | 1*576 | 7182
1 corner pixel | 2 * 2202 | 1*576 | 4980
4 edge pixels | 7 * 2202 | 4*576 | 17718

## Slide 11: This proposal
Reduces size of LUT from 2202 to 816 bytes
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 816 | 1*576 | 3840
1 edge pixel | 3 * 816 | 1*576 | 3024
1 corner pixel | 2 * 816 | 1*576 | 2208
4 edge pixels | 7 * 816 | 4*576 | 6288

## Slide 12: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 816 | 1*576 | 3840
1 edge pixel | 3 * 816 | 1*576 | 3024
1 corner pixel | 2 * 816 | 1*576 | 2208
4 edge pixels | 7 * 816 | 4*576 | 6288

## Slide 13: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Number of pixels filtered in parallel | weight-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 816 | 3264
1 edge pixel | 3 * 816 | 2448
1 corner pixel | 2 * 816 | 1632
4 edge pixels | 7 * 816 | 5712

## Slide 14: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Also uses Qualcomm’s non-localized inter filtering.
Number of pixels filtered in parallel | weight-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 816 | 3264
1 edge pixel | 3 * 816 | 2448
1 corner pixel | 2 * 816 | 1632
4 edge pixels | 7 * 816 | 5712

## Slide 15: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Also uses Qualcomm’s non-localized inter filtering.
Number of pixels filtered in parallel | weight-LUT storage needed | Previous size for LUTs | Proposed size for LUTs | Change
1 middle pixel | 4 * 816 | 9384 | 3264 | -63%
1 edge pixel | 3 * 816 | 7182 | 2448 | -65%
1 corner pixel | 2 * 816 | 4980 | 1632 | -67%
4 edge pixels | 7 * 816 | 17718 | 5712 | -68%

## Slide 16: LUT reduction
LUT is two-dimensional, with one row for each qp.
0 1 2 3 4 5 6 7 8 9 ...
Intensity difference
qp
255, 237, 191, 133, 80, 42, 19, 7, 2, 1, 0
255, 248, 227, 196, 159, 122, 89, 60, 39, 24, 14, 7, 4, 2, 1, 0
255, 252, 242, 227, 208, 185, 161, 136, 112, 90, 71, 54, 40, 29, 21, 14, 10, ...
255, 255, 255, 254, 253, 252, 251, 249, 248, 246, 244, 241, 239, 236, 233, 230, 227, ...
255, 255, 255, 255, 255, 254, 254, 254, 253, 253, 252, 251, 251, 250, 249, 248, 248, ...
18
19
20
33
51

## Slide 17: LUT reduction
LUT is two-dimensional, with one row for each qp.
0 1 2 3 4 5 6 7 8 9 ...
Intensity difference
qp
255, 237, 191, 133, 80, 42, 19, 7, 2, 1, 0
255, 248, 227, 196, 159, 122, 89, 60, 39, 24, 14, 7, 4, 2, 1, 0
255, 252, 242, 227, 208, 185, 161, 136, 112, 90, 71, 54, 40, 29, 21, 14, 10, ...
255, 255, 255, 254, 253, 252, 251, 249, 248, 246, 244, 241, 239, 236, 233, 230, 227, ...
255, 255, 255, 255, 255, 254, 254, 254, 253, 253, 252, 251, 251, 250, 249, 248, 248, ...
18
19
20
33
51

## Slide 18: LUT reduction
Rows are just stretched versions of each other
Example
  LUTqp34(x) = LUTqp51(2*x)
  Take every second value of black curve to get blue curve
We use powers of two:
  LUTused(x) = LUTbase(x << k)
Leaves a large gap between the black and blue curve
We therefore use four base tables
  e.g., LUTused(x) = LUTbase3(x << k)

## Slide 19: LUT reduction
LUT is two-dimensional, with one row for each qp.
0 1 2 3 4 5 6 7 8 9 ...
Intensity difference
qp
255, 237, 191, 133, 80, 42, 19, 7, 2, 1, 0
255, 248, 227, 196, 159, 122, 89, 60, 39, 24, 14, 7, 4, 2, 1, 0
255, 252, 242, 227, 208, 185, 161, 136, 112, 90, 71, 54, 40, 29, 21, 14, 10, ...
255, 255, 255, 254, 253, 252, 251, 249, 248, 246, 244, 241, 239, 236, 233, 230, 227, ...
255, 255, 255, 255, 255, 254, 254, 254, 253, 253, 252, 251, 251, 250, 249, 248, 248, ...
18
19
20
33
51

## Slide 20: Resulting storage needs
LUT is made up of four LUT base-rows of 235, 206, 178 and 150 eight-bit values. (769 bytes)
4 bytes to tell the size of each base-row (4 bytes)
2 bits to tell which base row is used and 3 bits for the shift value (2+3)*34/8 = 22 bytes
21 distanceFactor parameters of 8-bits each = 21 bytes
Total LUT size = 769+4+22+21 = 816 bytes
Previous LUT size 2783 bytes – a reduction by 71%

## Slide 21: Results
VTM BD rates
  -0.33% / -0.81% / -0.59% for AI / RA / LD
VTM decode complexity
  104% / 103% / 103% for AI / RA / LD
BMS BD rates
  -0.33% / -0.52% / -0.60% for AI / RA / LD
BMS decode complexity
  101% / 101% / 101% for AI / RA / LD
Old filter gain over JEM:
  -0.41% / -0.48% / -0.48% for AI / RA / LD

## Slide 22: Gain vs run time (adding to VTM)
better

## Slide 23: Gain vs run time (“removed” from BMS)
better

## Slide 24: Proposal
We propose to adopt JVET-K0274 to VTM.

## Slide 25: Detailed results VTM AI
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.25% | 0.09% | 0.05% | 97% | 106%
Class A2 | -0.31% | -0.06% | 0.10% | 109% | 105%
Class B | -0.32% | 0.09% | 0.01% | 104% | 103%
Class C | -0.39% | -0.06% | -0.21% | 100% | 104%
Class E | -0.39% | -0.45% | -0.32% | 101% | 104%
Overall | -0.33% | -0.06% | -0.07% | 102% | 104%
Class D | -0.40% | -0.07% | 0.00% | 105% | 102%

## Slide 26: Detailed results VTM RA
 | Random Access over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.55% | -0.16% | -0.20% | 109% | 104%
Class A2 | -0.88% | -0.40% | -0.33% | 108% | 104%
Class B | -1.01% | -0.05% | -0.13% | 109% | 102%
Class C | -0.68% | -0.14% | -0.39% | 106% | 102%
Class E |  |  |  |  | 
Overall | -0.81% | -0.17% | -0.25% | 108% | 103%
Class D | -0.63% | -0.26% | -0.23% | 105% | 101%

## Slide 27: Detailed results VTM LD
 | Low Delay over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.25% | 0.09% | 0.05% | 97% | 106%
Class A2 | -0.31% | -0.06% | 0.10% | 109% | 105%
Class B | -0.32% | 0.09% | 0.01% | 104% | 103%
Class C | -0.39% | -0.06% | -0.21% | 100% | 104%
Class E | -0.39% | -0.45% | -0.32% | 101% | 104%
Overall | -0.33% | -0.06% | -0.07% | 102% | 104%
Class D | -0.40% | -0.07% | 0.00% | 105% | 102%

## Slide 28: Detailed results BMS AI
 | All Intra over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | -0.13% | -0.18% | 103% | 101%
Class A2 | -0.35% | -0.19% | 0.07% | 110% | 101%
Class B | -0.25% | -0.07% | -0.22% | 99% | 101%
Class C | -0.53% | -0.25% | -0.30% | 103% | 102%
Class E | -0.38% | -0.38% | -0.44% | 102% | 101%
Overall | -0.33% | -0.19% | -0.22% | 103% | 101%
Class D | -0.37% | 0.05% | -0.09% | 97% | 102%

## Slide 29: Detailed results BMS RA
 | Random Access over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.24% | -0.10% | -0.12% | 106% | 101%
Class A2 | -0.58% | -0.42% | -0.04% | 106% | 102%
Class B | -0.60% | -0.05% | -0.29% | 106% | 101%
Class C | -0.60% | 0.00% | -0.51% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.52% | -0.12% | -0.26% | 105% | 101%
Class D | -0.52% | -0.08% | -0.59% | 99% | 100%

## Slide 30: Detailed results BMS LD
 | Low delay over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.47% | 0.38% | 0.98% | 104% | 101%
Class C | -0.69% | 0.50% | 0.48% | 110% | 102%
Class E | -0.70% | -0.28% | -0.19% | 105% | 99%
Overall | -0.60% | 0.26% | 0.52% | 106% | 101%
Class D | -0.73% | 0.39% | -0.08% | 98% | 101%